## Slide 1: NSLS II Physics Application and its Open Architecture
Guobao Shen
Controls Group, Photon Sciences
Brookhaven National Laboratory
Oct 23rd, 2014

## Slide 2: Motivation
Traditional high level application suites
  Closed environment
  Self consistent
  Come with its own simulation code
  Work good once successfully configured
    Expertise needed
Open structure environment
  Break into separate modules
  Portability
  Reusability

## Slide 3: System Architecture
3-tier open architecture at NSLS II
Distributed Front-Ends
Ethernet
Python Apps
CA Client
MMLT
CA Client
XAL
CA Client
SDDS
CA Client
CS-Studio
CA Client
IOC
HW
IOC
HW
IOC
HW
IOC
HW
IOC
HW
…
MySQL
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
IDODS
Python
MySQL
PVAS
HTTP/REST
MUNICONV
Python
SQLite/MongoDB
EPICS V4
MASAR
Python
MySQL
PVAS
HTTP/REST
AI DS
Python
IOC
Live Optics
IOC
Live MUNICONV
Tracy-III/Elegant
IOC
Orbit Correction
IOC
Dispersion Meas
…
IOC
JMS virtual accelerator
Tracy-III/Elegant

## Slide 4: Middle Layer Services
Distributed Front-Ends
IOC
Live Optics
IOC
Live MUNICONV
Ethernet
Python Apps
CAC PVAC REST
MMLT
CAC PVAC REST
Matlab Apps
CAC PVAC REST
Channel Arch
CAC PVAC REST
CS-Studio
CAC PVAC REST
Tracy-III/Elegant
IOC
Orbit Correction
IOC
Dispersion Meas
…
IOC
JMS virtual accelerator
Tracy-III/Elegant
MySQL
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
IDODS
Python
MySQL
PVAS
HTTP/REST
MUNICONV
Python
SQLite/MongoDB
EPICS V4
MASAR
Python
MySQL
PVAS
HTTP/REST
AI DS
Python

## Slide 5: Middle Layer Services
MASAR
  A save/restore tool
    Machine Snapshot, Archiving, and Retrieve
  EPICS V4 Service to snapshot machines
    General purpose tool
    Globally handle PVs distributed in different IOCs
  Machine
    A collection of EPICS PVs
  Snapshot
    Data at specific time point
      Value, time stamp, connection status, alarm status, alarm severity
Similar, but different purpose tools
  Autosave
    Single IOC bumpless rebooting
  Channel Archiver
    Archive periodically
    Save time serially data

## Slide 6: Middle Layer Services
MASAR Server (EPICS V4 Engine)
PyQt
Channel Access
Gather/C++
MASAR Client Python Library pvAccess Client
pvAccess
DSL-PY Module (C++ <->Python)
PYMASAR (Python)
SQLite
Scripting
IOC
IOC
IOC
CS-Studio/BOY
pvAccess Client Library (Java)
Finished
User Apps
Developing
Others
(Matlab)
MASAR Architecture
Restore
MongoDB
Plan
MySQL

## Slide 7: Middle Layer Services
MASAR terminologies
configuration
...
event
event data
pv
pv group
Snapshot

## Slide 8: Middle Layer Services
MASAR Client PyQt4 UI
Become official lattice ID in our commissioning reports, olog, …
Notes: User select data set to be compared
Select reference data set from a pop up dialog
By default, first selected data as reference set

## Slide 9: Middle Layer Services
Deployed in control network from the first day (3/27/2012)
MASAR snapshots taken with time (up to 10/15/2014)

## Slide 10: Middle Layer Services
RESTful based middle layer services
  For static data
  Data warehouse
  Middle layer IOC for live data
    In V3 currently, and planned to be in V4
Services at NSLS II
  MUNICONV: multiple unit conversion
  Lattice/Model
  Beam based interlock data service
  Insertion device data service

## Slide 11: Middle Layer Services
Python Client
Architecture for RESTful based Service
Finished
User Apps
Planning
Developing
MySQL
Python Data API
Python-MySQLdb
V4 channelRPC service
IOC
(Live Data)
RESTful
Scripting
CSS/BOY
Java Client
Others
(Matlab)
Browsers
RESTful
pvAccess
pvAccess
pvAccess
Django Service
HTML
RESTful

## Slide 12: Middle Layer Services
MUNICONV Service
  Multiple unit conversion
    First implementation targeting on magnets
    Convert value between different unit systems
      i: power supply current
      b: magnetic fields
      k: value in model/lattice domain
  Implemented with Django
  MySQL as RDB backend
  Client support
    Python library
    Web UI

## Slide 13: Middle Layer Services
MUNICONV WEB View

## Slide 14: Middle Layer Services
MUNICONV IOC
  pyDevSup: Python Device Support
  Initialize IOC thru RESTful web service
  Trigger processing when HW record processed
    ~ 1K HWs
    ~ 4K soft records
      SP, RB
      B, K values
    1 HW PVs => 1 or more soft PVs
      Power chain
  Separate from H/W IOC
  PV Mapping & relation thru C.F.
I PV_
I PV_
I PV_
B PV
K PV
I PV
Hardware IOC
MUNICONV IOC
1:1
1:N
1:N

## Slide 15: MUNICONV

## Slide 16: Middle Layer Services
Lattice/Model Service
  A further development based on our virtual accelerator
  Consists of 2 parts
    WEB service
    Live IOC for online requirement
  Support 2 simulation codes (Tracy-3 & Elegant)
    Transparent switching between each other
Beam Parameter
Beam Parameter
Simulation/ Measurement
Beam Parameter
Lattice Deck
Beam Parameter
Lattice (Geometric + Strength)
Input
Model (Simulation result)
Output

## Slide 17: Middle Layer Services
Lattice view

## Slide 18: Middle Layer Services
Model view

## Slide 19: Middle Layer Services
K PV
K PV
K PV
Lattice/Model IOC
  On demand mode
  CF to get all PVs
  MUNICONV to get physics unit
  Lattice/Model to produce result
    WEB service to capture all history data
  CS-Studio panel to present results
Lattice Deck Generator
MUNICONV IOC
Lattice/Model IOC
Quad
Sext
H/V Cor
Simulator
I PV_
I PV_
PVs
Data Processing
Lattice/Model RESTful
Django Service

## Slide 20: Middle Layer Services
Lattice/Model IOC CSS Panel

## Slide 21: High Level Physics Applications
IOC
JMS virtual accelerator
Tracy-III/Elegant
MySQL
PVAS
HTTP/REST
Lattice/Model
Python
MySQL
PVAS
HTTP/REST
IDODS
Python
MySQL
PVAS
HTTP/REST
MUNICONV
Python
SQLite/MongoDB
EPICS V4
MASAR
Python
MySQL
PVAS
HTTP/REST
AI DS
Python
Distributed Front-Ends
IOC
Live Optics
IOC
Live MUNICONV
Ethernet
Python Apps
CAC PVAC REST
MMLT
CAC PVAC REST
Matlab Apps
CAC PVAC REST
Channel Arch
CAC PVAC REST
CS-Studio
CAC PVAC REST
Tracy-III/Elegant
IOC
Orbit Correction
IOC
Dispersion Meas
…

## Slide 22: High Level Physics Applications
EPICS V3
IOC
CS-Studio
Python
Accelerator Physics High Level App
(APHLA Library)
Finished
User Apps
Developing
Architecture
Planning
EPICS Database
User Apps
EPICS V4
CS-Studio/BOY
EPICS V4 Java Client

## Slide 23: High Level Physics Applications
IOC as middle layer services
  Orbit correction, dispersion measurement, chromaticity measurement/correction, local bump
  beta function measurement + beta beat, tune correction, …
Orbit Correction
  Use orbit response matrix
U, s, V = np.linalg.svd(m, full_matrices=True)
rcond = s[kwarg["nsv"] - 1] / s[0]
# solve for m*dk + (v0 - ref) = 0
dk, resids, rank, s = np.linalg.lstsq(m, -1.0 * v0, rcond=rcond)
k0 = np.array(ca.caget(kker), 'd')
if dImax is not None and np.max(np.abs(dk)) != 0.0:
dk = dk / np.max(np.abs(dk)) * np.abs(dImax)
...

## Slide 24: High Level Physics Applications
Local bump for insertion device
Global orbit Difference display
Adjust offset in X plane
Adjust angle in Y plane

## Slide 25: System Integration
IDODS
MASAR
Lattice/Model
MUNICONV
Client App
(PyQt, CS-Studio)
MUNICONV
IOC
Olog
Lattice/Model
IOC
... IOC
Orbit Correction IOC
Channel Finder
Channel Archiver
Notes: User create a MASAR configuration with PV from for example channel finder
Client apps could request MASAR to save a snapshot, or restore a particular snapshot
After restoring, MUNICONV IOC will got update simultaneously
MUNICONV IOC initialized with MUNICONV data service, and provides data in for example K value, which is available to client app
Operator/physicist could check restoring result by comparing machine optics, which available by lattice/model IOC
Result would be saved into lattice/model data service automatically, and displayed on CS-Studio panel for example
MASAR action will be logged into Olog
Lattice/model result is available thru web browser either

## Slide 26: Conclusion
Major milestones
  2013-11-27: beam commissioning started
  2013-11-29: achieve 200 MeV
  2013-12-07: injection into booster
  2013-12-31: 3 GeV in booster
  2014-03-26: storage ring commissioning started
  2014-03-30: 1st turn around SR complete
  2014-04-05: 25 mA!
  2014-05-09: Near 100% injection efficiency
  2014-07-11: 50 mA
  2014-07-13: Phase I Commissioning complete
  2014-09-22: Official approval for routine operations
  2014-10-23: Expecting 1st light to beamline (10:30 EST) ?