## Slide 1: Kalman Filter in MarlinTPC
G. De Lentdecker
Université Libre de Bruxelles

## Slide 2: MarlinTPC installation
MarlinTPC is based on the Marlin framework:
  Based on LCIO data format
  Usage of successive « processors »
  One .xml file with the running parameters of each processor to steer Marlin
  Marlin provides interfaces to GEAR (geometry description) and LCCD (conditions data)
  Uses RAIDA (AIDA + ROOT) for histogramming
  + need additional packages: MySQL, CLHEP, Java, QT, etc.
You need to install a lot of things.
Fortunately the developers provide an installation python script: ilcinstall
Despite this script it took me a while to find the right recipe to compile and link everything together:
  32 vs 64bits,
  SL4 vs SL5
  special ROOT versions used by CMS (my other experiment).
Also helpful : https://znwiki3.ifh.de/MarlinTPC/HowToInstallMarlinTPC
Eventually I found the correct combination to work on CERN lxplus

## Slide 3: Installation of Kalman Filter
KalTest and KalDet are not installed by ilcinstall
Fortunatelly it is well documented in
  https://znwiki3.ifh.de/MarlinTPC/HowToInstallMarlinTPC
  MarlinTPC/reconstruction/README
  KalTest/README
And so it is rather straightforward to install (once you have installed all the rest, of course)

## Slide 4: Modifications to be done
Note : the code has been developed by our Japanese colleagues and therefore it has been mostly tested with GEM modules => so a few numbers are hardcoded; examples :
  The number of rows in the class HelicalTrack.cc
  The algorithm to find pulses looks behind pad #72 in TopoFinder.cc

## Slide 5: Before you run, you need:
gear_ilc_lp_micromegas_single_module.xml
  Describes the geometry of a single micromegas module in LP
TPCChannelMapping.slcio
  Provides the mapping in pad row and column
Files provided by Jason Abernathy
  Old geometry (not for TB with new electronics)

## Slide 6: Sequence:
<execute>
<!-- "manager processors" -->
<processor name="MyAIDAProcessor"/>
<processor name="MyConditionsProcessor"/>
<!-- "reconstruction processors" -->
<processor name="MyAFTERRawDataConverterProcessor"/>
<processor name="MyPedestalSubtractor"/>
<processor name="MyPulseFinder"/>
<processor name="MyChannelMapperProcessor"/>
<!-- "For KalmanFilter" -->
<processor name="MyHitTrackFinderTopoProcessor"/>
<processor name="MyTrackMakingKalmanFilterProcessor"/>
<!-- "validation processors" -->
<processor name="MyChargeOnPadsVisualisationProcessor"/>
<processor name="MyDumpResidualsProcessor"/>
<!-- "output processors" -->
<processor name="MyLCIOOutputProcessor"/>
</execute>
// Find the pulses in detector
// Do the mapping to (col,row)
//make TrackHit from pulses
//perform KF & produce
LCIO Tracks
// processors for x-checks &
histograms

## Slide 7: Comparison event by event
Compared some pulses between LPMon and MarlinTPC
  Pulse height and time looked in agreement although not exactly identical by a few ADC counts
One « event display »:
LPDisplay
MarlinTPC
RUN01007
1st event (Resistive Ink)
X (mm)
Y (mm)
Y
X

## Slide 8: Comparison
Time
Time
RUN01007 1st event (Resistive Ink)
X
Y
X
Y
Y
Hits included in track reconstructed
by Kalman Filter
X
LPDisplay
MarlinTPC

## Slide 9: Kalman Filter
Kalman filter seems to work:
  Tracks are reconstructed
  However pt values obtained are not correct (bad B field setting ?)
(GeV/c)

## Slide 10: Conclusions
The most difficult (for me) was to install Marlin & ILCSOFT
Once this done, installation of KalTest and KalDet is easy
Except few hardcoded values, Kalman Filters runs:
  Tracks are reconstructed
  BUT values returned by the fit doesn’t look right… investigating