## Slide 1: Beam tests of Fast Neutron Imaging in China
L. An2, D. Attié1, Y. Chen2, P. Colas1, M. Riallot1, H. Shen2,
W. Wang1,2, X. Wang2, C. Zhang2, X. Zhang2, Y. Zhang2
(1)
(2)
Workshop MPGD at Saclay, 2011

## Slide 2: The Helium-3 Shortage: Supply, Demand, and Options for Congress
The demand was small enough that a substantial stockpile of helium-3 accumulated. After the terrorist attacks of September 11, 2001, the federal government began deploying neutron detectors at the U.S. border to help secure the nation against smuggled nuclear and radiological material. The deployment of this equipment created new demand for helium-3. Use of the polarized helium-3 medical imaging technique also increased. As a result, the size of the stockpile shrank. After several years of demand exceeding supply, a call for large quantities of helium-3 spurred federal officials to realize that insufficient helium-3 was available to meet the likely future demand.
Until 2001, helium-3 production by the weapons program exceeded demand, and the program accumulated a stockpile. To recoup some of the cost of purifying recycled tritium, the program transferred helium-3 from the stockpile to the DOE Office of Isotope Production and Research for sale at auction. Despite these sales, the helium-3 stockpile grew from roughly 140,000 liters in 1990 to roughly 235,000 liters in 2001. Since 2001, however, helium-3 demand has exceeded production. By 2010, the increased demand had reduced the stockpile to roughly 50,000 liters.
Actions to reduce demand:
• Fund or encourage the development of alternative technologies.
• Require or provide incentives for the use of alternative technologies.

## Slide 3
Introduction: idea of Fast Neutron Imaging detector
Simulation of Micromegas as a neutron detector
Description of the detector
Data analysis and results
Conclusion and Next step
Overview

## Slide 4: Characteristics and simulation of FNI detector
Characteristics expected of Fast Neutron Imaging detector based on TPC:
High spatial resolution: <100 µm
high quality imaging from Micro-Pattern Gas Detector
as Micro-Mesh Gaseous Structure (Micromegas)
  Low efficiency: ~ 0.01-1%,
  subject to thickness and kind of converter
  suitable for beam monitor/profile
  imaging in very high flux
Simulation tools:
  Garfield (gas processes):
    ionization energy
    electron drift velocity
    electron avalanche
  Geant4 (physics processes)

## Slide 5: Monte-Carlo simulation
Garfield
Average ionization energy
Energy loss
Drifting velocity
Diffusion coefficient
Multiplication coefficient
Incident 14MeV
neutron flux
Charged particle (proton)
in converter
Initial electron
Geant4
Induced signal
Transportation of
electron in gas
Transportation function
Ionization of charged
particle in drift gap

## Slide 6: Monte-Carlo simulation
Data reconstruction method:
  identify cluster (track)
  extract hit position where the time is maximum tmax  interaction point
  integrate all events  image
Neutron event interacting
with polyethylene foil
and knocking out a proton
n
p
e- avalanche
Garfield
Avalanches
Drift lines from primary ionization e-
Proton track
X-Y readout plan
Drift time
 = 91.9 µm
p
Avalanche drift time
y-z readout plane

## Slide 7: Geant4 simulation for converter efficiency
CH2
gas
n
n, p
1 cm
6 cm
10 cm
25 µm ~ 20 cm
Neutronproton recoiling efficiency in a polyethylene [C2H4]n layer coming from 241Am-9Be source
Incident neutron spectrum
According to ISO 8529(*)
* INTERNATIONAL STANDARD ISO 8529. Reference neutron radiations – Part 1: Characteristic and methods of productions. International Standard ISO 8529-1 (2001).
W.Wang_Beam tests of Fast Neutron Imaging in China
7
07.12.2011

## Slide 8: Geant4 simulation for converter efficiency
Neutronproton recoiling efficiency in a polyethylene [C2H4]n layer coming from 14MeV neutron
W.Wang_Beam tests of Fast Neutron Imaging in China
8
* D. Vartsky et al, Nucl. Intsr. and Meth. A 376 (1996) 29.
07.12.2011
*

## Slide 9: Micromegas TPC for neutron imaging
gas
128 µm
HVmesh
Eamp ~ 30 kV/cm
10 mm
HVdrift
Edrift ~ 200 V/cm
Wax
Pb
Detector layout: 1728 (36 ×48) pads of 1.75 mm × 1.50 mm
Gas mixture: Argon + 5% Isobutane
+ bulk Micromegas
Elastic scattering on hydrogen n  p
+ masks (Pb, paraffin wax)
PCB
Micromegas
n
p
Aluminized polyethylene 25 µm
between 2 layers (0.5 µm) of Al
57.4 mm
88.6 mm
Cosmics
(x, y, t)

## Slide 10: Detector + electronics setup

## Slide 11
Gain curve measured from 5.9 keV line using 55Fe source. Signals read out on the mesh in Ar/Isobutane 5%: G~103 @ 300 V
Energy resolution of ~12 % due to detector capacitance and noise
best energy resolution measured for a bulk Micromegas (~7 %)
Performances of the Micromegas detector

## Slide 12
Data sample from source
36
48
Located in Lanzhou University, data taking in July 2011
Intensity: ~6 ×106 Hz (4π)
Neutron energy spectrum, according to ISO 8529 (reference radiations for calibrating neutron-measuring devices)
Mean energy ~4.5 MeV, up to 11 MeV
241Am–9Be source

## Slide 13
Data analysis and results
Electronic Gain = 360 fc
Vmesh = 300V
Electronic Gain = 120 fc
Vmesh = 300V
Electronic Gain = 600 fc
Vmesh = 320V
Electronic Gain = 360 fc
Vmesh = 300V
Electronic Gain = 120 fc
Vmesh = 350V
Operating gas gain < 1500 and electronics full-scale gain set  360 fC in order to cut the gamma-rays and cosmics events

## Slide 14
64mm plastic(polyethylene) in front of the detector
Vmesh = 300V Electronic Gain = 360
Cluster size is maximum at ~5
Uniform time spectrum
Data analysis and results

## Slide 15
Thickness: 17 mm
3 mm
Pb
Paraffin
+
Imaging
Counting
mode
Tracking +cuts in time & charge
Imaging with Lanzhou mask

## Slide 16
Counting
mode
Thickness: 17 mm
3 mm
Pb
Paraffin
Imaging
Tracking +cuts in time & charge
+
Imaging with CEA mask

## Slide 17
1.5 mm
3 mm
3.5 mm
5 mm
2.5 mm
Thickness: 17 mm
Imaging using others masks

## Slide 18: Conclusion and Next step
Since July 2011, the detector is ready for neutron imaging data taking
The Characteristics were studied using 55Fe and 241Am+Be
Still need to optimize the converter and the drift space
- Using 1mm polyethylene as converter layer
- Using thin drift gap (1mm) to reduce the inaccuracy
- Using thick drift gap (3cm) to get good proton track

## Slide 19
Terracotta soldier
Church
Clean room

## Slide 20
Thank you!