## Slide 1: TPC for ILC and application to Fast Neutron Imaging
L. An2, D. Attié1, Y. Chen2, P. Colas1, M. Riallot1, H. Shen2,
W. Wang1,2, X. Wang2, C. Zhang2, X. Zhang2, Y. Zhang2
(1)
(2)
5th FCPPL workshop Orsay-Saclay, France
21-23 March 2012

## Slide 2: Micromegazs TPC for ILC
A TPC for ILC:
2008-2011: 7 different modules have been tested at DESY, one at a time
2012: 7 fully integrated modules will be tested at DESY

## Slide 3: Micromegas TPC for ILC
Uniformity (B = 0T)
Resolution as a function of drift distance (B=1T)
Average charge by row using cosmic-ray events
The av. thickness is less than 0.2 Xo

## Slide 4: Fast Neutron Imaging
Within FCPPL:
application to Fast Neutron Imaging with Lanzhou University
1. R&D of Fast Neutron Imaging detector based on Bulk-Micromegas Mini-TPC , Huaya Shen, 4th FCPPL, Shandong
2. R&D of a Fast-Neutron Imaging Detector Based on Bulk-Micromegas TPC, David Attié, 2011 IEEE Nuclear Science Symposium and Medical Imaging Conference
Lanzhou
Sichuan
Distance: 800km
Data taking:
241Am-9Be source
14MeV Neutron beam

## Slide 5: Micromegas TPC for neutron imaging
gas
128 µm
HVmesh
Eamp ~ 30 kV/cm
10 mm
HVdrift
Edrift ~ 200 V/cm
Wax
Pb
Detector layout: 1728 (36 ×48) pads of 1.75 mm × 1.50 mm
Gas mixture: Argon + 5% Isobutane
+ bulk Micromegas
Elastic scattering on hydrogen n  p
+ masks (Pb, paraffin wax)
PCB
Micromegas
n
p
Aluminized polyethylene 25 µm
between 2 layers (0.5 µm) of Al
57.4 mm
88.6 mm
Cosmics
(x, y, t)

## Slide 6: Characteristics and simulation of FNI detector
Expected characteristics of Fast Neutron Imaging detector based on TPC:
High spatial resolution: <100 µm
high quality imaging from Micro-Pattern Gas Detector
as Micro-Mesh Gaseous Structure (Micromegas)
  Low efficiency: ~ 0.01-1%,
  subject to thickness and kind of converter
  suitable for beam monitor/profile
  imaging in very high flux
Simulation tools:
  Garfield (electric fields and gas properties)
  Geant4 (physics processes)

## Slide 7: Monte-Carlo simulation
Data reconstruction method:
  identify cluster (track)
  extract hit position where the time is maximum tmax  interaction point
  integrate all events  image
Neutron event interacting
with polyethylene foil
and knocking out a proton
n
p
e- avalanche
Garfield
Avalanches
Proton track
X-Y readout plan
Drift time
 = 91.9 µm
p
Avalanche drift time
y-z readout plane

## Slide 8: Geant4 simulation for converter efficiency
Neutronproton recoiling efficiency in a polyethylene [C2H4]n layer coming from 241Am-9Be source
Incident neutron spectrum
According to ISO 8529(*)
* INTERNATIONAL STANDARD ISO 8529. Reference neutron radiations – Part 1: Characteristic and methods of productions. International Standard ISO 8529-1 (2001).
W.Wang_5th FCPPL workshop Orsay-Saclay,France
21-23 March 2012
8

## Slide 9
Assembled FNI detector
Readout electronics:
The AFTER-based electronics

## Slide 10
Gain curve measured from 5.9 keV line using 55Fe source. Signals read out on the mesh in Ar/Isobutane 5%: G~103 @ 300 V
Energy resolution of ~12 % due to detector capacitance and noise
best energy resolution measured for a bulk Micromegas (~7 %)
Performances of the Micromegas detector

## Slide 11
Data sample from source
36
48
Located in Lanzhou University, data taking in July 2011
Intensity: ~6 ×106 Hz (4π)
Neutron energy spectrum, according to ISO 8529 (reference radiations for calibrating neutron-measuring devices)
Mean energy ~4.5 MeV, up to 11 MeV
241Am–9Be source

## Slide 12
64mm plastic in front of the detector
Vmesh = 300V Electronic Gain = 360
Cluster size is maximum at ~5
Uniform time spectrum
Data analysis and results

## Slide 13
Thickness: 17 mm
3 mm
Pb
Paraffin
+
Imaging
Counting
mode
Tracking +cuts in time & charge
Imaging with Lanzhou mask

## Slide 14
Counting
mode
Thickness: 17 mm
3 mm
Pb
Paraffin
Imaging
Tracking +cuts in time & charge
+
Imaging with CEA mask

## Slide 15
1.5 mm
3 mm
3.5 mm
5 mm
2.5 mm
Thickness: 17 mm
Imaging using others masks

## Slide 16: Conclusion and Next step
Since July 2011, the detector is ready for neutron imaging data taking
The Characteristics were studied using 55Fe and 241Am+Be
Still need to optimize the converter and the drift space
- Using 1mm polyethylene as converter layer
- Using thin drift gap (1mm) to reduce the inaccuracy
Or Using thick drift gap (3cm) to get good proton track

## Slide 17
Thank you!
IN CHINA this work is supported by the National Science Foundation of China,Grant No.:10875054 and 10605011 and by the Fundamental Research Funds for Central University, Grant No.lzu jbky-2010-24
IN FRANCE this work is supported by the FCPPL