## Slide 1: A TPC for the Linear Collider
P. Colas
on behalf of LCTPC
Frontier detectors for frontier physics
12 th Pisa meeting on advanced detectors
Isola d’Elba, 20-26 May 2012

## Slide 2: 2 detector concepts : ILD and SiD
SiD: all-silicon
ILD: TPC for the central tracking
Both based on the ‘particle flow’ paradigm
Benchmark process: e+e- -> HZ, Z->µµ
Requirements:
Momentum resolution
d(1/pT) <2.10-5 GeV/c with vertex constraint
d(1/pT) <9.10-5 GeV/c TPC only
(200 points with 100 µ resolution in Rf)
2-track separation: 2 mm in Rf and 6 mm in z in a high density background
Material budget: <5% X0 in the barrel region, <25% X0 in the endcap region
B=3.5 T

## Slide 3: All the R&D is gathered in LCTPC
38(*) member + 7 observer institutes from 12 countries
(*) 25 signed the MOA
www.lctpc.org

## Slide 4: The EUDET test setup at DESY
The EUDET (FP6) setup at DESY is operational since 2008
Just upgraded within AIDA (FP7): autonomous magnet with 2 cryo-coolers
SiPM trigger
Field cage

## Slide 5: Beam tests at DESY : 5 technologies
Laser-etched Double GEMs 100 µ thick (‘Asian GEMs’)
Micromegas with charge disper-sion by resistive anode
GEM + pixel readout
InGrid (integrated Micromegas grid with pixel readout)
Wet-etched triple GEMs (‘European GEMs’)

## Slide 6: Advantages of MPGDs over wires
Reduction of ExB effect (improves spatial resolution)
Less mechanical tension
Less ageing than wires
Fast signal O(few ten ns), fast and efficient ion collection
Natural or tunable suppression of ion backflow
Discharge probability and consequences can be mastered (use of resistive coatings, several step amplification, segmentation)

## Slide 7: Double GEM Modules (Asian GEMs)
Laser-etched Liquid Crystal Polymer 100 µm thick, by SciEnergy, Japan
28 staggered rows of 176-192 pads
1.2 x 5.4 mm²

## Slide 8: Performance of Double GEMs
Distortions due to HV setting on the frame : corrected offline
rf resolution at zero drift: 60 microns
Behavior consistent with expectation from diffusion.

## Slide 9: Tripple GEM Module (‘European GEMs ’)
3 standard CERN GEMs mounted on a light ceramic frame (1 mm) and segmented in 4 to reduce stored energy.
Partially equipped (1000 pads, 1.26 x 5.85 mm²)
5000 pad version being built

## Slide 10: Charge spreading by resistive foil
Resistive coating on top of an insulator: Continuous RC network which spreads the charge from s(avalanche)~15µ to mm: matching pad width improves position sensitivity
M. Dixit, A. Rankin, NIM A 566 (2006) 28
Z=20cm, 200 ns shaping
PAD RESPONSE: Relative fraction of ‘charge’ seen by the pad, vs x(pad)-x(track)
x(pad) – x(track) (mm)

## Slide 11: Micromegas Modules with resistive coating
24 rows x 72 columns of 3 x 6.8 mm² pads
Various resistive coatings have been tried: Carbon-loaded Kapton (CLK),
3 and 5 Mohm/square, resistive ink.

## Slide 12
Z=5cm
Z=35cm
Z=50cm
MEAN RESIDUAL vs ROW number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film (red points)
-> select CLK
Uniformity (B=1T data)
Row number

## Slide 13
Module 4
Micromegas results (B = 0T & 1T)
Carbon-loaded kapton resistive foil
χ2 : 10.6
Ndf: 10
B=0 T Cd = 315.1 µm/√cm (Magboltz)
Module 3
χ2 : 29.1
Ndf: 11
B=1 T Cd = 94.2 µm/√cm (Magboltz)
Cd : diffusion constant
Gas: Ar/CF4/Iso 95/3/2

## Slide 14
Module 4
Micromegas results (B = 0T & 1T)
Carbon-loaded kapton resistive foil
χ2 : 10.6
Ndf: 10
B=0 T Cd = 315.1 µm/√cm (Magboltz)
Module 3
χ2 : 29.1
Ndf: 11
B=1 T Cd = 94.2 µm/√cm (Magboltz)
Cd : diffusion constant
Gas: Ar/CF4/Iso 95/3/2
Extrapolates to <100 µm at 2.3 m in B=3.5 T

## Slide 15
Test in a high intensity p beam
Test at CERN (July 2010) at 180 kHz (5 x 2 cm² beam) showed no charging up and stable operation

## Slide 16
See T. Krautscheid’s talk, this session

## Slide 17: 7 module project – Micromegas electronic integration

## Slide 18: Integration of the T2K electronics
New detector : new routing to adapt to new connectors, lower anode resistivity (3 MW/sq), new res. foil grounding on the edge of the PCB.
New 300 points flat connectors (zero extraction force)
New front end: keep naked AFTER chips and remove double diodes (count on resistive foil to protect against sparks)
New Front End Mezzanine (FEMI)
New back-end for up to 12 modules
New DAQ, 7-module ready and more compact format
New trigger discriminator and logic (FPGA).

## Slide 19: Integrated electronics for 7-module project
Remove packaging and protection diodes
Wire –bond AFTER chips
Use 2 × 300 pins connector
25 cm
14 cm
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
3,5 cm
3,5 cm
FEC
Chip
after 2 weeks of operation: no ASIC lost:
  The resistive foil protects against sparks

## Slide 20
Goals:
-test of full integration
-test of quasi industrial production, with characterization and qality procedures
The goal of < 25% X0 is attained
radiator

## Slide 22
Thermal studies. IR camera shows hot spots (regulators, ADC). T-probes on every component.
Nitrogen cooling
Onset of the electronics
2-phase CO2 cooling under study (KEK, Nikhef)

## Slide 23
Confirms previous measurements (excl. rows with ASICs in bad contact).
Optimum resolution now obtained for peaking time below 200 ns : good for 2-track separation
Preliminary results (May 2011) : resolution (B=1T data)
Resolution vs z for various peaking times.

## Slide 25: Ion disk and gating
During 1 ms every 200 ms, bunch crossings produce ionization in the gas: positive ions drift very slowly to the cathode. Ions produced in the avalanches near the anode drift all the way back to the cathode, resulting in a slowly moving ion sheet.
Background evts have been simulated and charge density and resulting electric field estimated. Preliminary results :
Primary ionization gives up to 8.5 µm distortions (can be tolerated)
‘ion sheet’ effect results in 60 µ distortions (not acceptable)
With a gating grid near the anode, this can be reduced to a negligible amount.
-> gating is necessary between train crossings

## Slide 26: Preparation for future electronics
Design and optimization work in progress for a new chip GdSP, evolution from SALTRO16:
  64 or 128 channels
  130 nm technology
  Very low noise
  Integrated ADC
  Low power consumption (all-inclusive 7-8 mW/ch)
  6 different power regions for power cycling
  High level filtering (baseline subtraction, spike removal)
Gaseous detector Signal Processor, P. Aspell et al.

## Slide 27: Software : track reconstruction and fitting
Going from various programs for track reconstruction to one (Marlin TPC) within LC framework
  Can serve for all beam test prototypes and for ILD simulation data
  Allow multi-module alignment
  Kalman filter track finding and fitting

## Slide 28: CONCLUSIONS
MPGDs have been shown to fulfill the requirements for the readout of a TPC for the LC.
Pixel readout needs more development to gain in reliability and operability in large surfaces.
Integration work (electronics and cooling) is going on, and practical production issues are addressed for the pad readout.
All aspects/limitations are being addressed to be included in the ‘Detector Baseline Document’

## Slide 29
Uniformity
Average charge by row
Using cosmic-ray events
B=OT
Excellent uniformity up to the edge of the module, thanks to the ‘bulk’ technology.
Average charge by row
Using 5 GeV e-
B=1T
0 5 10 15 20
0 5 10 15 20
z distribution

## Slide 30: Neff measurement with Micromegas
Averaging B=0T and B=1T data, modules 4, 5 and 3 (excluding ink module):
  Neff = 38.0±0.2(stat) (systematics difficult to assess)
  σ0= 59 ± 3 µm
  Note that 1/<1/N> = 47.1 from Heed for 5 Gev electrons on 6.84mm long pads.
  Thus Neff has to be between 23.5 (for exponential gain fluctuations) and 47.1 if there are no gain fluctuations.
  1/<1/N> = 34.9 for 5.4 mm pads (GEM case).
D. Arogancia et al., NIM A 602 (2009) 403