## Slide 1: Construction and tests of a TPC endplate prototype for the ILC
P.Colas D.Attié, W.Wang, I.Giomataris
CEA/Saclay, France
K.Fujii T.Fusayasu, K.Kato, M. Kobayashi,
T. Matsuda, O. Nitoh, A Sugiyama, T. Watanabe
KEK/IPNS, Nagasaki U., Kinki U., TUAT, Saga U., Kogakuin U., Sokendai, Japan

## Slide 2: ILD &TPC
ILD detector concept
ILC-TPC Large Prototype
Design for an ILD TPC in progress 2x80 modules with 8000 pads each
Spatial Resolution δ(x) ~ 100 μm in a 3.5T
for the full 2.3 m drift
Seven Micromegas modules will be tested simultaneously in June 2012 with new integrated electronics.
New GEM modules and SALTRO16 chips are being prepared for the momentum resolution measurements in 2012.

## Slide 3: FJPPL Report
In May last year, despite the earthquake, P. Colas’s travel, planned well in advance, took place, and most of the Japanese team was present during this week of collaborative work.
A 2-phase CO2 circulation cooling system was built and will be installed at DESY.
Ion backflow studies were started.
The test-beam analysis software is being developed under the MarlinTPC framework. The Kalman filter implementation of track finding and fitting is used in the ILC software.
Akiya Miyamoto’s office after the big earthquake

## Slide 4: FJPPL Report from 4/2011 to 3/2012
Spending on French Funds |  |  |  | 
Description | €/unit | Nb of units | Total (€) | Provided by:1
P. Colas, 9 days in KEK (May 18-27) | 80 | 9 | 720 | CEA/Irfu
Travel | 1200 | 1 | 1200 | CEA/Irfu
W. Wang, 7 days in Kobe (August 28 – Sep 4) for MPGD/RD51 conference | 150 | 10 | 1500 | CEA/Irfu
Travel | 1200 | 1 | 1200 | CEA/Irfu
I Giomataris, 4 days in KEK | (150) | 4 | (600) | (KEK)
Kamioka to Tsukuba travel (IG) | (200) |  | (200) | (KEK)
Total |  |  | 4940 | 
Spending on KEK Fund |  |  |  | 
Description | k¥/Unit | Nb of units | Total (k¥) | 
K. Fujii, 8 days at Saclay, Jan 4-11 | 20 | 8 | 160 | 
T. Matsuda | 20 | 3 | 60 | 
Travel | 150 | 2 | 300 | 
Total |  |  | 520 | 

## Slide 5: Large prototype at DESY
May 2012 at DESY after upgrade
at Toshiba company (July,2011- March 2012)
Modification:
Add cryo-coolers at 4 and 10K.
PCMAG is based on the conduction cooling of the thin superconducting coil from the reservoir tank filled with Liq. He. It is rather easy to switch to the cooling by cryo-coolers (actually to cool the reservoir tank).
Advantages in the operation after the modification:
Simply switch-on the cryo-coolers to start cooling PCMAG.
No Liq. He fillings, no recovery of He gas, and no pre-cooling.
Safe operation without Liq. He.
Long-period, unattended-operations possible.

## Slide 6: Several type of readout modules are studied.
LP Modules
Readout | Pads (width:1~3mm) | Timepix (pixel: 55µm ×55µm)
MPGDs | Double GEMs (Laser-etched) Japanese team | 
 | Triple GEMs (wet-etched) | Triple GEMs
 | Micromegas (Resistive anode) French team | Ingrid (Micromegas)

## Slide 7
Resistive ink
~2(?) MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
2 Resistive Kapton
~3 MΩ/□
Micromegas modules (@ Saclay)

## Slide 8
7 Micromegas modules with electronic integration

## Slide 9
Remove packaging and protection diodes
Wire-bond AFTER chips
Use 2 × 300 point connector
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
14 cm
25 cm
FEC
3,5 cm
3,5 cm
Chip
after 2 weeks of operation: no ASIC lost:
  The resistive foil protects against sparks
integrate electronic

## Slide 10
New T2K Electronics
FEM
FEC
Module frame

## Slide 11
Temperature during switching on
Temperature after cooling (Nitrogen cooling)
Electronics thermal studies

## Slide 12
24 rows x 72 columns of 3 x 6.8 mm² pads
Events display

## Slide 13
Resolution of the detector (B=1T)
0 : the resolution at Z=0
Neff : the effective number of electrons

## Slide 14
Bench test using 55Fe
Tested at CERN
Tested at Saclay
55Fe spectrum
Preliminary

## Slide 15
MarlinTPC
Marlin based simulation, digitization, reconstruction and analysis code for the TPC.
see: http://ilcsoft.desy.de/portal/software_packages/marlintpc/
KalTest: (installed in Marlin)
A ROOT-based Kalman Filter Package.
- Minimum number of user-implemented classes
MeasLayer : measurement layer
KalDetector : an array containing MeasLayers
You can put different kinds of MeasLayers
Hit : coordinate vector as defined by the MeasLayer
Marlin TPC and Kalman filter

## Slide 16
Events display
Compared some pulses between LPMon online display programme and MarlinTPC (ILC framework)
One « event display »:
LPDisplay
MarlinTPC
Y
X

## Slide 17
CED Viewer

## Slide 18
Double GEM (@ KEK)

## Slide 19: GEM events in Marlin TPC

## Slide 20
Several type of readout modules(Micromegas and GEM) have been studied and the resolutions of both seem to fulfill the requirements for the readout of a TPC for the ILC.
Integration work (electronics and cooling) is going on.
A 2-phase CO2 circulation cooling system was built at KEK and will be installed at DESY
Software is being developed under the MarlinTPC framework.
Plan for this year is to continue collaborative analysis of GEM and Micromegas data, and develop common software. Request 8000 € for France and 1250 k¥ for Japan(4 travels for each side).
Conclusion

## Slide 21
Thank you!