## Slide 1: Study of the Micromegas-TPC Modules for an ILC Detector
Wenxin Wang
On behalf of LCTPC
2012 Nuclear Science Symposium, Medical Imaging Conference
& workshop on Room-Temperature Semiconductor X-Ray and Gamma-Ray Detectors
Oct. 29-Nov. 3, 2012, Anaheim, California

## Slide 2
7 Micromegas modules with integration of electronics
2008-2011
2012-

## Slide 3
Bulk Micromegas with charge spreading
PRF(Pad Response Functions) fits, z ~ 5 cm
M. Dixit, A. Rankin, NIM A 566 (2006) 28
x(pad) – x(track) (mm)
Resistive bulk : continuous RC circuit to spread the charge to improve resolution

## Slide 4
B=0 T Cd =315.1 µm/√cm (Magboltz)
B=1 T Cd = 94.2 µm/√cm (Magboltz)
Data analysis results (B = 0T & 1T)
(One module installed at the end plane of TPC with old electronics)
60 µm Resolution at z=0
z drift dependence agrees with diffusion, with large Neff
Extrapolates to better than 100 microns at 2.3 m in B=3.5T

## Slide 5
Remove packaging and protection diodes
Wire-bond AFTER chips
Use 2 × 300 point connector
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
14 cm
25 cm
FEC
3,5 cm
3,5 cm
Chip
The resistive foil protects against sparks
Electronics integration
(See D. Calvet et al. Real time 2012)

## Slide 6
New T2K Electronics
FEM
FEC
The av. thickness is less than 0.2 Xo
all included (det., FECs, Mezzanine, connectors, cooling, shielding)
Every module will be calibrated with a source on a test bench

## Slide 7
6 Modules Test
Cosmic event
In July 2012, 6 modules were installed on the endplate of LP-TPC at DESY and tested at the same time. Data were taken with cosmic rays and 5 GeV e- beam.
Notes: 77

## Slide 8
Event display (the first 100 triggers of a good run)

## Slide 9
Track reconstruction

## Slide 10
Outside crack
In crack
Upper crack
Lower crack
Padrow number (3x24=72)
5 GeV
e- Beam
Crack scan
x

## Slide 11
Number of hits vs x (72 pad-rows)
Study the hit reconstruction efficiency at or near the crack: take data with beam, moving by steps of 2mm
Crack scan

## Slide 12
Gain study
Using the fitted MPV of the (Landau) distribution of the measured charge
Effective gain vs mesh voltage
(compared with the direct gain measurements using 55Fe source on a bulk detector without resistive foil)
Effective gain vs drift distance
(Vmesh=380V, Vdrift=140V/cm, peaking time 100 ns and 400 ns)

## Slide 13
Data analysis results (B = 1T)
Row Number: 3 x 24 = 72
Displacement in mm
(a): Before alignment
(b): After alignment
df= 3.3 , 2.2 and 3.1 mrad
dx = 55 µm, -36 µm and 63 µm
(c): After ‘brute force’ correction (i.e. average subtraction and refit)
(a)
(b)
(c)
dx (mm)
Residuals by padrow
dx (mm)
dx (mm)

## Slide 14
Data analysis results (B = 1T)
drift distance 30cm
Row number
Residual rms (mm)
Effects of approximate geometry

## Slide 15
A lot of experience has been gained in building and operating Micromegas TPC panels. The measured resolution of one module is about 60 microns at zero drift distance with 3 mm wide pads. This meets LC needs.
Successful test of 6 modules simultaneously with full integration of the electronics flat behind the panels. The analysis work is on-going.
Next step: 7 modules high quality test, full calibration on the test bench
Summary
The analysis work is under the cooperation with Carleton colleagues. Thanks to our DESY colleagues, Japanese colleagues.

## Slide 16
Thank you!