## Slide 1: A Micromegas TPC for the ILC
Wenxin Wang

## Slide 2
L: 4.7m
: 3.6m
Design for an ILD TPC in progress:
Each endplate: 80 modules with 8000 pads
Spatial Resolution (in a B=3.5T magnetic field):
δ(x) ~ 100 μm for the full 2.3 m drift
ILD-TPC for ILC
ILD

## Slide 3
Large Prototype-TPC (LP-TPC)
Magnet up to 1.2T
Field cage: 61 cm length and 72 cm diameter
7 interchangeable modules with keystone shape

## Slide 4
MPGD: Micromegas & GEM
Several types of readout modules are studied
Readout |  | Pad Size | Electronics | Groups
MPGDs | Double GEMs (Laser-etched) | (~ 1 × 6 mm2 Pad) | ALTRO | Asia
 | Triple GEMs (wet-etched) |  |  | Desy
 | Micromegas (Resistive anode) | (~ 3 × 7 mm2 Pad) | AFTER | Saclay-Carleton
Micromegas
(test with 7 modules)
GEM
(test with 3 modules)

## Slide 5
pads
mesh
E
B
resistive foil
glue
pads
mesh
E
B
Pad width limits MPGD TPC resolution
Direct signal readout technique
: pad width
0 : resolution at Z=0 without diffusion
Charge dispersion technique with a resistive anode so that wide pads can be used for centroid determination
Micromegas with Resistive Anode

## Slide 6
Micromegas module
Module size: 23 cm × 17 cm
24 rows × 72 columns
Readout: 1726 Pads
Pad size: ~3 mm × 7 mm

## Slide 7
Resistive ink
~3 MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
Resistive Kapton
~3 MΩ/□
Micromegas modules

## Slide 8
Z=5cm
Z=35cm
Z=50cm
Mean Residual vs Row Number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film
(red points)
Uniformity
Row Number

## Slide 9
Beam test
2008~2011:
Test with one module
T2K electronics
(32cm × 25cm × 14cm )
2012~2013:
Test with
multi-modules
Integrated electronics ( 23cm × 17cm × 5cm )
Fully integrated Module
Resistive Micromegas Detector
FEC
FEM

## Slide 10
Event display
2D or 3D display software available
Online monitor
Offline monitor

## Slide 11
Drift Velocity
Test in 2009 (B=0T):
T2K gas: Ar:CF4:iso=95:3:2
T=19oC - P = 1035hPa
H2O:35ppm
At E=230 V/cm :
Vdrift = 7.698 +- 0.040 cm/µs (Magboltz : 7.583+-0.025(gas comp.))
The difference is 1.5+-0.6 %

## Slide 12
Gain Study
For 6.84 mm pitch and 5 GeV e-
Expectations for Ntot: 61.9
(from HEED simulation)
ADC
Gain

## Slide 13
Test bench
Energy Resolution :~13% rms
Gain ~2600
(using collimated source, Vmesh=380V)
The 55Fe source is put in an aluminum collimation tube and fixed on a set of two mechanical arms (X-Y).

## Slide 14
Spatial resolution
Event selection

## Slide 15
Spatial resolution
: supposed residual of the detector
: the fitted hit position in test row
: the position of track crossing the test row
X (mm)
X (mm)
(a) Fit track with all rows
(b) Fit track without using hit in row 35
(c) Fit track after selection hits (row 35)
Hits selection
Row number
Row number

## Slide 16
Spatial resolution
B=1 T Cd = 94.2 µm/√cm (Magboltz)

## Slide 17
Compare with GEM
( Spatial resolution )

## Slide 18
Field distortions
B=1T
B=0T
After alignment
B=0T

## Slide 19
Field distortions
Distortions at different drift distances
in B=0T or B=1T
B=1T
B=0T

## Slide 20
Conclusion
A lot of experience has been gained in building and operating Micromegas TPC panels.
The characteristics of the Micromegas modules, such as the uniformity, energy resolution, stability have been studied in detail.
7 modules have been successfully tested with full integration of the electronics at the same time.
Thanks to the resistive technology, the measured resolution is about 60 microns at zero drift distance with 3 mm wide pads. This meets ILC needs.
Distortions are observed. Their detailed study will allow to correct them and improve the design to minimize them.

## Slide 21
Thank you !