## Slide 1
On behalf of the LCTPC collaboration
Study of a Large Prototype TPC using
Micro-Pattern Gas Detectors
─ David Attié ─
CEA Saclay/Irfu
www.lctpc.org
Notes: I’m here to present a TPC review

## Slide 2: Overview
Introduction: Physics case at International Linear Collider (ILC)
R&D of a Large Prototype Time Projection Chamber for ILC
TPC Readout using Micro-Pattern Gaseous Detectors:
  GEM modules with ALTRO electronics
  Integrated AFTER-based electronics and resistive Micromegas detector module
  Pixel readout
Studies
  Transverses resolution
  Multi-module effect & field distorsions
  Ion feedback
  2-Phase CO2 cooling
Conclusion

## Slide 3: Introduction: Physics Case at ILC
B=3.5 T
e+eHZ,Zµµ
Identify the particle of cosmic dark matter
Find the origin of the masses of elementary particles
  precision of Higgs coupling to each particle mass
  sensitivity of the ILC experiments to Higgs boson couplings in a model-independent analysis
Higgs-strahlung recoil mass: e+e- → ZH (Z→μ+μ-/e+e-) + X
Next collider: linear e+e– collider, length: ~ 31km
Tunable center of mass energy of 200-500 GeV
Two detectors with push-pull concept
Particle Flow* concept necessary [*] Particle flow: the aim to reconstruct every particle in the best suited sub-detector

## Slide 4: Time Projection Chamber for ILD
TPC is the central tracker for International Linear Detector
– Large number of 3D points  continuous tracking
– Good track separation and pattern recognition
• Low material budget inside the calorimeters important for PFA
– Barrel: inner <1% X0 ; outer <5% X0 – Endplates: ~25% X0 (<10 cm)
• Two options for endplate readout (MPGD):
    – GEM
    – Resistive Micromegas
• Alternative: pixel readout
ILD
TPC Requirements :
Momentum resolution:
(1/pT) < 9×10-5 GeV-1
Spatial resolution at 3.5T:
(r) < 100 m
(z) < 500 m
Field uniformity:
E/E~2×10-4
Tracking eff. for pT>1 GeV: 97%
dE/dx resolution ~5%
4.7m
3.62m
Cathode membrane
Endplate
MPGD
Large Prototype
TPC

## Slide 5: Large Prototype TPC for ILC
Built by the LCTPC collaboration in 2008
Financed by EUDET
Magnet upgraded in 2012 within AIDA
Located at DESY: 6 GeV e- beam
Sharing out :
- magnet: KEK, Japan
- field cage, stage: DESY, Germany
- cosmic trigger: Irfu, France
- beam trigger: Nikhef, Netherlands
- endplate: Cornell, USA
- Resistive Micromegas: Irfu, France, Carleton/Montreal, Canada
- Double GEMs with 100m laser-etched crystal polymer: Saga, Japan
- Triple 50m GEMs: DESY, Cern
- TimePix pixel: F, G, NL<
1T PCMagnet on lifting stage
Large Prototype TPC
Endplate + 7 Micromegas modules

## Slide 6: Micro-Pattern Gas Detectors: Micromegas & GEM
50-100 µm
40 kV/cm
~1000 µm
1 kV/cm
GEM
~100 µm
80 kV/cm
Micromegas
Technology choice for TPC readout: Micro-Pattern Gas Detector
more robust than wires
no E×B effect
better ageing properties
easier to manufacture
Avalanche
fast signal & high gain
low ion backdrift
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes
use of 2 or 3 stages
MICROMEsh GAseous Structure (Y. Giomataris et al., 1996)
metallic micromesh (typical pitch 50-100 µm)
supported by pillars, multiplication between anode and mesh, high gain
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes (50-100 µm)
2-3 layers needed, high gain

## Slide 7: Asian GEMs
Double GEM module using Laser-etched Liquid Crystal Polymer of 100 µm
Made in Japan (SciEnergy)
Pad size: 1.21×5.4 mm2
28 staggered rows of 176-192 pads 4829 channels
3 modules equipped (10 000 channels) read out by ALTRO electronics
Next step: SALTRO with better integration

## Slide 8: European GEMs
Triple GEM module with thin ceramic frame (1mm)
Manufactured at Cern (50 µm)
Pad size: 1.26×5.85 mm2
28 rows (4829 channels)
3 modules equipped (10 000 channels)
read out by ALTRO electronics

## Slide 9: Resistive Micromegas
Pads PCB
+
Micromegas
Cooling system
Front-End Mezzanine
Front-End Card (FEC)
Fully integrated Module
Resistive Micromegas Detector
FEC
FEM
Micromegas with resistive coating
Various resistive coatings have been tried:
  Carbon-loaded Kapton (CLK): 3 and 5 M/,
  resistive ink
Pad size: 3×6.8 mm2
24 pad rows (1726 channels)
7 modules equipped (12 000 channels) read out by fully integrated electronics based on AFTER chips (T2K TPC)
Resistive foil
Isolated layer
Pads
PCB
Micromegas mesh
d/X00.24
See Dixit et.al., NIM A518 (2004) 721

## Slide 10: Pixel Readout R&D
GEM
InGrid
Bonn
Bonn, Nikhef
Irfu, Nikhef
TimePix chip: matrix of 256 × 256 pixels of 55 × 55 µm² size
Each pixel can be set to:
  Hit counting
  Charge measurement
  Time measurement

## Slide 11: LCTPC Software Framework
Reconstruction, simulation, analysis based on common ILC software tools:
  LCIO (Linear Collider I/O): event data model
  Marlin (Modular Analysis & Reconsctruction for the LINear Collider)
  LCCD: (Linear Collider Conditions Data toolkit)
  Gear: (Geometry Api for Reconstruction)
Specific software package of LCTPC:
MarlinTPC: https://znwiki3.ifh.de/MarlinTPC/MarlinTPC
  Reconstruction processors
  Conditions handling
  Simulation (coarse to detailed)
  Common analysis for standard plots
Data
  Testbeam data stored on Grid storage
  → accessible by whole collaboration
  Common conditions database server

## Slide 12: Transverse resolution [Resistive Micromegas]
Gas: Ar/CF4/Iso 95/3/2
B = 0 & 1T
B=0 T
Cd = 315.1 µm/√cm (Magboltz)
B=1 T
Cd = 94.2 µm/√cm (Magboltz)
0: resolution at z=0
Neff: effective number of electrons
Cd : the diffusion constant

## Slide 13: Transverse resolution [GEMs]
Gas: Ar/CF4/Iso 95/3/2
B= 1T
Asian GEM
European GEM
0: resolution at z=0
Neff: effective number of electrons
Cd : the diffusion constant

## Slide 14: Field distorsions at B=0T
B=0T, distortions due to E only
  r direction: 150 to 200 µm corrected down to 20 µm
  Z direction: few 100 µm (50 µm)
Before corrections
After corrections
14
r
Z

## Slide 15: Field distorsions at B=1T
Before correction
B=1T for GEM and Micromegas
  r et Z directions: distorsions up to 1 mm corrected down to 200 µm
GEM
Micromegas
After correction
r
Z
Before correction

## Slide 16: Ion Back Flow Issue
Primary ions create practically no distortions in the Electric field O(<1µm)
After each bunch train, a disk of positively charged ions from the amplification stage drifts back into the TPC volume
1 to 2 orders of magnitude safety margin with estimated background
is needed
A gating grid will be built

## Slide 17: Data taking in 2014
Cosmics
UV Laser
Beam 4 GeV
Edrift (V/cm) | Drift Velocity (cm/s) | 
 | Measured | Simulated
230 | 7.44±0.01 | 7,55±0.1
140 | 5.84±0.01 | 5,79±0.1
T2K gas: Ar/CF4/Iso 95/3/2
Gas impurity:
  60 ppm O2,
  150 ppm H2O
Electron momentum measurement

## Slide 18: Test of CO2 Cooling System
2-phase CO2 cooling system (TRACI) used with the LP setup of the Micromegas modules with integrated electronics (26W/module)
CO2 has lower viscosity & higher latent heat than all usual refrigerants
  Very small pipes (high pressure with low material budget)
  CO2 liquid & gas can be used at room temperature
Operation and test conditions :
  2PCO2 at 45 bars 10°C
  Temperature control during different regimes
    5V LV supply on, nocooling
    LV supply off, with cooling
    LV supply on, with cooling
    2 series of measurement
About 30°C stable temperature was achieved during operation of 7 Micromegas modules at DESY
7 FEMs
6 FECs per FEM
50 bars
45 bars

## Slide 19: Pulse Shape Fit Procedure
Fit each individual (main) pulse with f(t)
  normalize amplitude to Amax pulse-by-pulse
  force pulse maximum at zero
  3 time bins before and 2 time bins after
Significatively improved compared to parabolic or box fit
The following analysis function f(t) is proposed for
determination of the charge using pulse shape:

## Slide 20: Pulse Shape Fit Procedure
Z resolution study with the Kalman filter is then performed in MarlinTPC
  improvement of about 25% all over drift distance
  this method shows homogeneous resolution across a module

## Slide 21: Summary
The LCTPC collaboration have been working since many years on a Large Prototype of a TPC
The performance of two MPGD technology reached the requirements of the ILD detector
Studies are going on: ion back drift, electronics, mechanical integration, software processors ...
The readout technology has to be chosen (GEM or Micromegas) for the ILD
The presented infrastructure has received funding from the European Commission under
the FP7 Research Infrastructures project AIDA, grant agreement no. 262025.

## Slide 22: Thank you

## Slide 23: Backup slides

## Slide 24: TRACI Cooling System
Development of a portable CO2 laboratory cooling unit called Traci
  TRACI=Transportable Refrigeration Apparatus for CO2 Investigation.
Development in AIDA framework together with interested partners.
  Nikhef & CERN lead development with engineering support of the Cracow University of Technology.
  Co-funding from clients
Designed for applications like:
  Test beam telescope (AIDA)
  Micro channel development (LHCb)
  Pixel development (CMS)
  Detector thermal/mechanical support structure development (Atlas IBL, ILCTPC)
  Detector commissioning (Atlas IBL)
Focus on simplicity for easy production in series
bart@nikhef.nl