## Slide 1
Gaseous Detectors:
From Multi-Wire Proportional Chamber
to Novel MPGD Gaseous Detectors
Maxim Titov, CEA Saclay, France
50 mm
140 mm
Micromegas:
International Workshop on Advanced Detectors (IWAD),
Kolkata, India, October 27-28, 2014
TPC
OUTLINE:
Introduction: Gaseous detector family
Multi-wire proportional (MWPC) and drift chambers, time projection chamber (TPC)
Novel Micro-Pattern Gaseous Detectors
MPGD Technologies for future physics projects
Georges Charpak and CERN: 60 years of science for piece
Ingrid
Thick GEM +
(THGEM)

## Slide 2
The History of Instrumentation is VERY Entertaining
A look at the history of instrumentation in particle physics
 complementary view on the history of particle physics, which is
traditionally told from a theoretical point of view
The importance and recognition of inventions in the field of instrumentation is proven by the fact that
 several Nobel Prices in physics were awarded mainly or exclusively
for the development of detection technologies
Nobel Prizes in instrumentation (“tracking concepts”):
1927: C.T.R. Wilson, Cloud Chamber
1960: Donald Glaser, Bubble Chamber
1992: Georges Charpak, Multi-Wire Proportional Chamber

## Slide 3
History of Particle Detection

## Slide 4
History of Gaseous Detectors
M. Hoch, 2004 Wire Chamber Conference

## Slide 5
Multi-Wire Proportional Chamber (MWPC)
High-rate MWPC with digital readout:
Spatial resolution is limited to sx ~ s/sqrt(12) ~ 300 mm
S ~ 1 mm
TWO-DIMENSIONAL MWPC READOUT CATHODE
INDUCED CHARGE (Charpak and Sauli, 1973)
Spatial resolution determined by: Signal / Noise Ratio
Typical (i.e. ‘very good’) values: S ~ 20000 e: noise ~ 1000e
Space resolution < 100 mm
Resolution of MWPCs limited by wire spacing
better resolution  shorter wire spacing  more (and more) wires...

## Slide 6
Multi-Wire Proportional Chamber (MWPC): Electronics Imaging Device
The 1st “Large Wire Chamber”:
Georges Charpak with Fabio Sauli, Jean Claude Santiard
The invention revolutionized
particle detection and
High Energy Physics, which passed from the manual
to the electronic era.
MWPC:
1968 by Georges
Charpak;
Noble Prize 1992

## Slide 7
Born in Dabrowica, Poland in 1924 (now Dubrovytsia, Ukraine)
Moved from Poland to Paris in 1931
During 2nd war served in resistance and emprisoned
In 1944 he was deported to the Nazi concentration camp at Dachau
In 1955, Phd from the College de France, Paris, under Frederic Joliot-Curie
In 1985 member of the French Academy of Science
Nobel Prize for Physics in 1992
Georges
Charpak

## Slide 8
Georges Charpak with Friends
Slides and/or photos are taken from presentations of his colleagues and friends:
Amos Breskin, Fabio Sauli, Yannis Giomataris

## Slide 9
VERSAILLES,
10-13 September 1968
MWPC # 1
First Public Presentation of the Multi-Wire Proportional Chamber

## Slide 10
First Large Experiment with MWPCs

## Slide 11
1968: Multi-Wire Proportional Chamber (MWPC)
G. Charpak,R. Bouclier, T. Bressan,J. Favier and C. Zupancic: The use of Multiwire Proportional Counters to select and localize Charged Particles, Nuc. Instr. and Meth. 62(1968)262
ENERGY RESOLUTION ON 5.9 KeV:
DEPENDENCE OF COLLECTION TIME FROM TRACK’S DISTANCE:
DRIFT CHAMBERS

## Slide 12
Drift Chambers
THE ELECTRONS DRIFT TIME PROVIDES THE DISTANCE OF THE TRACK FROM THE ANODE:
FIELD
ANODE
Factors affecting spatial resolution:
Distribution of primary ionization
Diffusion
Readout electronics
Electric field (gas amplification)
Range of ‘delta electrons’
The spatial resolution is not limited to the cell size
FIRST DRIFT CHAMBER OPERATION (H. WALENTA ~ 1971)
HIGH ACCURACY DRIFT CHAMBERS (Charpak-Breskin-Sauli ~ 1973-75)

## Slide 13
Nobel Prize: W, Z - Discovery at UA1/UA2 (1983)
UA1 used the largest imaging drift chamber of its day (5.8 m long, 2.3 m in diameter)
It can now be seen in the CERN Microcosm Exhibition
Z  ee (white tracks)
Particle trajectories in the CERN-UA1
3D Wire Chamber TPC
Discovery of W and Z bosons
C. Rubbia & S. Van der Meer Nobel 1984

## Slide 14
Time Projection Chamber (TPC)
Gas volume
Readout
z
x
y
ALICE
Separate two regions:
Long drift along z ~ 1-3 m;
Amplification at the end plate
Challenges:
Long drift time; limited rate capability
LXe TPC
The TPC is a gas-filled cylindrical chamber with 1 or 2 endplates (D. Nygren, 1974)

## Slide 15
TOPAZ (KEK)
ALEPH (CERN)
DELPHI (CERN)
PEP4 (SLAC)
STAR (LBL)
Some Detectors in Particle and Heavy Ions Physics using a TPC

## Slide 16
Track point recorded in 3-D
  (2-D channels in x-y) x (1-D channel in z = vdrift x tdrift)
Particle identification by dE/dx
  long ionization track, segmented in 100-200 measurements
STAR ion TPC BNL-RHIC
LBL STAR TPC
at BNL RHIC ion collider
TPC Characteristics
Powerfull tool for:
Lepton Colliders
Modern heavy ion collisions
Liquid and high pressure noble gases for neutrino and dark matter physics program

## Slide 17
CERN – LHC: Enormous Gaseous Detector Systems
 | Vertex | Inner Tracker | PID/ photo- det. | EM CALO | HAD CALO | MUON Track | MUON Trigger
ATLAS | - | TRD (straws) | - | - | - | MDT (drift tubes), CSC | RPC, TGC (thin gap chambers)
CMS ----- TOTEM | - | - | - | - | - | Drift tubes, CSC ----- GEM | RPC, CSC ----- GEM
LHCb | - | Straw Tubes | - | - | - | MWPC | MWPC, GEM
ALICE | - | TPC (MWPC) | TOF(MRPC), PMD, HPMID (RICH-pad chamber), TRD (MWPC) | - | - | Muon pad chambers | RPC
ALICE TPC
Straw tubes
CMS CSC
Gaseous detectors are still the first choice whenever the large-area coverage (e.g. muon systems) with low material budget is required

## Slide 18
ALICE Multi-Gap RPC: Timing Resolution
Relevant scale in HEP: t ~ L(m)/c ~ o(ns)
Traditional technique:
  Scintillator + PMT ~ o (100 psec)
Breakthrough with a spark discharge in gas
  Pestov counter  ALICE MRPC ~ 50psec
Technology | Time resolution
Pestov Counter | 30-50 ps
RPC | ~ 1-5 ns (MIP)
MultiGap RPC | ~ 50 ps (MIP)
GEM | ~ 1-2 ns (UV) ~ 5 ns (MIP)
Micromegas | ~ 700 ps (UV) ~ 2-5 ns (MIP)
C. Williams, CERN Detector Seminar
“ALICE Time of Flight Detectors”: http://indico.cern.ch/conference
Display.py?confId=149006
ALICE-TOF has 10 gaps (two stacks of 5 gas gaps);
each gap is 250 micron wide

## Slide 19
ATLAS Muon Detector: Modern Large-Volume Spectrometer
L3 Muon Spectrometer (LEP):
~ 40000 chan. ; s (chamber) < 200 mm
ATLAS Muon Drift Tubes (LHC):
~ 1200 chambers, s (chamber) ~ 50 mm
370000 tubes, 740000 end-plugs
12000 CCD for optical alignment
1 chamber  2 layers of 3 drift tubes
Spatial resolution /chamber (2 layers of 3 drift tubes)
Intrinsic limitation of wire chambers:
(resolution degradation at high rates):
sspace ~ 50 mm

## Slide 20
AGING PHENOMENA IN GASEOUS DETECTORS
A permanent degradation of operating characteristics
of gaseous detectors under sustained irradiation,
has been and still remains the main limitation to their use in high-rate experiments

## Slide 21
Aging Phenomena in Wire Chambers: 30 Years Ago
It was difficult to understand truly any aging measurement and extrapolate it to other operating conditions  reality is a complex mixture of many processes
First systematic attempts to summarize aging results and
to provide remedies minimizing wire chamber aging
1986

## Slide 22
Aging Phenomena in Gaseous Detectors: “High-Rate Era” (15 years ago)
High Energy Physics Experiments enters a new era which required operation of gaseous particle detectors at unprecedented high rates and integrated particle fluxes
(… a lot of “new and unexpected experience”
from HERA-B @ DESY)
2001
The HERA-B Experiment was the first high-rate experiment, which
addressed SYSTEMATICALLY aging phenomena in gas detectors,
followed later by ALL LHC Experiments

## Slide 23
There are simply too many variables in the problem 
would be too naive to expect
that one can express the aging rate
using a single variable (C/cm)
Aging Phenomena in Gaseous Detectors
R = - (1/G)(dG/dQ) (% per C/cm)
Aging phenomena depends on many highly correlated parameters:
aging rate is proportional only to the total accumulated charge
Implicit
assumption:
(Kadyk’1985)
‘NEW
AGING’
EFFECTS:
CLASSICAL
AGING:
1985
Microscopic parameters:
Cross-sections
Electron or photon energies
Electron, ion, radical densities
…
Macroscopic parameters:
Gas mixture (nature of
gas, trace contaminants)
Gas flow & Pressure
Geometry/material of electrodes & configuration of electric field
Construction materials
Radiation intensity
Gas gain, ionization density
Size of irradiation area
1985
2000

## Slide 24
Radiation Hardness of Gaseous Detectors: Rules of Thumb
Build a “full-size prototype” (the smallest independent element of your detector)
Expose full detector area of to the real radiation profile (particle type, gas gain, ionization density)
Choose your gas mixtures (hydrocarbons are not trustable) and materials very carefully
Vary all parameters systematically (gas gain, irradiation intensity, gas flow, …)
and verify your assumptions  make aging studies on several identical prototypes
Do not extrapolate aging results for any given parameter by more than an order of
magnitude
If you observed unexpected result - understand the reason – and reproduce results …
Many ORIGINAL PROBLEMS in HIGH RATE GAS DETECTORS were due to CASUAL SELECTION of chamber designs, gas mixtures, materials and gas
system components, which worked at “low rates”, but failed in harsh environments
If properly designed and constructed, gas detectors (especially Micro-Pattern Gaseous Detectors) can be robust and reliable in the high-rate environment

## Slide 25
Why do Tracking Detectors Change ?
Higher Rate, enormous occupancy:
1D easily saturated  2D  3D
Silicon detectors:
Strips Pixels (2D) 3D det-electr. integ.
Gaseous detectors
Wire Chamber  Wireless MPGD (2D)  InGrid/Timepix (3D)
50 mm
140 mm
Micromegas:
10 mm
100 mm
Ingrid
TPC
Advances in Micro-electronics & Etching Technology  Micro pattern Gaseous Detectors
Drift Chamber

## Slide 26
CERN-LHC: Enormous Gaseous Detector Systems
ATLAS TGC
LHCb Outer
Tracker
ALICE MRPC
ALICE HPMID
Upgrade Options for HL-LHC:

## Slide 27
Typical distance between
wires limited to 1 mm
due to mechanical and
electrostatic forces
Typical distance
between anodes 200 mm
thanks to semiconductor
etching technology
MWPC
MSGC
anode
cathode
cathode
A. Oed, Nucl. Instr. and Meth. A263 (1988) 351.
Rate capability limit due to space
charge overcome by increased
amplifying cell granularity
Micro-Strip Gas Chamber (MSGC)

## Slide 28
ON EXPOSURE TO a PARTICLES
Micro-Strip Gas Chambers: Discharge Problems
Induced discharges are intrinsic property of all single stage micropattern detectors in hadronic beams (MSGC turned out to be prone to irreversible damages)
Major processes leading at high rates to MSGC operating instabilities:
Substrate charging-up and time-dependent modification of the E field
→ slightly conductive support
Deposition of polymers (aging)
 validation of gases, materials, gas systems
Discharges under exposure to highly ionizing particles
 multistage amplification, resistive anodes
Uncoated
MSGC
“Conductive” MSGC

## Slide 29
MSGC Discharge Problems
MICRODISCHARGES
FULL BREAKDOWN
Discharge is very fast (~ns)
Difficult to predict or prevent
Owing to very small distance between
anode and cathode the transition from
proportional mode to streamer can be
followed by spark, discharge, if the
avalanche size exceeds
RAETHER’S LIMIT
Q ~ 107 – 108 electrons

## Slide 30
Telescope of 32 MSGCs tested at PSI in Nov99 (CMS Milestone)
HERA-B Inner Tracker
MSGC-GEM detectors
Rmin ~ 6 cm
 106 particles/cm2 s
300 mm pitch
184 chambers: max 25x25 cm2
~ 10 m2; 140.000 channels
The D20 diffractometer MSGC
is working since Sept 2000
1D localisation
48 MSGC plates (8 cm x 15 cm)
Substrate: Schott S8900
Angular coverage : 160° x 5,8°
Position resolution : 2.57 mm ( 0,1°)
5 cm gap; 1.2 bar CF4 + 2.8 bars 3He
DIRAC
4 planes MSGC-GEM
Planes 10x10 cm2
Micro-Strip Gas Chamber (MSGC)

## Slide 31
Micromegas
GEM
Thick-GEM, Hole-Type and RETGEM
MPDG with CMOS pixel ASICs (“InGrid”)
Micro-Pixel Chamber (mPIC)
Electrons
Ions
60 %
40 %
Micromegas
GEM
THGEM
MHSP
InGrid
Micro-Pattern Gaseous Detector Technologies for Future Physics Projects
mPIC
Rate Capability:
MWPC vs MSGC

## Slide 32
Christian Lippmann, 2nd ECFA High Luminosity LHC Experiments
Workshop, Aix-les-bains, France, October 21-23 (2014)

## Slide 33
1988
MSGC (ILL, A. Oed)
GEM (CERN, F. Sauli)
1996
MicroMEGAS (CEA Saclay, Y. Giomataris)
1997
2000
m-PIC (A. Ochi, T. Tanimori)
Capillary plate (Yamagata U., H. Sakurai)
1996
2005
2008
RD51
collaboration
InGrid
RD28
1992
Historical Roadmap of the MPGD Technologies and RD51 Collaboration
2003
LEM (Periale)
THGEM(Chechik)
Many of the Micro-Pattern Gaseous Detector Technologies were introduced before
the RD51 Collaboration was founded
With more techniques becoming available (or affordable), new detection concepts
are being introduced and the existing ones are substantially improved

## Slide 34
RD51 – Development of Micro-Pattern Gaseous Detector Technologies
World-wide Collaboration for the
MPGD Developments 
RD51 (91 institute, > 500 people):
Large Scale R&D program to advance MPGD Technologies
Access to the MPGD “know- how”
Foster Industrial Production
The main objective is to advance MPGD technological development and associated electronic-readout systems, for applications in basic and applied research”
1998
2014
Advances in photolithography 
Large Area MPGDs (~ m2 unit size)
http://rd51-public.web.cern.ch/rd51-public
A fundamental boost is offered by RD51: from
isolate MPGD developers to a world-wide net

## Slide 35
RD51
Large Area Detectors
Assembly Optimization
RD51 Common Projects
Generic R&D, QA
Long Term Stability
Software Tools and
Simulations
MPGD Electronics
CERN MPGD
Workshop,
Quality Control
and Industrialization
RD51 Common
Test Beam and Lab Facilities
WG5:
WG4:
WG1:
WG2:
WG7:
WG6:
Conferences / Schools
Academia-Industry
Matching Events
Future RD51 Collaboration Activities (beyond 2013)
WG3/NEW WG:

## Slide 36
MPGD Technologies for Energy Frontier (HL-LHC, LC)
 | Vertex | Inner Tracker | PID/ photo- det. | EM CALO | HAD CALO | MUON Track | MUON Trigger
ATLAS | GOSSIP/ InGrid | GOSSIP/ InGrid |  |  |  | Micromegas | Micromegas
CMS |  |  |  |  |  | GEM | GEM
ALICE |  | TPC (GEM) | VHPMID (CsI-THGEM) |  |  |  | 
Linear Collider |  | TPC(MM,GEM, InGrid) |  |  | DHCAL (MM,GEM, THGEM) |  | 
Ongoing R&D Projects using MPGDs in the framework of HEP Experiments
ATLAS Micromegas:
On a road to large-area detectors:
(1.2 * 0.6 m2)
CMS GEM:
Trapezoidal GEM Prototype (99 x 45-22 cm2)

## Slide 37
GEMs for the CMS Muon System Upgrade:
R&D Started in 2009 within the RD51 collaboration:
Single-mask GEM technology (instead of double-mask)
 Reduces cost /allows production of large-area GEM
Self-stretching technique: assembly time reduction
from 3 days  2 hours
MM for the ATLAS Muon System Upgrade:
R&D Started in 2007 within the RD51 collaboration:
Standard Bulk MM suffers from limited efficiency at
high rates due to discharges induced dead time:
ATLAS small wheels upgrade project resistive MicroMegas prototype ( ~ 1 m2)
During LS2, a New Small Wheel containing
~ 1000 m2 of resistive MM will be installed in
ATLAS  the largest MM system, ever built
FOSTER INDUSTRIAL PRODUCTION NEEDS
MPGDs: Technology Developments Highlights
During the LHC End-Year stop of 2016/2017, two GEM super-chamber demonstrators will be installed

## Slide 38
MPGD-Based Readout for ALICE TPC Upgrade
Energy resolution vs IBF (4-GEM detector):
ALICE TPC Upgrade
 replace MWPC with GEM
Continuous TPC readout at 50 kHz
Physics requirement: IBF < 1%, energy:
s(E)E < 12% achieved
TDR Baseline Solution: 4-GEM Stack
Also option under study: Micromegas + 2 GEM
4 GEM Stack
engineering design
4 GEM Stack Configuration
(to minimize IBF)
Special ALICE TPC / RD51 workshop
during the RD51 Collab. Week in June 2014:
http://indico.cern.ch/event/323839/other-view?view=standard

## Slide 39
MPGD-based Readout for ILC TPC
Diameter 77cm
Large TPC Prototype with versatile endplate @ DESY
Efforts to improve the modules design for all technologies. Several test beams campaigns:
7 Micromegas modules with 2-phase C02 cooling
With beam and laser dots:
UV laser gererates MIP tracks
& illuminate calibration spots
2P CO2
Cooling
MM (B=0): Before correction
Goal for final TPC can be reached:
GEM / MM performance similar
MM (B=0): After correction
(note – different scale)

## Slide 40
MPGD-Based Gaseous Photomultipliers (GPM)
Multi-GEM Gaseous Photomultipliers:
Largely reduced photon feedback
(can operate in pure noble gas & CF4)
Fast signals [ns]  good timing
Excellent localization response
Able to operate at cryogenic T
CsI ~ 500 A
Semitransparent
Photocathode (PC)
CF4
770 torr
3 GEM
s = 1.6 ns
Single Photon Time Resolution:
CsI ~2500 A
Reflective
Photocathode (PC)
200 µm
FWHM ~160 µm
Beam ~ 100 µm
Intrinsic accuracy
s (RMS) ~ 55 µm
Single Photon Position Accuracy:
E.Nappi, NIMA471 (2001) 18; T. Meinschad et al, NIM A535 (2004) 324; D.Mormann et al., NIMA504 (2003) 93
Micromegas: s ~ 0.7 ns with MIPs
GEM Gaseous Photomultipliers (GEM+CsI photocathode) to detect single photoelectrons

## Slide 41
COMPASS RICH: Long-Term Experience, Performance and Upgrades
PMTs not adequate because of large angular acceptance  only small demagnification
factor of optical system allowed (large distortions); 5 m2 of PMTs not affordable.
COMPASS RICH I:
UPGRADE OF COMPASS RICH I:
1999-2000: 8 MWPC with CsI (RD26 @ CERN)
After a long-term fight for increasing electrical stability
at high rates: robust operation is not possible at gain~105 because of photon feedback, space charge & sparks
MPGD-Photon Detectors are the best option
beam off: stable
operation up to > 2300 V
beam on: stable operation
possible only up to ~2000 V
2006: 4 central CsI+cathodes:
remove and insert frames with
MAPMTs and lense telescopes
PMTs not adequate  only small demagnification
factor allowed; 5 m2 of PMTs not affordable.
 Micromegas +THGEM, the hybrid architecture
structure, is one of the most advanced scheme:
Higher performance reached with the MM + THGEM
architecture (than multiple-THGEM structures)

## Slide 42
A.Buzulutskov et al, IEEE TNS 50 (2003) 2491;
A.Bondar et al, NIMA 524 (2004) 130
A.Bondar et al, NIMA 556 (2006) 273
A.Rubbia, J. Phys. Conf. Ser. 39 (2006) 129
A.Buzulutskov, A.Bondar, JINST 1 (2006) P08006
Y.L.Ju et al, Cryogenics 47 (2007) 81
A. Bondar et al, JINST 5 (2010) P08002
A.Buzulutskov et al, EPL 94 (2011) 52001
L.Periale et al, IEEE TNS 52 (2005) 927
M.Gai et al, Eprint arxiv:0706.1106 (2007)
D.Akimov et al, JINST 4 (2009) P06010
A.Bondar et al, JINST 3 (2008) P07001
P.K.Lightfoot et al, JINST 4 (2009) P04002
N.McConkey et al, IPRD 2010, Siena, Italy; Nucl. Phys. B Proc. Suppl. 215 (2011) 255
D.Akimov, NIMA 628 (2011) 50
S. Duval et al, JINST 6 (2011) P04007
S. Duval et al, JINST 4 (2009) P12008
MPGD-Based Cryogenic Avalanche Detectors: Concept Gallery

## Slide 43
Advancing Concepts: Double Phase Ar LEM/TPC for Neutrino Physics
Double-phase Ar LEM TPC

## Slide 44
Focus on providing techniques for calculating electron transport in small-scale structures
The main difference with traditional gas-based detectors is that the electrode scale
(~ 10 mm) is comparable to the collision mean free path
Development and Maintenance of Garfield++: Garfield++ is a collection of classes for the detailed simulation of small-scale detectors.
Garfield++ contains: - electron and photon transport using cross sections provided by Magboltz - ionisation processes in gases, provided by Heed and MIP - ionisation and electron transport in semi-conductors - field calculations from finite elements, boundary elements, analytic methods Simulation Improvements:
 Transport:
- ion mobility and diffusion, measurement and modelling
- Magboltz cross sections (Ar, Xe, He, Ne; GeH4, SiH4, C2H2F4 ) are frequently
updated in collaboration with LXCAT (http://www.lxcat.laplace.univ-tlse.fr)
- e-ion recombination process in Xe
- thermal motion
 Photons:
- update in UV emission
- inclusion of IR production
- photon trapping and resulting excitation transport
- photon absorption in the gas (gas feedback)
- photon absorption in and electron emission from walls (feedback)
- photo cathodes
Development of MPGD Simulation Tools

## Slide 45
Development of MPGD Simulation Tools
Applications:
GEM: multiplication process and polyimide properties; charging up effects
MicroMegas: timing and effects of resistive layers
TPC GEM: ion backflow
 ALICE TPC end-cap upgrade studies: rate dependence of the Ion Back Flow in GEM
Summary of simulation improvements in 2013:
Systematic calculations of GEM charging-up as function of hole shape; these reproduce the trends observed in experimental data
Measurements in Krakow for numerous gas mixtures of energy transfer rates which permit much more accurate avalanche gain calculations
Start of a collaboration with Coimbra on ion transport measurements in mixtures and start of an effort to model ion transport microscopically, which will help to predict charging-up and ion feedback
Measurement in Orsay at particularly low gain and low noise of the avalanche fluctuations in He/iso, Ne/iso and Ar/isobutane (these fluctuations are reproduced by MC run)
Measurement
Simulation

## Slide 46
Advancing MPGD Concepts for Future Projects
Tracking
TPC readout
UV photon detection
Neutron detection
Applications :
HEP and Nuclear Physics
Neutrino Experiments
Dark Matter
Ground-based Astroparticle
Space Experiments
Spin-off outside HEP field
(some) experimental requirements:
HL-LHC (LHC luminosity upgrade)
 radiation, pileup, backgrounds
ILC
 high precision, hermeticity
Neutrino Facilities
 sensitivity (mass, size), efficiency, purity
Dark Matter
 purity, low bkg, large sensitive areas

## Slide 47
MPGD
Cosmic Ray Muon Tomography
Using GEMs for Homeland security
Spin off is important key word for the HEP labs to survive …
T2DM2: Temporal Tomography
Densitometric by the Measure of Muons
Liquid xenon detectors for functional medical imaging
Technology
CsI-RETGEM for UV
flame detection

## Slide 48
Wire Chambers, TPC, RPC  MPGD (GEM, Micromegas)  InGrid (3D)
Micromegas:
Ingrid
TODAY:
FUTURE:
YESTERDAY:
INTEGRATION
INTEGRATION
Advances in photolithography 
Large Area MPGDs (~ m2 unit size)
High rate capability ~106 Hz/mm2
Spatial res. ~ 30-50 mm (TRACKING)
Time res. ~ 3-5 ns (TRIGGER)
LHC
HL-LHC
ILC
ILC
CLIC
Gaseous Tracking: Detector-Electronics Integration Trends

## Slide 49
Science for Piece
CERN: 60 Years

## Slide 50
50
CERN – European Center for Nuclear Research
was founded in 1954:
12 European States “Science for Peace”
Today: 21 Member States
Member States: Austria, Belgium, Bulgaria, the Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Israel, Italy, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland and the United Kingdom
Candidate for Accession: Romania
Associate Member in Pre-Stage to Membership: Serbia
Applicant States for Membership or Associate Membership: Brazil, Cyprus, Pakistan, Russia, Slovenia, Turkey, Ukraine
Observers to Council: India, Japan, Russia, Turkey, United States of America; European Commission and UNESCO
~ 2300 staff
~ 1600 other paid personnel
~ 10500 users
Budget (2014) ~1000 MCHF

## Slide 51
CERN: 60 Years Science for Piece
“Physique-sans-Frontières” (PSF) was born in 1992, during the war in Bosnia when many scientists felt the necessity to "do something" for their colleagues of South East of Europe
Georges CHARPAK has kindly accepted to preside "Physics-without-Borders” and supported the effort of the association to set up the “Four-Seas-Conference”
The 1st Trieste-95 conference was a real success, despite the renewed war in Bosnia : 150 physicists, half of them from the South-Eastern Europe; all the countries of the Balkanic area were represented, despite the existing state of war between some of them
Four Seas Conference: « Physique-sans-Frontières »

## Slide 52
Four Seas Conference: Physics in Service of Mankind
Five conferences were organized (Trieste-95, Sarajevo-98, Thessaloniki-02, Istanbul-04, Iasi, Romania-07) to give opportunity for scientists, mainly the youngest ones, to hear about the most recent developments in sciences and technologies
Served as a way to express the solidarity of the scientific community with all those who, under difficult conditions, seek to keep alive the diverse intellectual and cultural links that constitute the essence of our civilization
2014: CERN is celebrating
“60 Years of Science for Peace!”

## Slide 53
Four Seas Conference: Physics in Service of Mankind
Five conferences were organized (Trieste-95, Sarajevo-98, Thessaloniki-02, Istanbul-04, Iasi, Romania-07) to give opportunity for scientists, mainly the youngest ones, to hear about the most recent developments in sciences and technologies
Served as a way to express the solidarity of the scientific community with all those who, under difficult conditions, seek to keep alive the diverse intellectual and cultural links that constitute the essence of our civilization
2014: CERN is celebrating
“60 Years of Science for Peace!”

## Slide 54
In 2014, CERN is celebrating “60
Years of Science for Peace”!
In a particularly fragile time for
Ukraine, physicists from France,
Ukraine, Poland and CERN get
together in Lviv, Ukraine in memory of Georges Charpak personality, continuing his scientific and cultural traditions.
Slides are available at:
https://indico.cern.ch/event/
331478/timetable/#20140721
A conference: “90th Anniversary
of Georges Charpak“
Bringing Nations Together
Through Science:
CERN Courrier, November 2014

## Slide 55
CERN: Bringing Nations Together Through Science
Global Science: go beyond the national interests
Power of Science: improve life of people via development of novel technologies (multinational community – competition and collaboration) providing unique scientific environment
Science Diplomacy: in a world which is exceedingly fragile today, science diplomacy opens the possibility to tackle global challenges, ensures cultural exchange of different nations
CERN is of a Global Influence (“Virtual Nation”)  work peacefully together at the frontiers of research and disseminate results as widely as possible
Science requires a long-term thinking and long-term planning  often underestimated by politicians' in a view of the short-term economical goals
TODAY, SCIENCE IS GETTING MORE AND MORE GLOBAL