## Slide 1
Micropattern Gas Detectors Technologies
and
RD51 Collaboration
Paul Colas and Leszek Ropelewski
CEA Saclay and CERN PH DT DD
RD51 Collaboration Site
OUTLINE:
Overview of MPGD Technologies
RD51 Collaboration Activities
Technology Achievements
Detector Assembly Optimization, QA, Long Term Stability
Electronics for MPGDs
Software tools
MPGD workshop upgrade & industrialization
Lab and test beam facilities
Training and Outreach

## Slide 2
Gaseous Detectors
Electrons liberated by ionization drift towards
the anode wire.
Electrical field close to the wire (typical wire Ø
~few tens of mm) is sufficiently high for electrons
(above 10 kV/cm) to gain enough energy to ionize
further → avalanche – exponential increase of
number of electron ion pairs.
The influence of (slower) ions on a conductor
generates a current in a pre-amplifier
The cylindrical geometry is not the only one to generate a strong electric field:
parallel plate
strip
hole
groove/well
mwpc
wire
Best way to make detectors on large volumes with little matter and at low cost

## Slide 3
Printed Circuit Board (PCB) technology allowed micro-structures to be patterned
In the 1990s
Photolithography
Etching
Coating
And later silicon wafer post-processing allowed to go further in small patterns
Micro-Pattern Gas Detectors
Operational instabilities:
Substrate charging-up
Discharges
Polymer deposition (ageing)
Rate Capability>106/mm2
Position Resolution ~40mm
2-track Resolution ~400mm
MWPC
MSGC
Amplifying cell
size reduction by
factor of 10

## Slide 4
Micro-Pattern Gas Detectors
Electrons
Ions
60 %
40 %
Micromegas
GEM
THGEM
MHSP
Ingrid
4
High Rate Capability
High Gas Gain
Good Space, Time and Energy Resolution
Good Ageing Properties
Ion Backflow and Photon Feedback Reduction
Large Size
Low Cost
Rate Capability Comparison for MWPC and MSGC

## Slide 5
MSGC – MicroStrip Gas Chamber
Thin metal strips on insulating support replace the wires
200 mm
However
High discharge probability under exposure to highly ionizing particles caused by the regions of very high E field on the border between conductor and insulator.
Charging up of the insulator and modification
of the E field → time evolution of the gain.
insulating support
slightly conductive support
Solutions:
slightly conductive support
multistage amplification
R. Bellazzini et al.
Anton Oed

## Slide 6
Surface charging
Bulk resistivity of the support material
Surface modification by doping or deposition
Discharges
High gain is at the cost of instability
LETHAL DAMAGES
MSGC – MicroStrip Gas Chamber

## Slide 7
Advanced passivation
Standard passivation
Cathode edge passivation
Bellazzini et al.
MSGC – MicroStrip Gas Chamber

## Slide 8
Spatial resolution = 34.5 ± 0.4 mm
2-track resolution ~400 mm
Ne(25)-DME(75)
Vcath= -530 V
Vdrift= -3000 V
Rate capability > 1 MHz/mm2
Energy resolution ~11% for 5.9 keV
Single event wire map
Surface resistivity !!
MSGC – MicroStrip Gas Chamber

## Slide 9
Telescope of 32 MSGCs tested at PSI in Nov99 (CMS Milestone)
HERA-B Inner Tracker
MSGC-GEM detectors
Rmin ~ 6 cm
 106 particles/cm2•sec
300 mm pitch
184 chambers: max 25x25 cm2
~ 10 m2; 140.000 channels
The D20 diffractometer MSGC
is working since Sept 2000
1D localisation
48 MSGC plates (8 cm x 15 cm)
Substrate: Schott S8900
Angular coverage : 160° x 5,8°
Position resolution : 2.57 mm ( 0,1°)
5 cm gap; 1.2 bar CF4 + 2.8 bars 3He
Efficiency 60% @ 0.8 Å
DIRAC
4 planes MSGC-GEM
Planes 10x10 cm2
MSGC – MicroStrip Gas Chamber

## Slide 10
MSGC – MicroStrip Gas Chamber
2D resistive MSGC
V. Peskov

## Slide 11
Micromegas – Micromesh Gaseous Structure
Micromesh mounted above readout
structure (strips or pads).
E field similar to parallel plate detector.
Ea/Ei ~ 50-500 to secure electron transparency
and positive ion flow back suppression.
100 mm
Ei
Ea
Y.Giomataris et al, NIM A 376 (1996) 29
Ioannis Giomataris

## Slide 12
D.Thers et al NIM A 469 (2001) 133
energy resolution ~ 10%
55 Fe
Ar + 10% C4H10
High voltage [V]
350
450
400
500
550
600
650
103
102
104
105
105
gain
gain
ageing:Ar-iC4H10 94-6% up to 24.3mC/mm2
10 years LHC
1
0.8
0.6
0.4
0.2
1.8*1012 particles/mm2
1
0.9
0.8
0.7
0.6
10-4
10-5
10-6
10-7
10-8
discharge probability
efficiency
efficiency & discharge probability
High Voltage [V]
Micromegas – Micromesh Gaseous Structure
1000 10000 20000 30000 time[min]

## Slide 13
300mm
420 V operating point
~3-4.103 Gain
s = 9 ns
s =70 µm
Large efficiency plateau > 40 V
Spatial resolution < 70 µm
Time resolution : 9 ns
D.Thers et al NIM A 469 (2001) 133
Micromegas – Micromesh Gaseous Structure

## Slide 14
Pixelized Micromegas
D. Neyret
Micromegas – Micromesh Gaseous Structure
COMPASS Micromegas
P. Rebourgeard, F. Kunne

## Slide 15
PCB
lamination
Mesh deposit
lamination
development
Bulk Micromegas technology
15
Fine segmentation 1cm², thickness 8mm for ILC Hadronic calorimetry
Tested in the RD51 1 kHz beam
Bulk Micromegas ILC DHCAL first m2
LAPP Annecy
Y. Giomataris
R. de Oliveira
M. Chefdeville

## Slide 16
T2K TPC, A. Delbart, M. Zito
24 bulk-Micromegas
3 m2 of bulk Micromegas
41472 FEE channels
Reconstructed cosmics
by a readout plane
Micromegas – Micromesh Gaseous Structure

## Slide 17
Micromegas ILC-TPC,
D. Attie, P. Colas
Micromegas – Micromesh Gaseous Structure
Red – thick
Micromegas
Blue – thin curved
Micromegas
Curved Micromegas CLAS12,
S. Aune

## Slide 18
Micro-Bulk Micromegas
Th. Papaevangelou
Readout plane + mesh all in one
Micromesh
5µm copper
Kapton 50 µm
Readout pads
An I. Giomataris and R. De Oliveira idea
Lower capacitance
Under development
Low background Micromegas,
J. Galan, E. Ferrer, A. Tomas
55Fe Calibration with Ar – 5% isobutane @ 1 bar
Collimated source to avoid border effects
FWHM @ 6 keV = 11.5 %
Micro-Bulk Micromegas

## Slide 19: MicroMegas detectors for the upgrade of the ATLAS muon system
Goal: development of large-area (≈2 x 1 m2) bulk-MicroMegas chambers for high-rate applications that combine precision measurement and trigger functionality
MAMMA Collaboration (21 institutes, including Arizona, Athens, BNL, CEA Saclay, CERN, Naples) in close collaboration with CERN/TE-MPE (R. de Oliveira) & CERN/PH-DT
Spark neutralization and/or suppression
  Resistive coating on readout strips
  Multi-stage amplification schemes
Underlying philosophy:
  Development and evaluation of full-size prototype chambers at CERN and in the collaborating institutes
  Transfer of know-how to competent industry
  Large-scale production in industry
1.2 x 0.6 m2 prototype chamber with 2048 readout strips (0.5 mm strip pitch) during construction in CERN/TE-MPE workshop
March 2011
J. Wotschack

## Slide 20
J. Wotschack
R. De Oliveira

## Slide 21: MM Resistive strip protection
Double sided Board
Res-strip depositing
Coverlay technique
Bulking
Test
Test before closing
Closing
R. De Oliveira

## Slide 22
MM Resistive strip protection
J. Wotschack

## Slide 23
X/Y read-out
U/V/X read-out
Bulk MicroMegas resistive anode and 2D readout
R. De Oliveira

## Slide 24
CAT – Compteur à trous
An insulator with holes is metalized both sides. A high potential difference is held between the two
sides. Avalanches take place after the holes.
This is the ancestor of GEMs. According to F. Sauli, this is not a MPGD (but in this case, is THGEM a MPGD?
(Bartol et al., 1996 ; J. Chaplain et al., 1999)
Lemonnier

## Slide 25
GEM – Gas Electron Multiplier
Induction gap
e-
e-
I+
70 µm
55 µm
5 µm
50 µm
Thin, metal coated polyimide foil perforated
with high density holes.
Electrons are collected on patterned readout board.
A fast signal can be detected on the lower GEM electrode
for triggering or energy discrimination.
All readout electrodes are at ground potential.
Positive ions partially collected on the GEM electrodes.
Electrons
Ions
60 %
40 %
Fabio Sauli

## Slide 26
GEM – Gas Electron Multiplier
A. Bressan et al, Nucl. Instr. and Meth. A425(1999)254
Full decoupling of the charge amplification
structure from the charge collection and
readout structure.
Both structures can be optimized
independently !
Compass
Totem
Most of the detectors use three GEM foils in cascade for amplification
to reduce discharge probability by reducing field strength.
Cartesian
Compass, LHCb
Small angle
Hexaboard, pads
MICE
Mixed
Totem

## Slide 27
Multi-GEM Detectors
Discharge Probability on Exposure to 5 MeV Alphas
Multiple structures provide equal gain at lower voltage.
Discharge probability on exposure to a particles is strongly reduced.
S. Bachmann et al Nucl. Instr. and Meth. A479(2002)294

## Slide 28
Efficiency for minimum ionizing particles with 3 mm gap
Space resolution ~ 40 mm rms
Cluster size ~ 500 mm FWHM
A. Bressan et al, Nucl. Instr. And Meth. A425(1999)262
Rate capability > 106 Hz mm-2
GAIN ~ 104
Ar-CO2 70-30
C. Altunbas et al, DESY Aging Workshop (Nov. 2001) Nucl. Instr. and Meth. A
1 mC~2.1010 min.ion. particles
J. Benlloch et al, IEEE NS-45(1998)234
3.106 particles/mm2
GEM – Gas Electron Multiplier

## Slide 29
GEM – Gas Electron Multiplier
4.5 ns
4.8 ns
5.3 ns
9.7 ns
Time resolution
Charge correlation (Cartesian readout)

## Slide 30
COMPASS
B. Ketzer
Pixel GEM
B. Ketzer
GEM – Gas Electron Multiplier

## Slide 31: LHCb Muon Trigger
Fast TripleGEM Detectors for LHCb Muon Trigger
12 double TGEM detectors operated with fast gas mixture (Ar-CO2-CF4)
Rate - 5 kHz mm-2
Time resolution 4.5 ns rms
Radiation hard up to integrated charge of 20 mC mm-2 (15 LHCb years)
M. Alfonsi et al, Nucl. Instr. and Meth. A535(2004)319
Pad readout plane
20x24 cm2 GEM modules
G. Bencivenni

## Slide 32
3 mm
2 mm
2 mm
2 mm
Cathode
GEM 1
GEM 2
GEM 3
Anode
Read-out
Conversion & Drift
Transfer 1
Transfer 2
Induction
TOTEM GEMs, T. Hilden, V. Greco
GEM
Chamber
Horse Shoe
Card
VFAT Hybrids
11thCard
Electronics cooling
HV cables
Coincidence
Chips
KLOE2 - Cylindrical Triple GEM
G. Bencivenni
GEM – Gas Electron Multiplier
S. Duarte Pinto

## Slide 33
50 mm Polyimide
25 mm Polyimide
125 mm FR4
15 mm Cu
Epoxy glue
5 mm Cu
10 mm Cu
Epoxy glue
Ni Au
15 mm Cu
2004 prototype
radial strips
pads
bonding contact
for pads
TOTEM GEM - Readout Board

## Slide 34
GEM ILC HCAL, A. White
GEM ILC TPC,
T. Behnke, T. Matsuda
A. Sugiyami
GEM – Gas Electron Multiplier

## Slide 35
Base material : Polyimide 50um + 5um on both sides
Polyimide : Apical NP from company Kaneka (Japan)
Supplier of the copper clad material : Nippon Mining (Japan)
Single Mask GEM
Same base material
Hole patterning in Cu
Polyimide etch
Bottom electro etch
Second Polyimide Etch
Limited to 40cm x 40cm due to
Mask precision and alignment
Limited to 2m x 60cm due to
Base material
Equipment
Double mask
Single mask
R. De Oliveira

## Slide 36
Similar patterns , similar behavior, same material.
Angles can be adjusted in both structure (Typ. value : 70um copper hole , 50um polyimide hole)
  Steeper angles give lower gain but also reduced charging up ( similar as RIM in THGEM)
Single Mask GEM
R. De Oliveira

## Slide 37
37
Second Polyimide etching
Chemical Polyimide etching
Copper electro etching
Stripping
Result
Single mask GEM technology
Large area GEM detectors for KLOE2 tracker
Frascati
KLOE2 - Cylindrical Triple GEM
G. Bencivenni

## Slide 38
38
CMS High Eta MPGD Project (GE1/1 1.6>h>2.1)
CMS High Eta MPGD - Workshop (30 September 2010)
15 institutes, 60 participants
Large Prototype: GE1/1
Beam Test @ RD51 setup
October 2010
Rate capability : 104/mm2
Space/Time resolution: ~ 100 m / ~ 4-5 ns
Efficiency > 98% ; Excellent Long Term Operation
Gas Mixture: Argon CO2 (non flammable mixture)
Large areas ~ 1m x 2m with industrial processes
A. Sharma

## Slide 39
39
  Time resolution for different
  gas mixtures and gap configurations:
  Ar(45):CO2 (15):CF4 (40)
  [gaps 3/1/2/1]
  Ar(70):CO2(30)
  [gaps 3/2/2/2]
CMS High Eta MPGD Project
A. Sharma

## Slide 40
PCB tech - etching + drilling
Simple and robust
VTGEM~2KV (at atmospheric pressure)
105 gain in single- & 107 double-TGEM
Sub-mm to mm special resolution
Fast (ns)
Low pressure (<1Torr) gain 104
Microlithography + etching
High Spatial resolution (tens of microns); VGEM~400V
>103 gain in single GEM
106 gain in cascaded GEMs
Fast (ns)
Low pressure – gain~30
1mm
THGEM
1mm
Standard GEM
V. Peskov, A. Breskin …
THGEM – Thick GEM
(called LEM in Switzerland)
Thick GEM
A. Breskin

## Slide 41
THGEM – Thick GEM
Thick GEM
A. Breskin

## Slide 42
Mask etching + drilling; rim = 0.1mm
6 keV X-ray
104
pitch = 1 mm; diameter = 0.5 mm;
rim=40; 60; 80; 100; 120 mm
Drilling + chemical rim etching without mask
Thick GEM
A. Breskin
THGEM – Thick GEM – the role of the rim

## Slide 43
anode
drift
THGEM 1
THGEM 2
Etransfer
2.0 mm
2.0 mm
CsI
THGEM 3
2.0 mm
Thick GEM
S. Dalla Torre
F. Tessaroto
RET-thick GEM
R. Akimoto
V. Peskov
THGEM – Thick GEM / RetGEM Resistive Thick GEM
Gain increase → stability gets worsen.
At first few hours, gain drops down.
After that, the fluctuation of gain is within ±4%.
Notes: 43

## Slide 44
44
89 institutes
~ 500 people involved
Representation (Europe, North America, Asia, South America, Africa)
RD51 Collaboration
“RD51 aims at facilitating the development of advanced gas-avalanche detector technologies and associated electronic-readout systems, for applications in basic and applied research”
The main objective of the R&D programme is to advance technological development of Micropattern Gas Detectors
RD51 contributes to the LHC upgrades, BUT, the most important is:
RD51 serves as an access point to
MPGD “know-how” for the world-wide community
Kobe, Japan, September 2011
http://gifna.unizar.es/mpgd13/
http://rd51-public.web.cern.ch/rd51-public/

## Slide 45
RD51
Large Area Detectors
Assembly Optimization
RD51 Common Projects
Generic R&D
Long Term Stability
Software Tools and
Simulations
MPGD Electronics
CERN MPGD Workshop
Quality Control
and Industrialization
RD51 Common
Test Beam and Lab Facilities
WG5:
WG4:
WG1:
WG2:
WG7:
WG6:
RD51 Collaboration
Conferences, Meetings and Schools

## Slide 46
Technology Development Highlights
GEM Single Mask Technique
Second Polyimide etching
Chemical Polyimide etching
Copper electro etching
Stripping
Result
Electrons
Ions
60 %
40 %
GEM Single Mask Process
Standard double mask method limits max. size of the detector to 30x30 cm2
Single mask technique reduces costs and production time
Performance comparison (max. gain, stability, rate capability..) shows no difference
46
CMS high eta upgrade triple GEM prototype in the RD51 test beam facility
ALICE triple GEM TPC end-cap module
Time resolution
4 ns
KLOE2 inner tracker: 4 layers of triple cylindrical GEM detectors

## Slide 47
Technology Development Highlights
Resistive MicroMegas
PCB
Lamination
Mesh deposit
Lamination
Development
Bulk MicroMegas Process
Standard Bulk MicroMegas suffers from limited efficiency at high rates due to discharges induced dead time
47
ATLAS small wheels upgrade project
resistive MicroMegas prototype

## Slide 48
Technology Development Highlights
THGEM Surface Treatment
Polyurethane Treatment
Polishing and Cleaning
Non-treated THGEM suffers from: limited max. gain, response non-uniformity and time instabilities
48
COMPASS RICH photo-detector upgrade prototype

## Slide 49
Detector Assembly Optimization
Industrialization and Cost Reduction
Simplified Bulk MicroMegas & GEM NS2
49
ATLAS muon system MicroMegas upgrade assembly
CMS high eta project triple GEM detector assembled using self-stretching method

## Slide 50
Quality Control
Electrical rigidity
Hole diameter uniformity in GEM
Gap uniformity in MicroMegas
THGEM thickness uniformity
Final detector calibration and characterization protocols and infrastructure
50

## Slide 51
Long Term Stability
Classical gas detectors ageing detector
Radiation hardness and activation of detector components
Sustainability to neutrons and heavily ionizing particles induced discharges
Exposure to X-Ray, Gamma, Neutron and Alpha Sources
Monitoring infrastructure
Resistive MicroMegas stability performance under X-Ray irradiation
Discharge studies of the triple GEM detector exposed to the low energy neutron flux
Portable gas monitoring system for detector stability studies; to be used by LHCb and CMS upgrade of the muon system

## Slide 52
New Developments Examples
Piggy Back, Light Beam Monitors, Glass GEM
52
Piggy Back – a novel method of the readout of the MPGD detectors using pixel chips; Electronics is completely separated from the detector volume
Light ( 0.4 % X0 ) 2D GEM detector for low energy antiproton beam monitoring
Glass GEM for sealed photon large area detector

## Slide 53
Physical Overview of SRS:
Scalability from small to large system
Common interface for replacing the chip
frontend
Integration of proven and commercial
solutions for a minimum of development
Default availability of a very robust and
supported DAQ software package
Development of a portable multi-channel readout system (2009-2012):
Scalable readout architecture: a few hundreds channels up to very large LHC systems (> 100 k ch.)
Project specific part (ASIC) + common acquisition hardware and software
Frontend hybrids:
based on
APV25, VFAT, Beetle, VMMx and Timepix chips
FEC cards (common):
Virtex-5 FPGA, Gb-Ethernet, DDR buffer, NIM and LVDS pulse I/O, High speed Interface connectors to frontend adapter cards
ADC frontend adapter
for APV and Beetle chips
ADC plugs into FEC to make a
6U readout unit for up to 2048
channels
Development of Scalable Readout System (SRS) for MPGDs
53

## Slide 54
ALICE EMCal Calorimeter upgrade, ORNL, SRS readout backend via DTCC links and 24 SRU’s , DATE Online system, being installed
ATLAS upgrade CERN, MAMMA project NSW , µMEGAS , APV frontend SRS Eurocrates-SRU, MMDAQ Online, installed
ATLAS upgrade Mainz, µMEGAS for MBTS, APV frontend- SRS Eurocrate, MMDAQ Online, waiting delivery
ATLAS Muon upgrade R&D, INFN Rome, APV frontend SRS Eurocrate, MMDAQ Online, delivered
ATLAS Saclay, µMEGAS R&D, APV frontend SRS Minicrate, MMDAQ Online, delivered
NA62 CERN straw tracker upgrade with µMEGAS, APV frontend with SRS Minicrate, MMDAQ Online, delivered
CMS upgrade CMS GEM collaboration CERN, Muon Endcaps, design of VFAT frontend digital readout SRS, ongoing with IFIN-HH
TOTEM upgrade GEMs Baris testlab, OPTO-Rx card design, Minicrate,Eurocrate, SRU, DATE Online, delivered
BNL GEM detectors, APV frontend-SRS Minicrate, RCDAQ Online, delivered
Stony Brook GEM detector R&D, APV frontend SRS Minicrate, RCDAQ Online, delivered
Bonn Phys. Inst. R&D for ILC, T24 DESY testbeam, Timepix Array Ingrid Module adapter for SRS , Eurocrate, Online unknown, ongoing
Florida Inst Tech GEMs, Muon Tomografy for Homeland security, 15k channel SRS prototype Eurocrate, DATE Online, delivered
Géosciences Azur-CNRS-UNSA, Muon Tomography w.µMEGAS for geology, APV frontend SRS Eurocrate, Date Online, delivered
GDD lab RD51, CERN, R&D for GEM and µMEGAS, APV frontend SRS Euro and Minicrates, DATE, Labview MMDAQ, delivered
HIP, HELSINKI, characterization MPGAD detactors, APV frontend SRS Eurocrate, DATE and Labview, delivered
INFN Napoli, ATLAS. Development of SRS Hardware and Firmware, Labview, delivered
Jefferson Lab, Virginia UVa upgrade GEM readout system, APV frontend SRS Eurocrate, DATE online, partially delivered
Yale University , GEM development ALICE, APV frontend SRS Eurocrate, DATE Online, delivered
NEXT Coll. small Xenon TPC with PM and Si PMs, SRS readout electronics co-development, SRS Eurocrate and SRU, DATE, delivered
UNAM, MEXICO, MX , R&D on THGEM, APV frontend SRS Minicrate, DATE Online, delivered
Radiation Laboratory, Nishina Center, RIKEN , APV frontend SRS Eurocrate, Online unknown, delivered
J-PARC /E16 experiment, GEM based tracking, APV frontend SRS Minicrate, Online Unknown, partially delivered
Jefferson Lab SHM spectrometer triple GEM, APV frontend SRS Eurocrate, DATE Online, waiting
Harward Univ. Physics, APV frontend SRS Minicrate, Online unknown, waiting
Tokyo Univ. ATLAS, APV frontend SRS Eurocrate, Online unknown, waiting
WIS and Aveiro Univ. GEM validation, APV Frontend SRS Eurocrate, MMDAQ and Labview, being delivered
East Carolina University, Health Physics, APV frontend, SRS Eurocrate, Labview, waiting
Munich LMU / ATLAS µMEGAS, APV frontend SRS Eurocrate –SRU, MMDAQ Online, partially delivered
NCSR Democritos ATHENS, APV frontend SRS Minicrate, Online unknown, waiting
IFIN-HH-Bucharest new Detector lab, APV and VFAT frontend, SRS Eurocrate and SRU, Labview, delivered
ATLAS NSW CERN, SRS-ATCA pilot system, MMDAQ Online, waiting
ALICE FOCAL ORNL, SRS-ATCA pilot system, DATE Online, waiting
NEXT Collaboration, SRS-ATCA pilot system, DATE Online, waiting
Lunds Univ, ILC TPC, SRU for 24 channel DTCC link readout, Online unknown, delivered
Produced by PRISMA Company (Greece), sold via the CERN store
SRS Users Status
54

## Slide 55
LAPP, Annecy, SRS hybrid with MicroROC chip for ATLAS , no news
Pacific Northwest National Laboratory, Radiation detection and Nucl. Sci, interest in APV SRS system, no CERN team account
Radcore LTD Republic of Korea, GEM production , small SRS system , no team account
Newflex GEM production, South Korea , small SRS system , enquiry status
GIF++ team CERN, interested in SRS as GIF++ base installation with DATE Online system , ongoing discussions, waiting
Budker INP, Novosibirsk, Deuteron Exp. @ VEPP-3 , APV readout SRS , APV order impossible, radhard export restriction
Tsinghua Univ. China , R&D on GEM Imaging detectors, APV readout SRS , APV order impossible, radhard export restriction
SAHA Inst Nucl Phys,KOLKATA, IN , Laboratory for characterization of MPGDs , APV order impossible, radhard export restriction
USTC Shanghai, CN , characterization of GEM and MicroMega with SRS , APV order impossible, radhard export restriction
Univ . Texas, DOE proposal with 18 GEMs , no news
National Univ. of Colombia, Dosimetry for mediical appl, no team account, no news
BNL Phenix upgrade, small SRS systems already delivered , no news
Helsinki University, Totem , no news
Freiburg University, verbal enquiry for SRS system, no news
Univ Calabria It, email enquiry for SRS, no news
Uni. Kobe, JP J-PARC /E16 upgrade , large SRS system, prelim offer sent
ALICE ITS, SRS 16 ch. ADC card for test of ITS chips , enquiry
NEOHM Italy, SRS system for test of hybrid production for CERN store, sending offer
Geoazur-CNRS-UNSA, Valbonne, FR, upgrade of existing SRS uMega readout systrem, APV readout Eurocrates ,waiting for news
A main feature of SRS, apart from its scalability, portability and affordable cost
(< 2 EUR/ channel), possible choice of the frontend ASIC (APV, VFAT, Beetle, VMMx, Timepix).
System was used for R&D for upgrades in ATLAS, CMS, ALICE ECAL and for SiPM readout
Potential New SRS Users
55

## Slide 56
AVD box : Active Voltage Divider with monitoring for GEMs (under test )
Remote I2C readout of AVD and CM via SRS (in progress)
CM box: Current Monitoring range 10 pA -100 mA ( design status )
QSA frontend: quad signal amplifier 2 GHz, factor 20, for MPGD’s (tb revised)
TPB trigger pickup box: generates triggers from Meshes ( working in several places)
I-GEM: Anode current summing hybrid for GEMs (planned)
Shaper-Discriminator: SRS card 50 OHM triggers from TPB (planned )
HGM: SRS card , programmable High Voltage for mesh grounded MM ( design status)
Active Voltage Divider
for GEM’s
High Voltage Monitoring
High Voltage pAmmeter
Readout pAmmeter
Hans Muller (CERN) et al.,
Towards a Complete SRS-Lab Equipment for MPGDs
56

## Slide 57
Development and Maintenance of Garfield++: Garfield++ is a collection of classes for the detailed simulation of small-scale detectors.
Garfield++ contains: - electron and photon transport using cross sections provided by Magboltz - ionization processes in gases, provided by Heed and MIP - ionization and electron transport in semi-conductors - field calculations from finite elements, boundary elements, analytic methods Simulation Improvements:
Transport:
- ion mobility and diffusion, measurement and modeling
- ongoing update of electron cross sections
- e-ion recombination process in Xe
- thermal motion
Photons:
- update in UV emission
- inclusion of IR production
- photon trapping and resulting excitation transport
- photon absorption in the gas (gas feedback)
- photon absorption in and electron emission from walls (feedback)
- photo cathodes
Focus on providing techniques for calculating electron transport in small-scale structures
The main difference with traditional gas-based detectors is that the electrode scale (~ 10 mm) is comparable to the mean free path between collisions
MPGD Simulation Tools
57

## Slide 58
MPGD Simulation Tools
GEM Avalanche Development

## Slide 59
Applications:
TPC GEM: ion backflow
GEM: multiplication process and polyimide properties; charging up
MicroMegas: timing and effects of resistive layers
MPGD Simulation Tools
TPC Ion Back Flow
ALICE TPC end-cap upgrade studies of rate dependence of the Ion Back Flow in GEM. Left: measurement; Right: Garfield++ simulation results

## Slide 60
MPGD Simulation Tools
GEM Charging Up

## Slide 61
Currently CERN-MPGD workshop is the UNIQUE MPGD production facility
(generic R&D, detector components production, quality control)
2008 RD51 Collaboration Survey:
61
RD51– MPGD Production
Construction of the new workshop’s building
Start : beginning 2012
Upgrade of the workshop approved by CERN management (Nov. 2009):
Installation of the new infrastructure to fabricate 2x1m2 Bulk MM and 2x0.5m2 GEM
GEM:
Continuous polyimide etcher
Cu electroetch line
MicroMegas:
Large laminator
Large Cu etcher
Large UV exposure unit
Large resist developer
Large resist stripper
Large oven
Large dryer

## Slide 62
Demand for the Micro-Pattern Gas Detectors – LHC Upgrades
Atlas MM 1200 m2
CMS GEM 1000 m2
Alice GEM 130 m2
LHCb GEM 57 m2

## Slide 63
GEM Technology
Mecharonix (Korea, Seoul)
New Flex (Korea, Seoul)
Tech-ETCH (USA, Boston)
Scienergy (Japan, Tokyo)
TECHTRA (Poland, Wroclaw)
MicroMegas Technology
ELTOS S.p.A. (Italy)
TRIANGLE LABS (USA, Nevada)
SOMACIS (Italy, Castelfidarco)
ELVIA (France, CHOLET)
THGEM Technology – ELTOS S.p.A. (Italy), PRINT ELECTRONICS
63
MPGD Technology Industrialization
GEM Licenses signed by:
-Mecharonics, 21/05/2013
-TECH-Etch, 06/03/2013
-China IAE, 10/01/2012
- SciEnergy, 06/04/2009
- Techtra, 09/02/2009
- CDT, 25/08/2008
- PGE, 09/07/2007
2012-2013: Industrial test runs for GEM and MM in companies (Techtra, ELTOS, ELVIA)
2013: Two large area MMs (1*0.5 m2) are ordered in ELVIA for GEOAZUR Project (Tomography Densitometric Meas.); 4 more det. to be produced at CERN
Technology Industrialization  transfer “know-how” from CERN workshop to
Industrial partners for MASS PRODUCTION

## Slide 64
2008-2013: > 20 RD51 groups participated;
3-beam telescopes
1 Bulk MM, 1 resistive MM and 1 triple-GEM with SRS readout
DT GDD lab infrastructure
JLAB-GEM 1-period
DHCAL-THGEM 1 period
CALICE-umegas 1 period
CMS-GEM 3-periods
COMPASS-THGEM 2 periods
TOTEM-GEM 3-periods
GEM-TRT 1-period
RD51-GEM-telescope
RD51-umegas-telescope
~ 25 m
Common RD51 infrastructure: 3 beam telescopes, services, DAQ, FEE
RD51 Test Beam Facility at H4 SPS
64

## Slide 65
Gas Detectors R&D Lab

## Slide 66
Training session

## Slide 67
Dear Colleagues,
It is my pleasure to inform you that the talk “Activity of CERN and LNF Groups on Large Area GEM Detectors”, presented by Danilo Domenici (LNF-Frascati) on behalf of the RD51 Collaboration at the "Frontier Detectors for Frontier Physics - 11th Pisa Meeting on Advanced Detectors", held in Isola d'Elba, Italy, has won the "Young Scientist Award" for the "contribution to the development and test of large area planar and cylindrical Gas Electron Multiplier detectors (GEM) in view of their use for various detector upgrades at SLHC and KLOE at LNF-Frascati”. I hope that this Award will motivate even stronger our younger collaborators to devote their efforts to the MPGD developments.
Congratulations !
Leszek Ropelewski
Education & Training

## Slide 68
68
Θ
Θ
~ 1.5 cm
Cargo container
hidden &
shielded
high-Z
nuclear
material
MPGD Tracking Detector (GEMs)
Technology Transfer

## Slide 69
RD51 Future – 2014 and beyond
Continuation of the R&D support for the experiments and LHC upgrades WG1
Generic R&D (new structures, ideas, detector physics) – RD51 Common Projects WG2 Development of new structures and consolidation of the existing structures, support to ALICE TPC upgrade
Applications - organization of series of specialized workshops disseminating MPGD applications beyond fundamental physics – RD51, potential users and industry (e.g. dosimetry, neutron detection, medical physics, …) WG3https://indico.cern.ch/conferenceDisplay.py?confId=265187
Development and Maintenance of Software & Simulation Tools; basic studies & software support for the RD51 community WG4
Development and Maintenance of the SRS Electronics; An extended support for the SRS including new developments and implementations of additional features WG5
MPGD Industrialization and QA Control - GEM, MicroMegas, Thick GEM; Completion of the industrialization of main technologies WG6
Maintenance and extension of the RD51 Lab and Test-Beam Infrastructure WG7
MPGD Education and Training : organization of schools for students and newcomers & academic training NEW WG, THESE LECTURES.

## Slide 70
SPARES

## Slide 71
https://espace.cern.ch/test-RD51/RD51%20internal%20notes/Forms/AllItems.aspx
RD51 Notes: 6 in 2013
12 in 2012
17 in 2011
9 in 2010
7 in 2009
RD51 Collaboration Notes

## Slide 72
RD51 Collaboration Supported Projects
2012:
R&D on large area GEMs for the ALICE TPC upgrade (GSI/ Tokyo / UNAM)
High resolution UV scanner for MPGD applications (Wigner FCP/INFN Trieste/ INFN Bari )
Large-area THGEM detector evaluation with SRS electronics (Weizmann/Coimbra/Aveiro)
2011:
Thin and high-pitch laser-etched mesh manufacturing and bulking (Saclay / CERN / Bari)
Development of innovative resistive GEM alpha detectors for earthquakes prediction and homeland security (INFN Bari / UNAM, Mexico / INFN Padova / INFN Frascati)
MPGDs technology laboratory for training, development, fabrication, applications and innovation (Universidad Antonio Nariño, Columbia / Brookhaven National Laboratory/ Helsinki Institute of Physics / HEPTech / GSI Helmholtzzentrum)
A low mass microbulk with real XY strips structure (NCSR Demokritos / Saclay/ Laboratorio de Física Nuclear y Astropartículas, Universidad de Zaragoza / CERN )

## Slide 73
MPGD are mostly used/proposed for high-rate tracking and photodetectors
COMPASS Upgrade:
Micromegas and GEM detectors for high-rate tracking
Photon Detectors Using THGEM technology for RICH 1
KLOE2 Upgrade:
Large-area cylindrical GEMs for Inner Tracker
RHIC Upgrades:
GEM Tracking for STAR Experiment
GEM Tracking for PHENIX Experiment(+ drift micro-TPC);
development of Ring Imaging version of HBD for particle ID
Future JLAB Projects:
Thin-Curved Micromegas for JLAB/CLAS12
GEM Tracker for JLAB/Hall A High Luminosity (SBS) experiments
Future FAIR Facility:
GEM Tracker PANDA Experiment
GEM/Micromegas tracking in CBM Muon Chamber (MUCH)
Future Electron - Ion Collider Facility:
Tracking and particle ID detectors based on MPGD-technology
Demand for the Micro-Pattern Gas Detectors

## Slide 74
2x106 p/mm2
Micro-Pattern Gas Detectors Performance Summary
Rate Capability
High Gain
Space Resolution
Time Resolution
Energy Resolution
Ageing Properties
Ion Backflow Reduction
Photon Feedback Reduction
Spatial
resolution
s ~ 12 mm
Ar/CO2/CF4
(45/15/40)
rms = 4.5ns
GEM
THGEM
Micromegas
GEM
Micromegas
Micromegas
MHSP

## Slide 75
Perspectives
Tracking and triggering
TPC end cap readout
X-ray radiography
UV light detection
Parallax error free detector
Hadron blind
Neutron detection
Optical GEM
Cryogenic detectors
Two-phase detectors
High resolution detectors integrated with pixel CMOS chips
Non planar large acceptance detectors
Light detectors – mass reduction
New readout structures adopted to experimental needs
Large size detectors
Radiation hardness of assembly materials
Industrialization of the mass production
Medical applications
Single mask process
Double mask process

## Slide 76
H. Van der Graaf ,
IEEE Nucl. Sci. Symp. Conf. Rec. (Dresden, October 2008)
Integrated Micromegas and Pixel Sensor
Postprocessing of the TIMEPIX chip to build a metal mesh on insulating pillars
Cosmic track in He-iC4H10
Electron tracks from90Sr in magnetic field (0.2 T):
INGRID

## Slide 77
TIMEPIX
256x256 pixels, 55x55µm2
14x14 mm2 active area
Triple GEM TPC with Solid State Pixel Readout
J. Kaminski, RD51 Workshop, Paris (October 2008)
Bonn University ILC-TPC
Cosmic track: short Drift
Long Drift:
Field Cage 26 cm
RWTH Aachen
Pixel MPGDs

## Slide 78
Technology Development Highlights
Pixel Readout Integration
Octoboards
78
Results of the tests of the GridPix type detector with TimePix chip readout with RD51 SRS mounted in LP TPC prototype for LC TPC application

## Slide 79
Consolidation of the Collaboration and MPGD community integration ( >80 Institutes, 450 members);
Major progress in the MPGD technologies development in particular large area GEM (single mask), MicroMegas (resistive), THGEM; some picked up by experiments (including LHC upgrades);
Secured future of the MPGD technologies development through the TE MPE workshop upgrade and FP7 AIDA contribution;
Contacts with industry for large volume production, MPGD industrialization and first industrial runs;
Major improvement of the MPGD simulation software framework for small structures allowing first applications;
Development of common, scalable readout electronics (SRS) (many developers and > 50 user groups); Production (PRISMA company and availability through CERN store); Industrialization (re-design of SRS in ATCA in EISYS);
Infrastructure for common RD51 test beam and lab facilities (>20 user groups)
RD51 Achievements Highlights

## Slide 80
“Transverse organization” of MPGD activities in 7 Working Groups
80
RD51 Collaboration – Working Groups

## Slide 81
WG1: large area Micromegas, GEM; THGEM R&D; MM resistive anode readout (discharge protection); design and detector assembly optimization; large area readout electrodes and electronics interface
WG2: double phase operation, radiation tolerance, discharge protection, rate effects, single-electron response, avalanche fluctuations, photo detection with THGEM and GridPix
WG3: applications beyond HEP, industrial applications (X-ray diffraction, homeland security)
WG4: development of the software tools; microtracking; neBEM field solver, electroluminescence simulation tool, Penning transfers, GEM charging up; MM transparency and signal development, MM discharges
WG5: scalable readout system; Timepix multi-chip MPGD readout
WG6: CERN MPGD Production Facility; industrialisation; TT Network (HEPTech)
WG7: RD51 test beam facility and GDD lab
81
Consolidation around common projects: large area MPGD R&D, CERN/MPGD
production facility, common electronics developments, software tools, beam tests
RD51 Collaboration Organization
RD51 Collaboration Organization

## Slide 82
Charge pre-amplification for ionization
released in high field close to cathode
MSGC: Discharge mechanisms
Field emission from the cathode edge
Very high ionization release:
avalanche size exceeds Reather’s limit: Q ~ 107
Uncoated MSGC
Coated MSGC
Electric field strength close to support plane in MSGC
Surface resistivity modification
MSGC – MicroStrip Gas Chamber