## Slide 1
A TPC for ILC
Deb Sankar Bhattacharya
D.Attie, P.Colas, S. Ganjour,

## Slide 2
Outline
ILC and ILD
Resistive foil Micromegas
Results of beam test 2015
2 Phase CO2 cooling results

## Slide 3
General Physics goal at ILC
The 125 GeV Higgs and possibly other Higgses, can be produced at ILC by Higgs-stahlungs.
This allows an unbiased selection by Z recoils, to measure mass and all possible decay modes. Jet reconstruction also benefit from continuous tracking in a TPC.
This sets the goal resolution of 100 m per pad row.

## Slide 4
Proposed ILD
ILD
Cross section
Length of the TPC ~ 4.6 m
Diameter of the TPC ~ 3.6 m
Magnetic field ~ 3.5 T

## Slide 5
Proposed ILC-TPC

## Slide 6
What is a TPC ?
A Time projection Chamber

## Slide 7
Anode Plane
Spacers
Mesh
Drift plane
Drift gap
(few hundred V/cm)
Amplification
Gap
30-40 KV/cm
Micromegas was invented by ‘Ioanis Giomataris’ in 1995

## Slide 8
Anode Plane
Spacers
Mesh
Drift plane

## Slide 9
Large prototype TPC for ILC
The 1T magnet.
The 60 cm long DESY field cage
1-6 GeV
e- beam

## Slide 10
Data taking during first two weeks of March-2015 at DESY

## Slide 11
Module size: 22 cm × 17 cm
24 rows × 72 columns
Readout: 1726 Pads
Pad size: ~3 mm × 7 mm
End plate of LP-TPC
The Micromegas module

## Slide 12
Different studies are done:
Studies | Range
At different drift distances | full available drift length of 60 cm
At different phi | 0, 2, 4
At different theta | 10 to 30 in steps of 5
At different X positions | ‘-40’ mm to ‘30’ mm
At different peaking time of the electronics. | 100 ns to 1000 ns
At two different fields | 140 V/cm, 230 V/cm
At different noise thresholds | 3 sigma and 4.5 sigma
At two different magnetic fields | 0 T and 1 T
At different momenta | 1 GeV to 5 GeV
Cosmic | B = 1 T and B = 0 T

## Slide 13
pads
mesh
E
B
~100m Amplification gap:
resistive foil: ~75m
insulator: ~100m
Charge dispersion 2mm
R is the the surface resistivity of the resistive layer, C is the capacitance per unit area and t is the shaping time of the electronics.
Before we have been using Carbon Loaded Kapton which is now unavailable.
A new resistive material, Diamond Like Carbon is available from Japan.
We used both in the beam test.
In standard Micromegas
resolution is given by,
Charge is dispersed in
Resistive Micromegas
We are using resistive Micromegas

## Slide 14
Track in 3-D space
Track on 7-module Micromegas
5-GeV electron beam
5-GeV electron beam
Row number
Mod 5
Mod 1
Mod 2
Mod 3
Mod 4
Mod 6
Mod 0

## Slide 15
The analysis is done within the framework of ‘MarlinTPC’
Noise threshold, Physical conditions are checked.
Geometry / Mapping are connected
Data is converted from ‘acq’ to ‘slcio’
Pulse Finder and the Hit Finder
Track Finder and Track Fitter
Reconstruction
General processing
Distortion Correction
Resolution Calculation
Analysis

## Slide 16
Number of Pads per Hit
Comparison between Black Diamond and the CLK modules
For CLK, number of pads per hit=2.8
For BD, number of pads per hit=3.6
Surface resistivity of BD modules is slightly less than in CLK

## Slide 17
Charge per Cluster for CLK and BD modules at 200 ns peaking time of the electronics
Charge per cluster in BD is slightly more than CLK.
This is because, BD has slightly large capacitance than CLK.

## Slide 18
Normalised main pulse for BD and CLK

## Slide 19
Measurement of drift velocity

## Slide 20
Potential distribution shows distortion
Simulation with COMSOL
Cathode
MM module 1
MM module 2
Anode
Anode
mesh
mesh
mm

## Slide 21
Drift of the electrons
Simulation with Garfield
B = 0
B = 1
Z (drift)
Cathode
Cathode
Anode
Mesh
ground

## Slide 22
Distortion at B = 0 T
Before alignment of the modules
After alignment of the modules

## Slide 23
Distortion in B = 1 T
The E×B effect can be seen near the edges
Before distortion correction
After distortion correction
Distortion correction is done in MarlinTPC/DistortionCorrectionProcessor

## Slide 24
r-phi resolution vs drift distance for B = 1 T
Preliminary
B=1T, peaking time = 200 ns, E=230 V/cm, phi =o

## Slide 25
r-phi resolution vs drift distance for B = 1 T
Preliminary
B=1T, peaking time = 200 ns, E=230 V/cm, phi =o

## Slide 26
z resolution vs drift distance for B = 1
Preliminary
B=1T, peaking time = 200 ns, E=230 V/cm, phi =o

## Slide 27
Two-phase CO2 cooling
Each module’s electronic takes nearly 30 W of electric power.
This rises the temperature of the detector up to 70 deg C
Temperature gradient in ILC-TPC
Simulation with COMSOL
Drift Distance Vs Temperature
Simulation with Magboltz

## Slide 28
Two-phase CO2 cooling
General lay out of the MM module
The radiators and the cooling pipe
Benefit of two-phase CO2 cooling is that the cooling happens during
phase change which ensures uniform cooling at constant temperature.

## Slide 29
Two-phase CO2 cooling
Experimental result with one module
Shows the heating and cooling
Simulated result for one module
Shows heating and cooling
Experimental and simulation result for one MM module shows heating and cooling

## Slide 30
Two-phase CO2 cooling during 2015 beam test
Stable temperature during cooling
Temperature rises when cooling is stopped
During cooling, temperature is below 30 deg C and
Stable within 0.2 deg C.

## Slide 31
Two-phase CO2 cooling
simulated model (COMSOL) shows how cooling works

## Slide 32
Summary
Different studies have been carried out with 7 Micromegas modules during beam test 2015.
In 1 Tesla magnetic field, the space resolution of Micromegas modules is below 150 micron in 60 cm drift length, which satisfies ILC requirement.
Two new Micromegas modules with resistive layer of Diamond Like Carbon (DLC) have been tested and the result is satisfactory.
Two-phase CO2 cooling is used uninterruptedly for more than 80 hrs. Temperature of individual Front End Cards (FECs) is stable within 0.2 degree C during the beam test. Recently a paper on two-phase CO2 cooling for Micromegas has been accepted in JINST.

## Slide 33
I sincerely thank to :
Maksym Titov
Boris Tuchming
Fabrice Couderc
Marc Riallot
Supratik Mukhopadhyay

## Slide 34
THANK You

## Slide 35
Backup Slides
Distortion of electric field lines

## Slide 36
Backup Slides
Before distortion correction

## Slide 37
Backup Slides
After distortion correction