## Slide 1
The n_TOF Collaboration, www.cern.ch/nTOF
The n_TOF facility at CERN: a bright future for neutrons
Enrico Chiaveri
Spokesperson of n_TOF Collaboration
Notes: Thanks for the invitation

## Slide 2: Outline of the talk
Scientific motivations
The n_TOF facility and experimental setup
Status, upgrades and future perspectives
Selected experimental results
n_TOF Experimental Area 2 Project

## Slide 3
Scientific motivations
The n_TOF facility and experimental setup
Status, upgrades and future perspectives
Experimental results and 2012 experimental program
n_TOF Experimental Area 2 Project
Outline of the talk

## Slide 4
Figura Nucleosintesi (frecce che si muovono)
Foto FIC
239Pu: 125 Kg/yr
237Np: 16 Kg/yr
241Am:11.6 Kg/yr
243Am: 4.8 Kg/yr
244, 245Cm
1.5 Kg/yr
LLFP
LLFP
76.2 Kg/yr
The nuclear waste problem
Quantities refer to yearly production in 1 GWe LW reactor

## Slide 5: Main waste problem of current nuclear reactors
Existing reactors have a relatively low burn-up efficiency and produce large amount of radioactive waste
97%
238U
Fuel (LWR)
94%
238U
Spent fuel
1% 235U
1% Pu and Minor Actinides
4% Fission products
3% 235U
96%
potential
fuel
Current reactors use only few % of U resources
Availability of U resources at current price may become a problem in the medium term (~100 y)
A closed cycle would make uranium resources sufficient for thousand of years

## Slide 6: Nuclear waste composition
Source: CEA – Clefs N. 46, Spring 2002
FF decay after some hundreds of years (with some exceptions)
Actinides last for millions of years
Constitute the main problem in the nuclear waste management
The long term radiotoxicity of nuclear waste is governed by actinides such as Pu, 237Np, 241,243Am and 245Cm

## Slide 7: Data needs for nuclear energy
Data on a large number of isotopes are needed for design of advanced systems and for improving safety of current reactors
Nuclear fuel (U/Pu and Th/U)
  Th, U, Pu, Np, Am, Cm (n,f) + (n,g)
Long-lived fission products
  99Tc, 103Rh, 135Xe, 135Cs, 149Sm  (n,g)
Structural and cooling material
  Fe, Cr, Ni, Zr, Pb, Na, …  (n,*)
The overall list if relatively long:
  Capture cross section of 235,238U, 237Np, 238-242Pu, 241-243Am, 244Cm
  Fission cross-section of 234U, 237Np, 238,240,242Pu, 241-243Am, 242-246Cm
NEA/WPEC-26 (ISBN 978-92-64-99053-1)

## Slide 8
 |  | Energy Range | Current Accuracy (%) | Target Accuracy (%)
U238 | inel | 0.5 ÷ 6.1 MeV | 10 ÷ 20 | 2 ÷ 3
 | capt | 2.04 ÷ 24.8 keV | 3 ÷ 9 | 1.5 ÷ 2
Pu241 | fiss | 454 eV ÷ 1.35 MeV | 8 ÷ 20 | 2 ÷ 5
Pu239 | capt | 2.04 ÷ 498 keV | 7 ÷ 15 | 4 ÷ 7
Pu240 | fiss | 0.498 ÷ 1.35 MeV | 6 | 1 ÷ 3
Pu242 | fiss | 0.498 ÷ 2.23 MeV | 19 ÷ 21 | 3 ÷ 5
Pu238 | fiss | 0.183 ÷ 1.35 MeV | 17 | 3 ÷ 5
Am242m | fiss | 67.4 keV ÷ 1.35 MeV | 17 | 3 ÷ 4
Am241 | fiss | 2.23 ÷ 6.07 MeV | 9 | 2
Am243 | fiss | 0.498 ÷ 6.07 MeV | 12 | 3
Cm244 | fiss | 0.498 ÷ 1.35 MeV | 50 | 5
Cm245 | Fiss | 67.4 ÷ 183 keV | 47 | 7
Fe56 | Inel | 0.498 ÷ 2.23 MeV | 16 ÷ 25 | 3 ÷ 6
Na23 | inel | 0.498 ÷ 1.35 MeV | 28 | 4 ÷ 10
Pb206 | inel | 1.35 ÷ 2.23 MeV | 14 | 3
Pb207 | Inel | 0.498 ÷ 1.35 MeV | 11 | 3
Si28 | inel | 1.35 ÷ 6.07 MeV | 14 ÷ 50 | 3 ÷ 6
 | capt | 6.07 ÷ 19.6 MeV | 53 | 6
Uncertainty reduction requirements for Gen IV fast reactors
An accuracy better than 3-4% is required for most Pu isotopes and Minor Actinides, from few keV to several MeV
Aliberti, Palmiotti, Salvatores – Validation of simulation codes for future systems, NEMEA-4 Workshop, October 2007
(in order to meet integral parameters target accuracies)
Notes: Quantitativamente gli studi di senbilitita’ forniscono le incertezze che I dati nucleari per certe reazioni, isotopi e intervalli energetici devono raggiungere per ottenere una accuratezza predeterminata su parametri integrali di un reattore come ad esempio il coefficiente di moltiplicazione. E’ evidente che nel caso della maggior parte degli isotopi e attinidi minori e’ richiesta una accuratezza dell’ordine del 3-4%

## Slide 9: New generation reactors
Generation IV (especially fast) reactors would be in principle able to recycle part of spent fuel
Other options considered:
  Accelerator Driven Systems (nuclear waste incineration)
  Use Th/U fuel cycle (current being developed, e.g. India)
Recycling and reuse!
The development of Gen-IV fast breeder reactor requires accurate neutron data to minimize design uncertainties and optimize safety parameters (reduced b-delayed fraction compensation)

## Slide 10: Stellar Nucleosynthesis
s-process (slow process)
  Capture times long relative to decay time
  Involves mostly stable isotopes
  Nn=108 n/cm3, kT=0.3-300 keV
r-process (rapid process)
  Capture times short relative to decay time
  Produces unstable isotopes (neutron –rich)
  Nn=1020-30 n/cm3
Neutron beams
Radioactive beam facilities

## Slide 11: Status of neutron capture cross-section for astrophysics
Huge amount of data collected on many isotopes, mostly stable
Cross-section uncertainties remain high, in particular compared with progresses in:
  Observation of abundances
  Models of stellar evolution
For three classes of nuclei data are lacking or need improvements:
  Nuclei with low cross-section, i.e. neutron magic nuclei (s-process bottlenecks) (N=50,82, e.g. 88Sr, 90Zr, 139La, etc.)
  Isotopes unavailable in large amount (rare or expensive, 186,187Os, 180W)
  Radioactive branching isotopes (“stellar thermometers”)
    79Se, 85Kr, 151Sm, 204Tl, 205Pb, etc.
Bao et al., ADNDT 76 (2000)

## Slide 12
Scientific motivations
The n_TOF Collaboration, facility and experimental setup
Status, upgrades and future perspectives
Experimental results and 2012 experimental program
n_TOF Experimental Area 2 Project
Outline of the talk

## Slide 13: n_TOF Collaboration Institutions
n_TOF Collaboration is an International endeavour since 2001
Members as of 2012 (not necessarily CERN member states):
  30 Institutions (EU, USA, India) + collaboration with JP and RUS
  100 scientists
  16 PhD students
Newcomers since 2009:
  Joint Research Center IRMM (Belgium)
  University of Zagreb (Croatia)
  University of Manchester (United Kingdom)
  University of York (United Kingdom)
  University of Frankfurt (Germany)
  PSI – Paul Scherrer Institute (Switzerland)
  University of Thessaloniki (Greece)

## Slide 14: n_TOF facility at CERN
n_TOF (*) is a spallation neutron source based on 20 GeV/c protons from the PS of CERN
(*) C Rubbia et al., A High Resolution Spallation Driven Facility at the CERN-PS to measure Neutron Cross Sections in the Interval from 1 eV to 250 MeV, CERN/LHC/98-02(EET) 1998.

## Slide 15: CERN Accelerator complex (2012)

## Slide 16
Concept by C.Rubbia
CERN/ET/Int. Note 97-19
1997
Proposal
submitted
Aug 1998
Phase II
2009
Upgrades:
Borated-H2O
Second Line
Class-A
2010
Construction
started
1999
Problem Investigation
2004-2007
2001-2004
Phase I
Isotopes
Capture: 25
Fission: 11
Papers: 21
Proc.: 51 Doc: 150
V. Vlachoudis
EAR2
design
2011
1995-1997
TARC experiment
Feasibility
CERN/LHC/98-02+Add
May 1998
2000
Commissioning
New Target
construction
2008
Commissioning
May 2009
1996
2012
n_TOF Facility Timeline
EAR2
2014
Commissioning

## Slide 17: Accelerator complex for the n_TOF facility
PS 20 GeV/c
PSB 1.4 GeV/c
n_TOF 185m flight path
n_TOF target

## Slide 18: n_TOF experimental setup
Spallation target  neutrons
1st collimator (Ø=11 cm)
  Halo cleaning, first shaping of the beam + filter station
Sweeping magnet
2nd collimator (Ø=1.8/8 cm) – beam shaping for EAR
Experimental Area 1
  186 m from spallation target, location of samples and detector

## Slide 19: Time-of-flight method at n_TOF
Determination of the neutron kinetic energy via the time difference between neutron production and the detection of reaction products (g or FFs)

## Slide 20: The n_TOF facility
Main feature of n_TOF is the extremely high instantaneous neutron flux (105 n/cm2/pulse)
Unique facility for measurements of radioactive isotopes (maximize S/N)
  Branch point isotopes (astrophysics)
  Actinides (nuclear technology)
Other features of the neutron beam:
  High resolution in energy (DE/E=10-4)  study resonances
  Large energy range (25 meV<En<1 GeV)  measure fission up to 1 GeV
  Low repetition rate (<0.8 Hz)  no wrap-around

## Slide 21: n_TOF basic characteristics
n_TOF average flux comparable to GELINA (with 30 m flight path)
Average flux (n/sec)
Instantaneous flux (n/pulse)
3 orders of magnitude!
Very high instantaneous neutron flux
  High proton intensity per pulse
  Spallation process
Great advantage in measuring radioactive samples (improved S/N ratio)

## Slide 22: Complementarity with NFS (Neutron for Science)
Average flux (n/sec)
Instantaneous flux (n/pulse)
water-moderated neutrons
neutrons in stellar environments
kT = 5-100 keV
neutrons from thermal fission
water-moderated neutrons
neutrons in stellar environments
kT = 5-100 keV
neutrons from thermal fission

## Slide 23: Detectors for capture (n,g) reactions
Neutron capture reaction are studied by detecting g-rays emitted in the de-excitation of the CN
Two types of background (source of systematic errors)
  g-rays from neutron scattered by the sample and captured in the setup (“neutron sensitivity”)
  g-rays from background, radioactivity of the sample or competing reactions
A unique solution does not exists. At n_TOF two different detectors built to minimize the two background types
Neutron sensitivity: big problem for isotopes with low capture cross-section (e.g. astrophysics)
(n,n)
(n,g)

## Slide 24
Parallel Plate Avalanche Counter
(PPAC)
MicroMegas (MGAS)
sCVD diamond (3x3 array)
BaF2 Total Absorption Calorimeter (TAC)
Low neutron sensitivity C6D6
(n,chp) reactions
(n,xng) reactions
n_TOF Detectors

## Slide 25: Detectors with low neutron sensitivity
At n_TOF neutron sensitivity enormously reduced relative to past detectors
Very small amount of material and extensive used of carbon fibers
However: low efficiency and selectivity

## Slide 26: The n_TOF calorimeter
n_TOF TAC:
  4p array of 40 BaF2 scintillators (15 cm thick)
  High efficiency allows to reconstruct the entire de-excitation cascade
High neutron sensitivity (detectors and heavy support structure)
  Minimize neutron sensitivity with inner sphere of absorbing material and capsules in carbon fibre with 10B

## Slide 27: The fission setups
The main problem in fission measurements is the background due to a-decay
At n_TOF minimized by the very high instantaneous neutron flux
Three different detectors employed:
  Fission Ionization Chamber (FIC) [2002-2005]
    Standard detector, with fast gas (Ar+CF4) and electronics
  Parallel Plate Avalanche Counters (PPAC) [2001-20xx]
    Fission fragments detected in coincidence
    Very good rejection of a-background
  MicroMegas detector (MGAS) [2010-20xx]
    Innovative detector based on the micro-mesh concept
    In beam monitoring, no sensitivity to g-rays, fast response, compact device

## Slide 28
n_TOF Ph-2 set-up:
Samples tilted 45degrees wrt. neutron beam
10 PPAC detectors with 9 targets in between (235U, 238U, 237Np, 6x232Th)
Segmented cathodes to study the ang. distributions of FF, in addition to sn,f(En).
Parallel Plate Avalanche Counter PPAC

## Slide 29: n_TOF Data Acquisition System
High instantaneous neutron flux
  Several events for each neutron pulse expected + pile-up between
Standard DAQ methods are largely inadequate
n_TOF DAQ based on flash-ADC:
  ~56 fADC channels, up to 1 GS/s
  Full history of every detector digitized during time window of up to 80 ms
  Nearly zero dead time
Offline signal reconstruction for time and charge
  Pulse-shape fitting analysis (pile-up)

## Slide 30
Scientific motivations
The n_TOF Collaboration, facility and experimental setup
Status, upgrades and future perspectives
Experimental results and 2012 experimental program
n_TOF Experimental Area 2 Project
Outline of the talk

## Slide 31: n_TOF facility improvements 2009/2014
New lead spallation target [2008/9]
  Extended operation of n_TOF
Improved cooling and ventilation system [2009]
  Optimization of heat dissipation and water chemistry
Separated moderator system: 10B water as moderator [2010]
  Reduction of the in-beam g-rays by factor of 10x
Transformation of the EAR1 in a type-A laboratory [2010]
  No need for certified sealing for radioactive samples
Extended memory of flash-ADC digitizers [2011]
  n,g measurement with C6D6 down to thermal energies (25.3 meV)
Experimental Area 2 Project [2012-2014]

## Slide 32: n_TOF new spallation target
Neutron window, Ø= 600 mm
Proton window, Ø= 200 mm
Spallation target is now enclosed in a new pressurized vessel
Pure lead 99.99% monolithic
Support and anti-creep structure in AW5083 H111
Uncladded design
Water chemistry continuously monitored
Water jet flow on the proton entrance surface to maintain local temperature less than boiling point

## Slide 33: Borated water system moderator
Main goal is to reduce the in-beam g-ray background from 1H(n,g)  2.2 MeV
Increased capture in 10B rather than 1H, by operating in saturated conditions (1.3% in H3BO3)
  Improvement of neutron-induced capture reaction with C6D6 liquid scintillator

## Slide 34: Performances with the borated water circuit
Expected reduction of the neutron fluence <1 keV
Reduction of the 2.2 MeV g-ray (~10x)

## Slide 35
Entrance of n_TOF beam line
Escape line
EAR-1
N_TOF Beam Line

## Slide 36
Scientific motivations
The n_TOF Collaboration, facility and experimental setup
Status, upgrades and future perspectives
Selected experimental results
n_TOF Experimental Area 2 Project
Outline of the talk

## Slide 37
n_TOF Phase 1 (2001-2004)
Capture
151Sm
204,206,207,208Pb, 209Bi
24,25,26Mg
90,91,92,94,96Zr, 93Zr
186,187,188Os, 139La
232Th, 233,234U
237Np,240Pu,243Am
Fission
233,234,235,236U
232Th, 209Bi
237Np
241,243Am, 245Cm
The n_TOF activity
  Misurements of capture reactions:
    25 Isotopes (8 of which radioactive)
    Astrophysics and Nuclear Technology (transmutation)
  Measurements of fission cross-sections:
      11 isotopes (10 radioactive)
      Mainly for Nuclear Technology (ADS, Gen IV, Th/U cycle)
      strong interest by International Nuclear Agencies
Papers: >50
Other pubblications: >150
Data are becoming available on EXFOR
Notes: Motivazioni Zr, Mg / Misure precedenti Os (orela ’80) / Proprietà nucleari (average level spacing, average radiative width, average neutron strength) / ISO 2919

## Slide 38
n_TOF Phase 2 (2008-2012)
Capture
25Mg, 54, 56,57Fe
58,60,62Ni, 63Ni,88Sr
236,238U
241Am
Fission
240,242Pu
235U(n,g/f)
232Th , 234U, 237Np ang. distr.
(n,a)
33S, 59Ni
The n_TOF activity
  Measurements of capture reactions:
    12 Isotopes (4 of which radioactive)
    Astrophysics and Nuclear Technology (transmutation)
  Measurements of fission cross-sections:
      6 isotopes (5 radioactive)
      Mainly for Nuclear Technology (ADS, Gen IV, Th/U cycle)
  Other measurements:
      Simultaneous capture and fission
      (n,a) reactions (using diamond detectors)
Notes: Motivazioni Zr, Mg / Misure precedenti Os (orela ’80) / Proprietà nucleari (average level spacing, average radiative width, average neutron strength) / ISO 2919

## Slide 39
Data for the Th/U fuel cycle
At n_TOF we have measured the two main reactions of the cycle: the 232Th(n,g) and 233U(n,F).
Results with high resolution, high accuracy (3 - 5 %) and wide energy range (from thermal to several MeV).
232Th(n,g)
Important data for the development of the Th/U fuel cycle

## Slide 40: Results from 245Cm(n,f) reaction (FIC)
Significant a-particle contribution due to t1/2=8500 y and of 244Cm contamination (t1/2=18 y)
High amplitude threshold + spontaneous fission subtraction
Data normalized at thermal energies with a weighted average of two recent measurement
From thermal up to 1 eV n_TOF data intermediate between Browne et al. and White et al.
M. Calviani et al. (n_TOF Coll.), accepted for publication in Phys. Rev. C (2012)

## Slide 41
M. Calviani et al., Phys. Rev. C 85, 034616 (2012)
245Cm(n,f)
The 245 Cm(n,f) cross section between 10 and 17 eV neutron energy, compared with two previous data sets and with evaluations.
The 245Cm(n,f) cross section in the un- resolved resonance region from 1 keV to 1 MeV neutron energy, compared with the data and with the evaluated data sets of ENDF/B-VII.0 and JENDL/AC-2008.

## Slide 42
The sample (disk-shaped with 12.2 mm diameter) consists on 32.2 mg of 241Am oxide embedded in a 305 mg Al2O3 matrix and encapsulated in a 0.5 mm thick aluminum canning.
(3.8 GBq)
First time that complete region is covered from thermal to MeV in a single measurement
Combined C6D6/TAC measurement for improved accuracy
Unprecedented resolution and statistics, to extend RRR beyond 150 eV
241Am(n,g)
PRELIMINARY

## Slide 43
63Ni(n,g)
First high-resolution measurement of 63Ni(n,g) in the astrophysical energy range
First experimental observation of resonances in the keV region.
63Ni-sample
62Ni-contam.
63Ni (t1/2=100 y) represents the first branching point in the s-process reaction path:
  Highest uncertainty in 63,65Cu abundances comes from the 63Ni(n,g) unknown cross section
PRELIMINARY
62Ni sample irradiated in thermal reactor (in 1984 and 1992)
total mass of 1002 mg
enrichment in 63Ni: ~13 % (131.8 mg)
contaminants: ~15.4 mg 63Cu
After chemical separation at PSI:
NiO powder, (919 mg Ni)
<0.01 mg 63Cu
C.Lederer et al Neutron capture cross section of unstable 63Ni: implications for stellar nucleosynthesis to be published in Phys.Rev.

## Slide 44
Scientific motivations
The n_TOF Collaboration, facility and experimental setup
Status, upgrades and future perspectives
Experimental results and 2012 experimental program
n_TOF Experimental Area 2 Project
Outline of the talk

## Slide 45: n_TOF Experimental Area 2 Project
2nd Experimental Area:
  Flight path located at ~19 m at 90˚ vertically with respect to the proton beam
  Experimental area at ground level
  INTC-O-015
Operative by mid-2014

## Slide 46: n_TOF EAR2 advantages
Main advantages of Experimental Area 2:
  Neutron fluence is on average increased by a factor of 25
  Very small mass samples (<1 mg) could be measured
  Very small cross-section
  Much shorter time scale measurement
  Running in parallel with Experimental Area 1
Example of EAR2 possible measurements:
  Measurement of the 25Mg(n,a)22Ne cross section
  Measurement of 7Be(n,p)7Li and 7Be(n,a)4He cross sections
  Capture (and fission) cross sections of the fissile 245Cm
  Cross section and angular distribution of fragments from 232U(n,f)

## Slide 47
The main features of EAR 2
n_TOF target pit
ISR
Maximum neutron fluence gain: x27 (keV region)
Higher fluence, by a factor of 25, relative to EAR1.
The shorter flight path implies a factor of 10 smaller time-of-flight.
Global gain by a factor of 250 in the signal/background ratio for radioactive isotopes!
The huge gain in signal-to-background ratio in EAR2 allows to measure radioactive isotopes with half lives as low as a few years.

## Slide 48: EAR-2 for Neutron Irradiation
Neutron Tube has 32 cm diameter
at 1.5 m from the target center
Total: 6.22e1015 n / cm^2 / 7e12 ppp
Basket for material irradiation

## Slide 49: Overview of n_TOF target area
n_TOF target pit
Technical gallery (@10 m from pit)
EAR2 (@20 m from pit, above ground)
Existing hole
To be built
ISR

## Slide 50
Experimental Hall
Dump
Detector Support

## Slide 51
Beam Dump
EAR-2 Exp. Hall
Collimator
Magnet
Pit shielding
Target
New area
Existing area
The future: n_TOF vertical flight path at 20 m

## Slide 52
Experimental Hall

## Slide 53
The experimental program in EAR2
n_TOF target pit
ISR
The EAR2 will allow to:
  measure samples of very small mass (<1 mg)
  measure short-lived radioisotopes (down to a few years)
  collect data on a much shorter time scale
  measure (n,charged particle) reactions with thin samples
Letter of intent for measurements in EAR2:
  (n,p) and (n,a) cross sections on 7Be, 25Mg, 26Al
  Fission cross sections of the short lived actinides 232U, 238,241Pu and 244Cm
  Capture cross section of 79Se, 245Cm
  Cross section and angular distribution of fragments from 232U(n,f)
Status of the EAR2:
Approved by CERN, final design phase
Start construction in 2013
Beam ready in mid-2014
Physics start after commissioning in 2015

## Slide 54: Conclusions
There is need of accurate new data on neutron cross-section both for astrophysics and nuclear technology
Since 2001, n_TOF is contributing to the world efforts aimed at collecting high quality data, mostly on capture and fission
Main advantage of n_TOF is the high instantaneous neutron flux and high performance detectors
Improved background conditions in EAR1 with the borated water system
Radioprotection issues solved by transformation of EAR1 in a Work Sector Type A
The 2nd experimental area (EAR2) will open new perspectives for measurement with lower masses (ready by 2014)

## Slide 55
Thanks a lot for you attention!