## Slide 1
The Higgs Boson, the SM… and now what? aFCC (ee,pp,ep)
CSTS
June 6, 2014
Introduction
FCC: The Frontiers for Particle Physics
FCC: Organization
SACLAY involvements
Conclusion
LHC
SPS
FCC
PS
SPP : R. A., H. Bachacou, M. Besançon, F. Couderc, F. Deliot, S. Ganjour, P.-F. Giraud, C. Guyot, G. Hamel de Monchenault, E. Lançon, J.-F. Laporte, E. Locci, J. Malcles, C. Royon, P. Schune, P. Schwemling, M. Spiro, J. Zinn-Justin
SACM : A. Chancé, B. Dalena, J. Payet, J.-M. Rifflet
SEDI : en discussion
J. Ellis et al.

## Slide 2
With the discovery of the Higgs Boson
Self-consistent model (SM) accounting for all Particle Physics phenomena at presently accessible energy
but does not explain major issues
Mass of neutrino (in the most general way)
Baryon Asymmetry of Universe
Dark Matter, Dark Energy
Unification of all interactions
New Physics must exist … but at which energy scale?
Precision measurements rare process studies
Direct Exploration of Higher Energy Scales

## Slide 3
Grand unification of Interactions (Strong, Weak, Electromagnetic)
e.g. supersymmetric particles at TeV’s energy scales affect the running of the coupling constants
Need to explore higher energy regions (up to ~10 TeV)
BICEP2
points to 1016 GeV unification scale
Interaction strength varies with energy scale depending on available quantum numbers and particle species

## Slide 4
Either using existing
LEP/LHC tunnel to reach 26-32 TeV collisions
Or build (or reuse) a 80km tunnel to reach 80-100 TeV collisions FCC-hh
a more detailed study of such a tunnel needed
VHE
VHE-LHC
Paramètres | Valeurs
Energie c.m. (TeV) | 100
Circonférence (km) | ~100
Champ des dipôles (T) | 16 (Nb3SN) [20 option HTS]
Luminosité (cm-2s-1) | 5 1034
Energie stockée/faisceau (GJ) | 8.2
Puissance dissipée (W/m) | 26
Espacement bunch (ns) | 25 [ 5 option]
Pile up | 171 [34]
Population bunch | 1 [0.2] x 1011
Nombre bunch | 10500 [53000]
In both cases, SC challenge to develop 16-20 Tesla magnets!
Magnets for HL_LHC is an indispensable first step

## Slide 5
Type de particule | Section efficace (fb) | Limite de masse (TeV)
Quark excité | ~10-2 | ~50
Z’ () | ~4 x 10-3 | ~30
Squark/gluino | ~0,4/2 | 8/8-13
Stop | ~0.2 | 6
Type de particule | Section efficace (fb) | Limite de masse (TeV)
Quark excité | ~10-2 | ~50
 | ~4 x 10-3 | ~30
Squark/gluino | ~0,4/2 | 8/8-13
Stop | ~0.2 | 6
Today’s most promising manner to explore directly the energy scale up to 10 TeV and higher for some specific new particle is a 100 TeV p-p collider
FCC
A more complete study of the physics reach for the search of new particles needs to be carried out
Assuming very significative sensitivity to new particles
Examples

## Slide 6
Chart: pp->H Xsections
| 8 | 14 | 33 | 40 | 60 | 80 | 100
ggF | 19520 | 50350 | 178320 | 231610 | 468255 | 563920 | 740145
VBF | 1559 | 4400 | 16720 | 22880 | 40920 | 59840 | 81840
WH | 696 | 1630 | 4727 | 5868 | 9291 | 12551 | 15811
ZH | 394 | 900 | 2970 | 3780 | 6120 | 8640 | 11250
ttH | 130 | 620 | 4526 | 6820 | 14880 | 25420 | 37820
HH | 33.8 | 206.18 | 297.44 | 608.4 | 980.2 | 1419.6
FCC-pp permits to study “conventional” physics, thanks to the large production cross sections
Outstanding example is Higgs production
x 60
x 40
Parameter | uncertainty
dgHtt/gHtt | ~1%
dlHHH/lHHH | ~10%
Particular examples are the H to tt and self couplings
A more complete study of the sensitvity reach for the Higgs couplings is needed with a dedicated detector
Detector with high h (~6) acceptance!

## Slide 7
120 kt yoke
Detector concept studies have started
B ~6.0 T
Shield coil
Bout ~-2.3 T Bin ~8.3 T
52m
Btor.~2 T
BID~3.5 T/3m(2T/4m)
Optimization of overall detector design is needed!!!
Stored energy 65 GJ
Stored energy 54 GJ

## Slide 8
Future large scale accelerators
p-p collider FFC-hh (VHE-LHC) in
80-100 km tunnel
LEP/LHC
Muti-TeV e+e- Linear Colliders
(CLIC)
pp Colliders
(HE-LHC, VHE-LHC,…)
Muon Colliders
(n-Fact. as possible 1st step
HE-Frontier Colliders
Plasma Colliders
…for HE-physics and -Frontier exploration
up to 3 TeV
up to 100 TeV
up to 10 TeV
> 5 TeV

## Slide 9
TLEP Ring e+e- collider: Primary Cost Driver is the tunnel
80 km tunnel
LEP/LHC
Building on existing technologies and experience (LEP, KEKB, PEPII…)
Could cover a wide range of energy up to 400 GeV collision energy.
Using SC cavities
Energy CM (GeV) | 90 | 160 | 240 | 350
Luminosity (x1034cm-2s-1)/IP | 28-56 | 12-16 | ~6 | ~1.8
Cavity Gradient (MV/m) | 20 | 20 | 20 | 20
#5-cell SC cavities | 600 | 600 | 600 | 600
Beam lifetime (mn) | 200 | 50 | 21 | 15
Total AC power (MW) | 250 | 250 | 260 | 300
Most parameters have been achieved or are planned at SuperKEKB
If e+e- needed, it is likely to come first

## Slide 10
Chart: Luminosity vs Energy
| 90 | 160 | 240 | 350 | 500 | 1000 | 1500 | 3000
TLEP(1-IP) | 560 | 160 | 48 | 13
ILC | 3 | 5 | 7.5 | 12 | 18 | 49
CLIC | 23 | 30 | 37 | 59
TLEP(4-IP) | 2240 | 640 | 192 | 52
arXiv:1308.6176v1 [hep-ex] 28 Aug 2013
To know more about FCC-ee/TLEP see
Main features:
Very High luminosity
Multi Interaction Regions
Low beamstrahlung
Excellent beam energy knowledge

## Slide 11
 | LHC(300) | LHC (3000) | ILC programme | FCC-ee programme | Comment/caveat
DmW (MeV) | ~10 | ~10 | ~7 | <0.5 | Theor. limited
Dmt (MeV) | 800-1000 | 500-800 | 34 | 10 | ~100 from theo.
DmH (GeV) indirect | -25 | ~20 | ~5 | ~1.4 | Theor. errors should match!
DmH (MeV) direct | ~100 | ~50 | ~35 | ~7 | Overkill for now
FCC-ee instant. Luminosity (cm-2s-1) | 5.6 1035 @Z-pole | 1.6 1035 @161 GeV | 5 1034 @240 GeV | 1.3 1034 @~350 GeV
FCC-ee Programme | #Z in 1 year @Z-pole | #W in 1 year @161 GeV | #H in 5 years @240 GeV | #top in 5 years @~350 GeV
# events@FCC-ee with 4 detectors | ~ 1012 | ~ 5 107 | >2 106 | > 106
Beam E cal. with
reson. depolar.
Unique to FCC-ee

## Slide 12
High precisions at Z pole and WW and top thresholds
Indirect mH measurement error
TLEP + matching theory a dmH ± 1.4 GeV
TLEP + present theory a dmH ± 11 GeV
Ebeam calibration with resonant depolarization unique to circular collider
a dEbeam < 0.1 MeV should be possible @TLEP

## Slide 13
High precisions at Z pole and WW and top thresholds
Actual MH
(HL-LHC)
TLEP
Indirect:MH=94.0 ± 1.4
Direct: MH=125.500 ±0.007
.

## Slide 14
High precisions Higgs couplings at 240 GeV and 350 GeV
Great e+e- asset: Tagged Higgs sample
  Total Higgs decay width
  Individual branching ratios to sub %
  Invisible and exotic decays
Reconstruct Z
Determine recoil mass
(thanks to be beam-energy constraint)
Z → nn
Z → All
Unpolarized cross sections
P Janot and G. Ganis
Spin,
mass
sHZ, BRs,
width
sHnn, BRs,
width
But …
Cross section modest a very large luminosity
d(sHZ) = 0.4%
Model independent way to measure GH

## Slide 15
n
n
n
DGH /GH
d(sWWgHgbb )
= 0.6%
Total Higgs decay width can also be extracted from W-fusion

## Slide 16
Accelerator  Physical quantity  | HL-LHC 3000fb-1 /exp | ILC (250+350) | TLEP 240 +350 4 IP
H/H | -- | 6.0% | 1.0%
Δinv/H | ~7% | 2.9% | 0.45%
ΔgH/gH | 2.0% | 14.5% | 1.5%
ΔgHgg/gHgg | 3.0% | 4.4% | 0.8%
ΔgHww/gHww | 2.0% | 0.5% | 0.19%
ΔgHZZ/gHZZ | 2.0% | 0.9% | 0.15%
ΔgH/gH | <10% | 45% | 6.2%
ΔgH/gH | 2.0% | 2.9% | 0.54%
ΔgHcc/gHcc | ~7% | 3.8% | 0.71%
ΔgHbb/gHbb | 4.0% | 2.4% | 0.42%
Sensitivity to Higgs couplings at FCC-ee/TLEP using data at 240 and 350 GeV (5 years at each energy)
Comparison with of TLEP sensitivities with HL-LHC and ILC
Sub-percent (permille) level measurements are needed

## Slide 17
ElectroWeak Symmetry Breaking precision measurements
SUSY modifies tree-level couplings
e.g. Pseudo-scalar A is difficult to find for moderate tanb=5
Largest effet expected for bb, tt
e.g. light stop is an important search (hierarchy problem)
Compositness
All couplings reduced according to compositness scale
Higgs couplings should be measured as precisely as possible!
H. Baer, M. Peskin et al.
Example : Precision for Higgs couplings

## Slide 18
Chart: Particle Mass (GeV)
| 91 | 81 | 173 | 4.5 | 1.76 | 1.2 | 7.4999999999999997E-2 | 0.105 | 5.0000000000000001E-3 | 3.0000000000000001E-3 | 5.1099999999999995E-4
 | 0.50047 | 0.44548 | 0.96111 | 0.025 | 0.0097778 | 0.0066667 | 0.00041667 | 0.00058333 | 2.7778e-05 | 1.6667e-05 | 2.8389e-06
t
Z
W
b
t
c
m
s
d
u
e
f +
f -
H
Measuring precisely the particle coupling to H0
M = 246.0 ± 0.8 GeV, ε = 0.0000+0.0015-0.0010

## Slide 19
High precisions at ttbar threshold
 | Dmtop | DGtop | Dltop/ltop
TLEP | 10 MeV | 11 MeV | 13%
ILC | 31 MeV | 34 MeV | 40%
stt
p@max
AFB
mtop = 175 GeV
M. Martinez and R. Miquel, 2003
-
-
Scan of the tt threshold
  Observables stt, AFB and <p@max> sensitive to mtop , Gtop , and ltop (ttH Yukawa coupling)
    Experimental precision for ILC with 100,000 tt events
      No beamstrahlung and 500,000 tt events at TLEP
    Expected sensitivity for TLEP (full study to be done) and ILC
Study made for TESLA

## Slide 20
Possible future large scale accelerators to address PP frontiers
FCC-ee (TLEP) in
80-100 km tunnel
LEP/LHC
Linear e+e- Colliders
(ILC, CLIC)
gg Colliders
(SAPPHIRE, SILC, CLICHE, HFiTT )
Muon Colliders
(n-Fact. as possible 1st step
Circular e+e- Colliders
(TLEP, super TRISTAN, CEPC…)
~14kH/year
~400kH/year (4 det.)
~10kH/year
~10kH/year (2det.)
From electroweak high precision tests to Higgs studies
<1 TeV
~160 GeV
~126 GeV
up to 400 GeV
Higgs Factories
laser~5J,
~100kHz
m +
m -
H

## Slide 21
Recommendations from European Strategy Group (cont’d)
Recommendation #2
High-priority large-scale scientific activities (2)
d) To stay at the forefront of particle physics, Europe needs to be in a position to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update, when physics results from the LHC running at 14 TeV will be available.
CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.

## Slide 22
CPEC
  Pre-study, R&D and preparation work
    Pre-study: 2013-15
      Pre-CDR by the end of 2014 for R&D funding request
    R&D: 2016-2020
    Engineering Design: 2015-2020
  Construction: 2021-2027
  Data taking: 2028-2035
SppC
  Pre-study, R&D and preparation work
    Pre-study: 2013-2020
    R&D: 2020-2030
    Engineering Design: 2030-2035
  Construction: 2035-2042
  Data taking: 2042 -
A 50-70 km tunnel is very affordable in China NOW
Slides from Yifang Wang (IHEP director)
CEPC+SppC
« The FCC in China »
Contact with IHEP/Tsinghua has been established. Agreement to joint effort on specific physics and TPC studies

## Slide 23
FCC Design Study : 100km Circular (pp, ee, ep) collider
FCC DS is huge a WP with EC funding and WP without EC funding
a number of partners for H2020 part will be limited
For these topics, Working Groups are being set up, each WG being divided in sub-groups
Kick-off meeting of the FCC was held on February 12-14, 2014

## Slide 24
Overall coordination: A. Blondel, P. Janot
  Discovery through precision measurements, rare, or invisible processes.
  Develop the necessary tools Understand the experimental conditions
  Set constraints on the possible detector designs to match statistical precision
Electroweak Physics at the Z pole
R. Tenchini
Di-boson Physics mW measurement
R. Tenchini
H(126) Properties
M. Klute
K. Peters
Top Quark Physics
P. Azzi
QCD and gg Physics
D. d’Enterria
P. Skands
Flavour Physics
S. Monteil
New Physics
M. Pierini
C. Rogan
Detector Designs
A. Cattai
G. Rolandi
Experimental Environment
N. Bacchetta
Offline Software
P. Janot, F. Gianotti
B. Hegner (PH-sft)
Online Software
C. Leonidopoulos
Synergy with FCC-hh
Coordination with accelerator team
(Wenninger, Burkhardt, etc)
Synergy with linear collider detectors
Example of breakdown of the working group on lepton collider
Periodic Workshops and vidyo meetings are organized

## Slide 25
Performance requirements
and experimental challenges
Detectors layout, R&D and technologies
important to maintain flexibility at
this stage
synergies with FCC-ee, ILC and
CLIC being established
Detector-machine
interface issues
Main physics goals
High-precision studies,
may require dedicated
experiments
FCC-hh, a very versatile facility?
ideas for experiments of different types (collider, fixed target),
maintain flexibility in e.g. injector system
Example of breakdown of the working group on hadron collider
F. Gianotti, M. Mangano

## Slide 26
Study timeline
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Explore options
“weak interaction”
Report
Study plan, scope definition
Workshop & Review
 contents of CDR
Release CDR
Workshop & Review: identification of baseline
conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Elaboration,
consolidation
H2020-DS submission

## Slide 27
WP4: High-field Accelerator Magnet Design FCC-hh
Magnet design
Field quality evaluation and comparison
Field optimisation for DA maximum
WP3: Arc design FCC-hh
Arc lattice design
Dynamic aperture evaluation
Impedance calculations and instabilities
SR: photo-electrons and e-cloud effect
Aperture and field quality specifications
WP2: Interaction region design FCC-hh
IR and final focus design
MDI
Shielding and FF quad protection
Beam parameters
Collimation requirements
Beam-beam
WP5: Beam pipe design FCC-hh
Vacuum design
Beam screen optimisation
Beam screen coating
Cryogenics integration
Prototype production
Performance measurements
WP1: Management, Coordination, Implementation & Costing
Coordination & Outreach
Realization aspects
WP6?: IR&beam-beam FCC-ee
FCC EU DS Status – DRAFT
Implication de l’IRFU à l’étude
Implication de l’IRFU à l’étude

## Slide 28
Involvement of IRFU in FCC
Both for FCC-hh and FCC-ee , the areas of interest cover
Physics Studies , Detector Studies, Accelerator Studies
Physics Studies
FCC-hh
FCC-ee
Measured parameter | Method | Energy (GeV)
 |  | 240
 | ) | 
 | ) | 240
 | ) | 240
 | ) | 240
 | ) | 
 | ) | 
 | ) | 126
 |  | 126
mt , Gt , | , , | Scan 350
Measured parameter | Method | Energy (GeV)
 |  | 240
 |  | 240
 |  | 240
 |  | 240
 |  | 126
 |  | 126
 |  | Scan 350
The physicists are mainly interested to study the mass reach at FCC-hh for BSM particles : SUSY and heavy resonances in di-lepton, or multi-boson final states.

## Slide 29
Involvement of IRFU in FCC
Nn at FCC-ee (240 GeV)
Combined (ZZ, ZH) precision potentially lead to dNn= 0.006
gZ events potentially lead to dNn= 0.001
LEP measurement :
n
n
n
n
n
n

## Slide 30
Involvement of IRFU in FCC
Detector study
FCC-hh
FCC-ee
Capitalizing on IRFU’s experience in LHC, we propose to participe to the studies for the magnetic configuration and magnet layout of the FCC-hh detectors.
Comparative studies of the solenoid options with passive and active shielding.
Study of the a large toroid option.
This may be useful for the FCC-ee detectors
Study of the operability of a TPC for a FCC-ee detector
Two important issues have to be studied
1) Ions
Primary ions
Back flow of ions
2) Low power electronic
Minimization of material in the end plates
A contact at SACM is needed to define the possible studies

## Slide 31
Involvement of IRFU in FCC
TPC for FCC-ee
There is a believe that TPC is the ideal detector for e+e-. Certainly TPC have been used with success at LEP and LHC (ALICE)
Minimum of material
For excellent tracking capability (large number of measured points)
Some PID with de/dx (5% resolution)
Capitalization of studies done at IRFU (T2K/ILC) using micromegas
Possible synergies with linear collider studies (ILD)
But cannot be used in all environments!
Rin : 229 mm
Rout : 1808 mm
Lz : 2×2350 mm
B=4 T
sR-f ~100 mm
sR-Z ~500 mm
dp/p2 = 8 x 10-5 (full tracking : 2 x 10-5)
Most demanding conditions @ Z-pole
~33 kHz Bhabhas
~17 kHz of hadronic events with <mult.> ~20 (~1 evt / 60 μs avg)
Total drift time ~50ms
On average < 1 evt drifting in TPC
2-hit r-z resolution is 8 mm (160 ns drift time) a evt mixing is negligible

## Slide 32
Involvement of IRFU in FCC
TPC for FCC-ee : ions are the main issue
Primary ions
Secondary ions
With high evt rate TPC is filled with primary ions
Preliminary calculations for Z-pole operation
0.70*109 Ions (B=3.5 T)
(0.66*109 @ ILC dominated by beamstrahlung g-g events; non-issue @ FCC-ee)
Maximum distorsion
8.5 mm (negligible)!
FCC-ee
0.4 1.8
r(m)
We need
To improve simulations for FCC-ee environment
To carry out an R&D programme for measuring these effects
Secondary ions are a serious issue. May in principle be gated but one needs
Study gating feasibility in FCC-ee conditions
Calculate the impact on resol.
Verify with test
Support from SEDI needed (~0.2 FTE/y)

## Slide 33
Involvement of IRFU in FCC
TPC: Electronic power consumption
Typically, the present power per channel for high rate operation is 30-40mW. With 1 x 4mm2 pads one gets 7-10kW/m2
This is manageable but requires but significant (excessive?) material will be needed to evacuate such a heat load. ILC solves the issue with power pulsing, not possible @ FCC-ee.
Other possible studies
Conceptual architecture study to reduce consumption by factor 10
We would need the help of an electronicien (0,2 FTE/year)
Comparative study of options for calorimetry and optimization for FCC-ee requirements of resolution/operability/cost
Investigation of wireless powering and data transmission

## Slide 34
Involvement of IRFU in FCC
Accelerator study
Design of the arc lattice , e.g.
  Dynamic aperture evaluation
  Aperture and field quality specifications
High-field Accelerator Magnet Design e.g.
  Magnet design
  Field quality evaluation, comparison and optimization
IRFU has expertise on Beam Dynamics and SRF system
However, no commitments can be taken at this point. We propose to follow-up the developments for a possible contribution at a later stage.
We propose to play a leading role in these areas.
FCC-hh
FCC-ee

## Slide 35
Funding
The R&D for TPC related issues requires material cost
  Cosmic telescope for test bench
  Modification of cylindrical TPC end plate
  Development of an ion generation system based on UV flashes
  Test with magnetic field (cost not included) probably in 2015
Many studies require simulation/calculation studies i.e. physicists / engineer time
2014 request: 30 K€ (12+8+10)
It also requires travels for discussions/meetings/workshops
2014 request: 20 K€ +(2k€ for co-organizing a workshop in Paris)
2015 estimation: 50 K€ (30 for travels + 20 for R&D)
2016 – 2017 : will depend on studies in 2014-15 and new studies/R&D ideas

## Slide 36
Conclusions
FCC (hh, ee) is a very exciting project and addresses these frontiers in a very efficient way
High precision and High energy frontiers have to be overcome to explore and understand further the fundamental law of the universe
FCC (hh, ee) design study is in line with the highest priority of the European Strategy after the LHC
There is a strong interest to FCC from IRFU’s physicists.
We have periodic FCC-Saclay meeting with many contributions (see http://tlep-saclay.extra.cea.fr/ )
We propose to participate in this project an IRFU group to
  Physics Studies
  Detector Studies
  Accelerator Studies
We are already actively contributing to the project in several ways :
- Workshops/vidyo-meeting
  TLEP workshops (3rd, 5th, 6th ) : R. A.
  Kickoff meeting: Ph. Schwenling
  Vidyo meetings : R. A., S. Ganjour, E. Locci, Ph. Schwemling
  Publications (see http://arxiv.org/abs/arXiv:1308.6176 )
  Development of the H2020-DS proposal

## Slide 37
Backup

## Slide 38
Increase beam current a protect SC dipole (diffracted protons)
Reduce beam size at IP a Larger aperture quads near IP
Protect Electrical Distribution Feedbox’s (DFBX)
Improve and adjust the luminosity with beam overlap control
8T-15m (20 magnets) a 11T-2x5.5 m dipoles
Change Quadrupole Triplets a 140T/m, 150mm (13T, 8m)
a 2100 kA ~500m HTS links
a SC RF «Crab» Cavity, for p-beam rotation at fs level!
All this work is essential for precision measurements and is a first step toward higher energy
13-14 TeV
L= 5 1034 cm-2 s-1

## Slide 39
K; Oide
Continuous High luminosity
The « revolution » of circular e+e- colliders
The Top up scheme
8x1035@superKEKB

## Slide 40
Improve further the consistency tests of the Standard Model
…Why e+e-…
Moriond EW ’12
Standard Model
Z pole measurements
Affects Z lineshape, Asymmetries, Cross section, Decay Rates…
µ Mt²
µ ln(MH)
Direct mW, mtop
measurements
MW= 80.385 ± 0.015 GeV
Mt= 173.5 ± 1.0 GeV
Need to improve
Measurement @Z-pole
Mw and Mt ( @threshold)
MH
MH= 93 ± 26 20 GeV

## Slide 41
Polarization at circular colliders
e-(e+) spin naturally align along dipole magnetic field
Transverse polarization builds up by synchrotron radiation emission (or if needed using wigglers)
Transverse to longitudinal polarization is achieved with Spin Rotators
Resonant depolarization is achieved with small field (perpendicular to dipole field) RF-magnet with frequency in phase with precession frequency. (Precession period is proportional to beam energy)
Depolarizing RF-magnet frequency measures beam energy with <0.1 MeV
RF-m
B^

## Slide 42
High precisions at Z-pole
Many other measurements would benefit from Tera-Z production
Channels | Production/year | Physics
t+t- | 3 1010 pairs | Rare decays, conservation laws…
c or b quarks | > 2 1011 | CP violation, rare decays…
 | e.g. > 3 1010 Bs | Large Bs sample with clean environment within SM, > 1000 Bs g t+t- detected
SM
Complement to Bs g m+m- for NP search
Example of non-SM
… or any NP loop process favoring 3rd generation

## Slide 43
High precisions at H threshold
Sub % sensitivities on couplings to Higgs are highly desirable to probe new physics at and above the TeV scale

## Slide 44
 | LHC(300) | LHC (3000) | ILC (250+350) | TLEP (240+350) | Comment
DmH (MeV) | ~100 | ~50 | ~30 | ~7 | Overkill for now
DGH/GH (DGinv) | --(14) | --(7) | 6(2.9)% | 1.0(0.45)% | 
H spin | P | P | P | P | 
DmW (MeV) | ~10 | ~10 | ~7 | <0.5 | Theo. limits
Dmt (MeV) | 800-1000 | 500-800 | 31 | 10 | ~100 from theo.
DgHVV/gHVV | 4-7%* | 2%* | 0.5-14.5% | 0.15-1.5% | 
DgHff/gHff | 6-13%* | 2- 7%* | 2-2.5% | 0.2-0.7% | 
DgHtt/gHtt | 14%* | 7%* | ~40% | ~13% | 
DgHHH/gHHH | -- | ~30% | 44%** | -- | Insufficient ?
**Sensibility with 2ab-1 at 500 GeV
*Assuming systematic errors scales as statistical and theoretical errors are divided by 2 compared to now
Do we have the technology to carry out these measurements?
Could be significantly improved at VHE-LHC

## Slide 45
Sensitivity to Higgs Coupling at TLEP using data at 240 GeV (5 years, 4 detectors)

## Slide 46
Project | Beam Type | RF freq. (MHz) | Beam Power (MW) | Pulse length (ms) | # cavity | Gradient (MV/m)
ILC 250 | elect. | 1300 | ~8 | 727 | 8000 | 31,5
CLIC 3000 | elect. | 12000 | 14 | 0,155 | 30000 | 100
TLEP | elect. | 700-800 | 100 | CW | 600 | 20
VHELHC | prot. | 400 | 2 | CW | 16 | 2
RF system needs
Selected Future Projects
We do have the technologies for Higgs factories and Energy frontier up to TeV scale with e+e- and 60 (100) TeV with pp colliders
We do not have the technology for multi TeV (>5) lepton colliders
m collider or « plasma acceleration » colliders may be the solution but many issues to be solved

## Slide 47
Possible future large scale accelerators to address PP frontiers
superB e+e- Factory
… and Flavor physics …
L=8 1035 cm-2 s-1
>1010 B/year
SuperKEKB
Multi-MW
SC cavities
5-10 GeV
n,m
Goal: >1021 m/y stored
Fast
accumulator
target/horn station
ν
Flavor Factories
ESS based 5MW p-beam
n super Beams (T2HK, LBNE, LNBO…)
1.6x1016 pot/s

## Slide 48
FCC-ee tentative timelines (personal) | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043
CDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TDR +R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R&D + Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Physics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FCC-pp tentative timelines (personal) | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043
CDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TDR +R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R&D + Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Physics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Delivery of CDR and European Strategy update