## Slide 1
Advanced methods & concepts
for very high intensity beams
P. A. P. NGHIEM
N. CHAUVIN, M. COMUNIAN, L. DUCROT, C. OLIVER
W. SIMEONI Jr., M. VALETTE, D. URIOT

## Slide 2
What is HIGH intensity ?
Only in the sense of comparison:
Beam A intensity is higher than Beam B intensity
Only makes sense if
higher intensity  higher issues to face
Issues to be analyzed are twofold:
High intensity
High power
Strong
space charge
- even tiny losses
are harmful
- ….
- strong nonlinear
repulsive forces
- …
Combination of the two issues  particularly critical situation

## Slide 3
Final
Beam analysis (1)
Classically: assimilation to high power
Final
Power
Example of three accelerators:
Average, peak intensity; startingfinal energy
- Accel A: 125 mA, 125 mA; 0.1  40 MeV
- Accel B: 8 mA, 10 mA; 0.05 1500 MeV
- Accel C: 40 mA, 0.8 mA; 0.03  600 MeV
This graph is highly reductive:
● Only last section, no upstream sections
- Each energy range ↔ specific acceleration-focussing technologies
Source, LEBT, RFQ, DTL, CCL, SC-HWR, Spoke cav, Elliptical cav
- Challenges are not comparable at very different energies
- Challenging last section doesn't mean challenging upstream sections
The most challenging : Accel B, then A, then C ???
● No space charge
- need of strong focusing
- non-linearities
- emittance growth
- halo creation
- sudden losses

## Slide 4
Beam analysis (2)
Beam power issues
Only last section: B, A, C
For a given section: A, B, C
Space charge issues
Only first section: C, A, B
For a given section: A, C, B
RFQ end
RFQ end
Advanced analysis:
Beam power & Space charge along the accelerator
(average & peak intensity, start & final energy)
Direct comparison between accelerators
for a same acceleration component
⇒ challenging or not
⇒ adjust section start/end could help
⇒ see effects of combination of
high power & space charge

## Slide 5
Examples of accelerators achieved or under construction or planned
Classically
Advanced
Beam analysis (3)
Nucl. Instru. Meth. Phys. Res. A 654, 63–71, 2011

## Slide 6
Advanced methods and concepts
New idea for: Beam analysis
New protocol for: Beam loss prediction
New method for: Beam optimization
New strategy for: Beam measurement
New concept for: Beam characterization

## Slide 7
Advanced methods and concepts
New idea for: Beam analysis
New protocol for: Beam loss prediction
New method for: Beam optimization
New strategy for: Beam measurement
New concept for: Beam characterization

## Slide 8
Beam loss prediction (1)
High power  even a tiny part of the beam, when lost,
can take away a significant power
High intensity  High power on almost the whole accelerator
 Carreful and exhaustive prediction of losses
all along the accelerator is needed
● Accidental loss  brutal heat deposition  damage equipment
● Permanent loss  activate materials  harmful radiations for personnel
 cryogenic systems must be able to cool down
Hands-on maintenance requirement: Losses << 1W/m
MW beam  well less than 1 particle lost over 106 is tolerated !!
 microlosses

## Slide 9
Beam loss prediction (2)
Double issue:
- Define exhaustively all the loss situations in the accelerator lifetime
- Define the protocols to simulate and estimate them
Loss situations and protocols: (Laser Part. Beams (2014), 32, 461-469)
A. Ideal machine: nominal theoretical conditions, without any error
B. Starting from scratch: errors as tolerances, not corrected, tunable param.±10%
C. Commissioning, tuning, exploration: same as above but errors corrected
D. Routine operation: errors corrected, tunable param. nominal
E. Sudden failure: individual or combination of sudden trips of tunable param.
from 100% up to 110%, or down to 0%.
 CATALOGUE of LOSSES:
affects all the subsystems: hot points, beam stop system velocity,
limitations for control system, maximum beam power for operation,
dynamic range of diagnostics, etc.

## Slide 10
Beam loss prediction (3)
Example: CATALOGUE of LOSSES for the IFMIF Prototype accelerator
Laser Part. Beams (2014), 32, 461-469
Beam loss power probabilities when starting from scratch for a full power beam
Beam loss power in case of sudden failure of the second LEBT solenoid

## Slide 11
Advanced methods and concepts
New idea for: Beam analysis
New protocol for: Beam loss prediction
New method for: Beam optimization
New strategy for: Beam measurement
New concept for: Beam characterization

## Slide 12
Beam Optimization (1)
Classically:
Global parameter: rms Emittance
Minimize emittance growth
Emittance matching
Halo may be indirectly minimized
What are the parameters to be optimized ?
Emittance : figure of merit
But: MW beam microlosses
10-6 of the beam must be avoided
 very external part
 halo
Advanced:
Extension of the outermost particles
Minimize directly the halo
Halo matching
Maximize margin between
beam border and pipe wall
Halo: figure of merit
Results:
comfortable margin between
beam external border
and beam pipe wall

## Slide 13
Beam Optimization (2)
Classically: Emitt. matching
Advanced: Halo matching
1 particle over 106
Example: IFMIF SRF Linac (Laser Part. Beams 32, 10-118, 2014)

## Slide 14
Beam Optimization (3)
Classically: Emitt. matching
Advanced: Halo matching
1 particle over 106
Example: IFMIF SRF Linac (Laser Part. Beams 32, 10-118, 2014)

## Slide 15
Issue: The beam must be optimised to an accuracy of 10-6
But simulations are not reliable to that accuracy
components are not reproducible to that accuracy
 Frequent in-situ fine tunings are mandatory
Perform only Beam Dynamics optimizations
that could be reproduced in-situ on the real machine
with the appropriate Beam Diagnostics
in sufficient quantities
STRATEGY: SELF-RULE
In other words:
Each BDyn tuning procedure MUST have its in-situ Avatar on the machine
Beam Optimization (4)

## Slide 16
… to the RFQ
Optimization
Not to fulfill theor.Twiss param.
But to maximize RFQ transmission
… to the SRF Linac
Optimization
Not to minimize RMS envelope, emittance
But to minimize micro-losses
Diagnostic
Current measurements at
RFQ entrance and exit
Diagnostic
Micro-loss measurements
the closest to solenoid vacuum chamber
Beam Optimization (5)
Examples of beam matching …
Enough independent diagnostics:
at least the same number as that of available tuneable parameters
Rev. Sci. Instru. 83, 02B320, 2012 Proc. of PAC. Vancouver, BC, Canada, 2009

## Slide 17
Advanced methods and concepts
New idea for: Beam analysis
New protocol for: Beam loss prediction
New method for: Beam optimization
New strategy for: Beam measurement
New concept for: Beam characterization

## Slide 18
Beam Measurement (1)
Strong non-linear effects
High sensitive settings
Delicate optimisations
Lack of space for installing
diagnostic devices
B Dyn simulations are not precise at the level of 10-6 !
Machine tuning based on beam diagnostics is mandatory
Diagnostics not only necessary for beam characterization
But also critical for achieving targeted performances
Strong Space Charge
Compact structure
to limit beam halo,
emittance growth
High Power
Losses << 10-6
High intercepted Power
Interceptive devices not possible
Installation of
diagnostic devices
difficult or not possible
Deposited power on diagnostic devices ~ kW
HIGH INTENSITY
Conflicting
Issues !!

## Slide 19
Beam Measurement (2)
- for commissioning & tuning & operating the accelerator
- in order to meet required specifications of current and losses
- direct impact on the achievement of accelerator specifications
- available for everyday beam tuning at full power, non interceptive
- beam position, beam phase, current, losses, micro-losses
ESSENTIAL measurements
- for beam commissioning or beam study or beam dynamics understanding
- could be measurements during beam commissioning only, if lack of room
- could be interceptive devices for low duty cycle, if pb of power deposition
- transverse profile, emittance, halo, energy spread,
- mean energy, bunch length
CHARACTERIZATION measurements
Classically: A lot of measurements, no need of sorting, classification
Advanced: clearly distinguish between

## Slide 20
Beam Measurement (3)
Measurement: with Bdiag
Correction: with corrector
Errors
Automatic
correction
algorithm
Essential:
Characterization: Knowledge, Understanding, Surveillance
Definition of the complete beam diagnostic system

## Slide 21
Beam Measurement (4)
Best mLM: CVD diamond
Best correction: PSO (Part. Swarm Opt.) algorithm
⇒ Ideally as many mLM as foc. elements upstream (one-to-one correspondence)
⇒ Located at foc.elements where loss probability is the highest,
and the closest to the beam to allow locating losses
Performances: resolution 1/10 of maximum allowed losses
1 macroparticle over 106
Example of essential diag: Microloss monitors for IFMIF
(Proc. of DIPAC11, Hamburg, Germany)
(Proc. of PAC09, Vancouver, Canada)

## Slide 23
Advanced methods and concepts
New idea for: Beam analysis
New protocol for: Beam loss prediction
New method for: Beam optimization
New strategy for: Beam measurement
New concept for: Beam characterization

## Slide 24
Beam Characterization (1)
Classically
106 particles in 6D phase space
 6 106 parameters
 very big number  num. simulations
Concentration ellipse
RMS e, a, b (,g)
 3 global parameters
High intensity
109 particles in 6D phase space
 6 109 parameters
 huge number
RMS e, a, b (,g)
Not enough !!

## Slide 25
Beam Optimization (3)
Smaller emittance: Bigger size
Bigger emittance: Smaller size
Example: IFMIF SRF Linac (Laser Part. Beams 32, 10-118, 2014)

## Slide 26
HEBT entrance
exactly same a,b,g,e
3.5 m downstream
through 3 quadrupoles:
significantly different beam outputs
a,b,g,e
"Nominal" distribution
Gaussian distribution
Beam Characterization (2)

## Slide 27
Two different beams...

## Slide 28
e = 3.30, a = -0.40, b = 0.95
e = 3.30, a = -0.40, b = 0.96
Same Emittance but different Halos

## Slide 29
Example: Beam along the IFMIF prototype accelerator

## Slide 30
Beam Characterization (4)
Advanced:
1) Massive simulations with the actual number of particles
5 109 particles (125 mA) for IFMIF-LIPAc (WEPOY032, IPAC'16)
 175 processors for 25 days
 confirm losses < 10-7
 representative statistics of microlosses
2) Characterize the beam by its projections onto a few axes
3) Characterize the beam by its core and halo separately
MENT method: reconstruct a distribution from its projections (MOPOR032, IPAC'16)
Projection axes correctly chosen
 2 projections for the core
 6 projections for the external parts
 ~ 10 - 30 parameters for 2D
2 projections
6 projections
Actual distribution
Loose fine details but gain more insight into the physics of the beam

## Slide 31
Beam Characterization (5)
We propose: Core-Halo limit based on the beam internal dynamics
Extreme case:
Core: uniform, sc force strictly linear
Halo: tenuous, sc force nonlinear
 core-halo limit: very steep (infinite)
variation of the slope
General case:
Continuously varying density
Core-Halo limit: steepest variation of
the slope  max of 2nd derivative
 Core & Halo are submitted to two
different space charge force regimes
Appl. Phys. Lett. 104, 074109, 2014
Phys. Plasmas 22, 083115, 2015: This core-halo limit ≡ good indicator of beam internal dynamics

## Slide 32
Beam Characterization (6)
Example: Beam along the IFMIF prototype accelerator

## Slide 33
Beam Characterization (8)
Example: Beam along the IFMIF Prototype accelerator
Classically
Advanced
PHS
PHP

## Slide 34
Beam Characterization (10)
MOPWA010, IPAC'15: Extension to 2D
"Wheel algorithm": Max of second derivative
along many sections
Core-Halo limit contour
PHS, PHP
Emittance e and Twiss parameters a, b, g
of the core and the halo separately
THPMR014, IPAC'16:
This Core-Halo limit contour is consistent
with the well-established halo formation dynamics

## Slide 35
Beam Characterization (11)
Classically
Advanced

## Slide 36
Summary
High intensity
High power
Strong space charge
Combination of the two aspects  new and serious issues
Advanced methods and concepts:
Catalogue of Losses, Halo matching, online Avatar of BD optimization,
Essential and Characterization diagnostics, Core-Halo limit, PHS, PHP
For the five purposes of:
Beam analysis, beam loss prediction, beam optimization
beam diagnostic and beam characterization
Laser Part. Beams 32, 639-649, 2014

## Slide 37
Extra

## Slide 38
Two different beams...

## Slide 39
e = 3.30, a = -0.40, b = 0.95
e = 3.30, a = -0.40, b = 0.96
Same Emittance but different Halos

## Slide 40
PHS=90.1% PHP=30.9%
PHS=28.9% PHP=3.2%
e a b
Global 3.30 -0.40 0.96
Core 3.15 -0.41 1.00
Halo 8.95 -0.46 1.00
e a b
Global 3.31 -0.40 0.95
Core 1.40 -0.39 1.01
Halo 7.56 -0.40 0.93