## Slide 1
S3 Collaboration (LoI signed by 28 laboratoires)
ANL (US), CENBG, CSNSM, JINR-FLNR, (Russia), GANIL, France, GSI (Germany), INFN Legnaro, (Italy), IPHC, France, IPNL, , Irfu CEA Saclay, IPNO, France, JYFL (Finland), K.U. Leuven (Belgium), Liverpool-U, (UK), LNS (Italy), LPSC, MSU (US), LMU, (Germany), Nanjing-U (China), Northern Illinois University (US), SAS Bratislava, (Slovaquia), IFJ PAN Cracow (Poland), Smoluchowski Institute (Poland), CEA-DAM; SUBATECH, TAMU (US), U. Mainz (Germany), York-U (UK), Vinca Institute (Serbia)
INP
S3 : Super
Separator
Spectrometer
Some Physics at (or a bit above) Coulomb Energy
from the S3 Letters of Intent

## Slide 2
Fed by the very high intensity
stable heavy ion beams
of LINAG
- He to U nuclei
- From 2 to 14MeV/u
- beyond 1pµA ( 1014pps)
S3 in Spiral2@Ganil
SPIRAL2
Phase 1
Neutron for Science
S3
Phase 1++
DESIR (low energy)
Accelerator Upgrade
Phase 2
- RIB
Present Ganil
NfS
Desir
S3

## Slide 3
Faisceau
Achromate en moment
Spectromètre de masse
Cible
Multipôles supraconducteurs
Arrêt faisceau primaire
Détection
Grande acceptance
ΔΩ = 11msr
ΔE = ±14%
5 états de charge
Double sélection
Réjection du faisceau primaire, sélection en moment
Dipôles électrique & magnétique : sélection en masse

## Slide 4
Physics objectives
Study of very rare events in nuclear and atomic physics
Nuclei produced by
Fusion-Evaporation
58Ni+46Ti100Sn +4n
(I=10pµA)  3evt/s @ σth=5nb
48Ca+238U-283112+3,4n
(I=10pµA) 20evt/week/pb
Heavy and Superheavy
Elements
Limit of the nuclear existence
Reaction mechanism
Shell correction effects
Atomic properties
Proton Dripline & N=Z nuclei
Shelll correction effects
Study the role of π-ν correlations
Deformation – shape coxistence
Exotic decay
Astrophysics rp-process
Fundamental interaction
Atomic physics
FISIC project
Ion-Ion interactions
 High Selectivity and High Transmission versatile separator-spectrometer

## Slide 5
nuclide | feature | X-section [pb] | rate [h-1] | 21UT integral | 
 |  |  |  | day 1 | phase 1++
254No | ER | 2000 | 60.000 | 6107 | 1107
256Rf | ER | 17 | 550 | 90.000 | 5.4105
266Hs | ER | 15 (270Ds) | 0.34 | 57 | 285
266mHs | K-isomer | 15 (270Ds) | 0.01 | 2.5 | 12.5
270Ds | ER | 15 | 0.45 | 76 | 380
270mDs | K-isomer | 15 (270Ds) | 0.22 | 38 | 190
262Sg | α-decay | 15 (270Ds) | 0.02 | 5 | 25
276Cn | ER | 0.5 (277Cn) | 0.01 | 2.5 | 12.5
288115 | ER | 10 | 0.3 | 50 | 300
288115 | L X-rays | 10 | 1,8 | 300 | 1800
Nuclear structure
Quasi-particle excitations  deformation/K-isomers
Alpha/gamma/electron spectroscopy
X ray spectroscopy
Reaction studies
Isospin dependent investigation
Z > 112  Actinide targets
48Ca beam and heavier
Very and Superheavy elements studies
Instrumentation
SIRIUS for Decay spectroscopy

## Slide 6
Phase 1b:
Ground state properties
(mass, size, moments, spins)
REGLIS3 setup
Low Energy
Branch
DESIR
Atomic physics
FISIC setup
Fast Ion Slow
Ion Collisions
Electron exchange
Phase 1.a : Decay spectroscopy
SIRIUS setup
Implantation-decay
station at the mass
dispersive plan
(α,e-,fission,γ)
In-beam spectroscopy
Two step reactions
EXOGAM2/AGATA
PARIS
MUST2/GASPARD
Experimental Techniques
Primary Beam dump
Secondary
Beam dump
Achromatic point
Mass
focal
point

## Slide 7: SIRIUS (Spectroscopy & Indentification of Rare Ions Using S3)
Large size (200x150 mm2)
Time Resolution < 1ns
Position resolution = 1mm
Very low thickness
Germanium detector
e.x. Exogam2, CLODETTE
Time of flight + tracking detector
Implantation detector
(HI,  and e- decay)
Tunnel detector for escaped e- and 
Conversion electrons FWHM <5 keV
Escaped alpha FWHM 15 keV
Large detector size 10x10cm2
High resolution FWHM
  Ability to detect large> 50MeV pulse
  Followed (≈ 10µs)
  by a weak (<15MeV) pulse.
No Dead time
R&D is ending  Construction phase starts this year (CPIER funding)

## Slide 8
efficiency ( 4 %): including S3 transmission - experiments possible with I to <1 pps
selectivity: suppression of unwanted isotopes in the order of 1/10 000 - extra cleaning necessary
fast: short lived isotopes (delay time 250 ms) - trade off between efficiency and delay time
spectral resolution: down to ~200 MHz: isotope/isomer shift, spins and moments.
Expected performances of S3 LEB

## Slide 9
Zone Dispersive
Station cibles
Triplet Ouvert :
Au Ganil,
À installer...
Dipôle électrique
Électrodes au T4 de 2016
Beam Dump en cours de réalisation
Chambre station cibles stables
Profils de cibles avec canon à électrons
SMT
Phase proto :
Fin au T2 2016
Série :
→ août 2017
Equipements majeurs Phase "0" S3
Boite froide
MES : fin 2016

## Slide 10: Planning S3

## Slide 11
Beam-Dump : IRFU

## Slide 12
Section Beam Dump
Triplet chaud
Plug Amont
Plug Aval
SMT2
½ culasse triplet – avant été 2016
D11 – Fin 2016
Plugs + SMT2 – mars 2017
Salle 169

## Slide 13
Budget Beam dump
Attention : coût des translateurs en cours d’estimation

## Slide 14: Planning SMTs
Training GANIL (SDA/GAC, SDA/GVC,…)
Chemin critique

## Slide 15
Projet de référence ≤ 1015 pps, p-Ni, 0.75 MeV/n – 14.5 MeV/n
Phase 1++ ≤ 1015 pps, p-U, 0.75 MeV/n – 9 MeV/n
LINAC SPIRAL2 A/Q=3
LINAC SPIRAL2 A/Q=6 (Phase 1 ++)
Projet Haute Intensité (SPIRAL2 Phase 1++)
Renforcer le programme scientifique phase 1+
Ouvre nouvelles perspectives scientifiques
(Faisceaux lourds Xe, Pb, U)
Ions | Intensity (pµA)) [A/Q=3] | High Intensity [A/Q=6-7]
18O | 216 | 375
19F | 28,6 | 50
36Ar | 17.5 | 40
40Ar | 2.9 | 30
36S | 4.6 | 30
40Ca | 3 | 20
48Ca | 1.25 | 15
58Ni | 1.1 | 10
84Kr | 0 | 20
124Sn | 0 | 10
139Xe | 0 | 10
238U | 0 | 2.5
✕5-10
✕10x
Notes: RIB available GANIL will cover the following regions.
Very promising RIB will be available in the next future at GANIL, and if you want to get more precise beam intensity as well as the energy, please
Use the new interactive web interface has been put online
where any users can estimated the currently available and future beams at the GANIL/SPIRAL1/SPIRAL2 facility.
Regions produced with light beams (ISOL), HI beams ISOL and in-flight completed by nuclei produced with high intensity RIB of ff.

## Slide 17
Principles
Multistep selection
Large acceptance (11 msr, Δp=15%)
Mass resolution (ΔM/M ≈ 300)
Versatility (Bρmax=1.6Tm; Eρmax = 12MV)
Horizontal
300
mm
Momentum Achromat
Mass spectrometer
300
mm
Vertical
Image 1
Momentum Selection
and beam rejection
Image 2
Achromat selection
Extended drift to place detector arrays
Image 3
TKE selection
Tracewin simulation code:
Full raytracing in the multipole 3D
field maps
Automatic optimisation of 80 fields
Image 4
Δ(M/Q) ≈ 460
A=101,100,99
24+
25+
26+
23+
22+
Image 4 : Mass selection
High
Intensity
Beams
Target point
High power rotating target
Notes: The design we propose is a two-stage selection (Bρ & m/q) for very good rejection of both the beam and adjacent mass channels of reaction products
The optical design of such complex spectrometer is only possible with full raytracing sophisticated software and modern computer capabilities

## Slide 18
Physics Programs for Day 1 experiments
VHE-SHE & N=Z decay studies
S3’s niche within an intense worldwide competition
(high beam intensity capabilities, mass resolution and high transmission)
GS properties @ REGLIS3
Unique characteristics
(nuclei not available elsewhere, REGLIS ANR, high selectivity, DESIR coupling in 2018)
Well identified strategy for day 1 (day 2) experiments
Doubly magic 218U; in depth spectroscopy of Fm isotopes; bridge the gap between cold and hot fusion ; Search for isomers beyond Z=110; X-ray identification of SHE; 112Ba-108Xe -104Te super-allowed a decay
Beams: Si, Ar, 48Ca, 64Ni
Targets: 208Pb
Instrumentation: SIRIUS
new RFQ and high power source = Phase 1++
Actinides targets
In beam spectroscopy detection for N=Z
Crucial
Next steps
Beams: Ne, 40-48Ca, 58Ni
Targets: stable
Instrumentation: LEB
New RFQ and high power source = Phase 1++
New lasers @ Ganil
to the DESIR facility
Crucial
Next steps
Well identified strategy for day 1 (day 2) experiments
94Ag, 100Sn, 80Zr studies : mass, charge radius, decay characteristics for ground or isomeric states
then going to very heavy nuclei (254No)
D. Ackermann Talk
P. van Duppen Talk

## Slide 19
Ti:sa
λ-meter
gas cell
CYCLONE 110
cyclotron beam
SPIG
target
accel.
optics
dipole
magnet
detector station
collector
plates
SEM
SHG
Nd:YAG
Diode
Ti:sa
SHG
de Laval
nozzle
Rep. rate 10 kHz
Figures of merit:
Resolution ~ 5e-7
(FWHM= 400 MHz)
Selectivity ~ 200
Efficiency ~ 0.5%
First test: In-Gas-Jet Spectroscopy of 214,215Ac
R. Ferrer · LAP 2015, East Lansing, July 7-11, 2015
ionization
volume

## Slide 20: Low Energy Branch
The RFQ system (LPC-Caen, KULeuven)
PILGRIM Multi Reflection – Time of Fight –Mass Spectrometer
Tests experiment: Laser scans of 212-215Ac in-gas cell laser spectroscopy experiments at LISOL facility (Louvain-La-Neuve).

## Slide 21
From the study of elementary processes
to damage in materials and ion energy transfer in plasmas
vp
Zp
Zt
capture
excitation
ionization
Stellar plasmas
inertial confinement plasmas
stopping power and ion-plasmas interaction
FISIC (Fast Ion — Slow Ion Collision)
FISIC*: a collider project on SPIRAL2/GANIL for Atomic Physics of ion-ion collisions
All the elementary processes have  max and of the same order of magnitude
Investigations of ion-ion collisions
“clean plasmas” with well known charge states
Ability to investigate a large variety of systems
Possibility to easily scan the charge state dependence
[E. Lamour]
Primary beam
+Q
Low
Energy
Beam
+q
Detection
of q+/-1
Detection
of Q-/+1
Notes: Thoses processes are strongly correlated to damage in materials and to ion energy transfer at various plasma conditions such as…