## Slide 1: MARCO, the solenoid for the ePIC detector at EIC
Valerio CALVELLI (CEA/IRFU) On Behalf of EIC Detector Magnet team
2022-10-14

## Slide 2: Outline
The EIC and the Detectors forecast
Why MARCO
Design Requirements
Magnetic Design
Conductor Design
Mechanical Design
Cryogenics Design
Protection Studies
Conclusions
TEAMS & CONTRIBUTORS
R. Rajput-Ghoshal, S. Gopinath, P. Ghoshal, E. Sun, D. Young, K. Hall, R. Ent, M. Lainey, J. Tenbusch
E. Aschenauer, R. Sharma, R. Wimmer, T. Lewis, R. Than
V. Calvelli, H. Reymond, F. Stacchi, F.P. Juster, M. Segreti, C.Berriaud, D. Simon, J.P. Lottin, L. Boccardo, L. Quettier

## Slide 3
The Electron – Ion Collider
Design based on existing RHIC
Hadron storage ring 40-275 GeV (existing)
Electron storage ring (2.5–18 GeV (new))
Electron rapid cycling synchrotron (new)
High luminosity interaction region(s) (new)

## Slide 4
ePIC
ATHENA
ECCE
ATHENA | 
Location | IP6
Detector Length | 9.5 meter
Magnet Field | 3 Tesla
Magnet Bore | 3.2 meter
Magnet Length | 3.6 meter
ECCE | 
Location | IP6 (or IP8)
Detector Length | 8.5 meter
Magnet Field | 1.5 Tesla
Magnet Bore | 2.8 meter
Magnet Length | 3.51 meter
94 institutions (CEA included)
96 institutions
Not recommended due to the high costs but discussions are ongoing
it has the best performances
UE countries contribute for 1/3
Approved in March 2022
Only US & Asia countries + Orsay
ePIC
ePIC | 
Location | IP6
Detector Length | 8.5 meter
Magnet Field | 1.7 Tesla
Magnet Bore | 2.8 meter
Magnet Length | 3.51 meter
160 institutions (CEA included)
Approved and financed in September 2022

## Slide 5
Why MARCO?
ECCE
Reuse of BaBar @ 1.4 T
25y operative life + 30y of operation forecast
Sensors problems
New solenoidal magnet @ 1.5 T for replacement as contingency plan
ePIC
New solenoidal magnet @ 1.5 T (minimum), possibly 2.0 T
Waiting for approval
MAgnet with Renewed COils

## Slide 6: The Requirements
Geometric
- Must fit into BaBar’s volume
Magnetic
B @ IP = 1.5 T to 2.0 T
Field Uniformity < 12.5%
Projectivity < 10 T/Amm-²
Transparency
- Thickness / interaction length < 1
Stray field
B < 10 G in the focalising magnets zone

## Slide 7: Geometric Requirements
Parameter | Value
Coil length | 3512 mm
Warm bore diameter | 2840 mm
Cryostat length | < 3850 mm
Cryostat outer diameter | < 3540 mm
MARCO must fit into BaBar’s Volume
We adopted BaBar’s cryostat dimensions as reference
MARCO Cryostat preliminary design
MARCO Cryostat surrounded by the supporting mechanical structure of ePIC

## Slide 8: Magnetic Field Requirements
Parameter | Value | Comment
Central Field B0 | 0.5 T 1.5 T 1.7 T 2.0 T | Lowest Safe operation Optimal Reachable
Field Uniformity in FFA | 12.5 % ± 100 cm around center 80 cm radius | 
Projectivity in RICH Area | < 0.1 (mrad@30GeV/c) < 10 T/A/mm² From Z = 180 cm To Z = 280 cm | 
Parameter | Value | Comment
Central Field B0 | 0.5 T 1.5 T 1.7 T 2.0 T | Lowest Safe operation Optimal Reachable
Field Uniformity in FFA | 12.5 % ± 100 cm around center 80 cm radius | 
Projectivity in RICH Area | < 0.1 (mrad@30GeV/c) < 10 T/A/mm² From Z = 180 cm To Z = 280 cm | 
Lepton HCAL
Hadron HCAL
Barrel HCAL
sPhenix iron yoke
FFA
If protons of 30 GeV/c stay within a cone of 1 mrad (plus incertainties)
1 mrad

## Slide 9: Stray Field Requirements
Lepton HCAL
Hadron HCAL
Barrel HCAL
B7400
B3400
B5300
sPhenix iron yoke
Parameter | Value | Comment
B5300 (B @ Z= -5300 mm) | < 10 G | Stray field requirement is based on IR magnet location
B7400 (B @ Z= 7400 mm) | < 10 G | 
B3400 (B @ R= 3400 mm) | < 10 G | 
These requirements depend on the magnet and the iron yoke around it

## Slide 10
Interaction Length Limits
Mean range
(Bethe equation)
Stabilizer material for conductor
Copper
Aluminium
3x less stopping power with the same coils dimensions and NbTi fraction in the cable if Aluminum is used
TRANSPARENCY for the transverse momentum
Aluminum stabilized for detector magnet
NbTi Rutherford Cable
Pure aluminium
Doped aluminium
Aluminium alloy
No existing extrusion line in the world
Conclusions from Workshop on Superconducting Detector Magnets @ CERN, 12/14 Sept 2022
We will not be able to use Aluminum stabilized conductors for long long time

## Slide 11
Interaction length optimization
& MARCO Layout
Material | Thickness/Nuclear interaction length |  | 
 | BaBAR 1.4 T | Marco 1.5 T (4 layers) | Marco 2T (6 layers)
Al | 0.382 | 0.113 | 0.113
Cu | 0.011 | 0.114 | 0.166
SS/Brass | 0.000 | 0.136 | 0.181
NbTi | 0.007 | 0.003 | 0.008
G10 |  | 0.009 | 0.028
Total | 0.400 | 0.372 | 0.468
How could we achieve that?
 | Copper
 | NbTi/Cu
 | Brass
 | G10
 | Fiber-glass
RIC: Rutherford cable In Copper Channel
RIC conductor for Iseult (MRI magnet)
  Designed at CEA Saclay
  Cable insertion by Luvata at Waterbury*
*The insertion line still exists !
33.6 mm
30 mm
mandrel
Winding on the large side reduce the thickness of the coil
Copper has wonderful mechanical properties!
Normal winding side
Increase the mechanical inertia

## Slide 12
Iron Yoke evolution
Version 0
Version 1
Version 2
Asym case
100 % iron
Sym case
Different iron
Used for all the analysis except for the stray field
ePIC
Iron yoke is evolving according to the physics needs
It has a moderate impact on the magnet
But
It has a strong impact on the stray field
sPhenix / ECCE
Interaction with the Physics groups ongoing

## Slide 13
Iron Yoke layout
Lepton Hcal composition
32 assembled and tested sectors - 1.9m inner radius, 2.6m outer radius
10 rows of 8mm scint. tiles (24 tiles per row), 12o tilt angle
Tapered 1020 steel plates ~26.1mm - ~42.4mm
Barrel Hcal composition
Hadron Hcal composition
Iron fraction = 75.0 %
Iron fraction = 87.5 %
Iron fraction = 70.0 %
Versions largely vary for shape and dimensions, but the iron fraction not

## Slide 14
Marco Magnetic Design Results
Value | 1.5 T | 1.7 T | 2.0 T | Units | Criterion
Current | 2900 | 3296 | 3924 | A | 
B0 | 1.500 | 1.704 | 2.023 | T | 2.0
Bpeak | 1.925 | 2.187 | 2.602 | T | 
Energy | 25.050 | 32.344 | 45.732 | MJ | 
Energy mass density | 1.5 | 1.9 | 2.7 | KJ/Kg | 
Energy mass density | 11.636 | 15.024 | 21.243 | MJ/m3 | 
Uniformity | 12.3 | 12.3 | 12.3 | % | < 12.5%
Projectivity | 1.806 | 2.047 | 2.408 | T/Amm² | < 10
MARCO respects the criteria on
The magnetic field at center
The uniformity
The projectivity
Homogeneity region
RICH Projectivity
B field along Z axis
1.72 T
2.08 T
Chart: Z (mm)

## Slide 15
Impact of the Yoke
Version 0
Version 1
Version 2
ePIC
sPhenix / ECCE @ 2.0 T
-11 kN
-458 kN
-172 kN
-296 kN
Parameter | Value
B5300 | 61.8 G
B7400 | 37.2 G
B3400 | 61.5 G
Parameter | Value
B5300 | 33.5 G
B7400 | 20.2 G
B3400 | 9.4 G
Any of the proposed configurations satisfies the criteria on the stray field.
Why?
MARCO is moved of 10 cm towards the Lepton HCAL
Lepton HCAL
Hadron HCAL
Barrel HCAL
Asym cut
Sym cut
Version used for MECH analysis

## Slide 16
Impact of the Yoke – Version 2
Need to close these holes
Flux lines escaping from the barrel
Need to increase the dimensions
Need to close these lines before
7400
5300
3400
We need a lot more of iron for this yoke configuration

## Slide 17
Yoke – Version 3
Lepton HCAL moved of Δz = - 679 mm
Distance between Barrel HCAL and Iron Yoke = 8 mm as indicated by BNL
Outer radius = 3262 mm
Parameter | Value
B5300 | 15.1 G
B7400 | 8.8 G
B3400 | 1.5 G
FZ | +37 kN
37kN
Possible solutions to reduce B5300:
- Local yoke around the holes
Under discussion with BNL

## Slide 18
Conductor definition (6 layers)
 | Parameters | Values | Units
Strand | Strand diameter | 0.7 | mm
 | Cu/NbTi | 1.3 | 
 | Ic @ 2.6T & 4.7K | >680 | A
 | Filament diameter | <70 | µm
 | RRR Cu | >80 | 
Cable | NbTi strands | 20 | 
 | Transposition pitch | 50 | mm
Channel | RRR Cu | >100 | 
 | Copper section (Final) | 43.7 | mm²
Conductor | Nominal current | 3924 | A
 | Temp. margin @ 2.6T & 4.7K | 2.5 | K
 | Hot spot Temperature | 71.2 | K
 | σ0.2% @ 293K | >165 | MPa
 | Total length | 16.2 | km
 | Unit length (supposed) | 2 | km
 | Coils weight (impregnated) | 7.9 | t
Technical Feedback from Luvata on this design: OK
Dimensions are in mm
12.4
6.78
4.6
1.26
11.4
5.6
20×Ø=0.7
R~0.3
(2.31)
Copper
Fiber Glass Insulation

## Slide 19
Margin @ 4.7 K
B0 | 1.5 T | 1.7 T | 2.0 T | Units
Current | 2900 | 3296 | 3924 | A
Bpeak | 1.925 | 2.187 | 2.602 | T
Temp. margin | 3.1 | 2.9 | 2.5 | K
Enthalpy margin |  |  | 7.4 | kJ/m3
Load line margin | 60.6 | 55.3 | 46.8 | %
I / Ic(Tm,Bpeak) | 17.3 | 21.3 | 28.8 | %
Chart: Bpeak [T]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Jc @ 4.7K | 7360.1711 | 4905.6453 | 3646.4254 | 2796.8281 | 2147.8738 | 1614.8926 | 1154.8952 | 741.714 | 354.2996 | 0
Load line | 0 | 870.1062 | 2206.6058 | 6328.0451
B0 = 2T | 1175
B0 = 1.7T | 987
B0 = 1.5T | 870
:= 1 MJ/m3
with a typical zone epoxy crack of 1 mm3, we get a potential heat deposition of 1 mJ.
What about the dose from radiation?
Stability

## Slide 20
Geant4 Simulations
MARCO is here
The simplified geometry of the tracker & ECAL
The detailed geometry of the coil
Results for 1 fb-1 (105s) | 
Total dose | 0.00112662 Gy
Dose per second | 1.13E-08 Gy s-1
Total energy | 9.47 J
Power | 9.5E-05 W
Power density | 7.14E-11 W cm-3
Particles profile over η
No issue from radiation
Stability is assured
Resin degradation is negligible
Z (mm)
RESULTS

## Slide 21
Mechanical Analysis and Design
What is it missing?
The tie-rods
We need to fix the iron yoke to design them
Brass
G10
Homogenized coil

## Slide 22: Results for “Cool down + Energizing”
Visu x150

## Slide 23
Chart: Normal stress as a functions of the different load cases
| 4 | 54 | 104 | 154
COIL Normal stress X | 25 | 43 | 50 | 15
G10 Normal stress Y | 2 | 46 | 15 | 32
BRASS Normal stress Y | 11 | 66 | 51 | 97
Limit COIL | 110 | 133.3333 | 133.3333 | 133.3333
Limit G10 | 102.8 | 198.4 | 198.4 | 198.4
Limit BRASS | 275.3333 | 344.6667 | 344.6667 | 344.6667
Chart: Von-Mises equivalent stress as a functions of the different load cases
| 1 | 51 | 101 | 151
COIL Von-Mises eq. stress | 23 | 38 | 68 | 46
G10 Von-Mises eq. stress | 2 | 44 | 20 | 57
BRASS Von-Mises eq. stress | 27 | 64 | 69 | 97
Limit COIL | 110 | 133.3333 | 133.3333 | 133.3333
Limit G10 | 102.8 | 198.4 | 198.4 | 198.4
Limit BRASS | 275.3333 | 344.6667 | 344.6667 | 344.6667
Chart: Hoop stress as a functions of the different load cases
| 21 | 71 | 121 | 171
COIL Hoop stress θ | 25 | 45 | 50 | 15
G10 Hoop stress θ | 1 | 46 | 15 | 20
BRASS Hoope stress θ | 30 | 66 | 51 | 97
Limit COIL | 110 | 133.3333 | 133.3333 | 133.3333
Limit G10 | 102.8 | 198.4 | 198.4 | 198.4
Limit BRASS | 198.4 | 275.3333 | 275.3333 | 275.3333
Chart: Shear stress as a functions of the different load cases
| 15 | 65 | 115 | 165
COIL Shear stress RZ | 0 | 2 | 1 | 4
G10 Shear stress RZ | 0 | 4 | 1 | 3
BRASS Shear stress RZ | 0 | 4 | 1 | 8
Limit COIL | 8.4 | 12 | 12 | 12
Limit G10 | 16.92 | 29.04 | 29.04 | 29.04
Limit BRASS | 88 | 105.6 | 105.6 | 105.6
General Mechanical Behaviors – 3D
Gravity
Cool down
EM forces
Energizing
Gravity
Cool down
EM force
Energizing
Gravity
Cool down
EM forces
Energizing
Gravity
Cool down
EM force
Energizing

## Slide 24
Detailed conductor analysis
2D-axi mechanical model with Cast3m
Uz = 0
Z
R
Axial middle zone
Homogenized conductors
Homogenized conductors

## Slide 25
Cool-down
Peak Von Mises stress (MPa):
in cable = 72 < 150
in Cu stabilizer = 91 < 133
in glass fiber = 89 < 198
Peak Von Mises stress (MPa):
in cable = 114 < 150
in Cu stabilizer = 125 < 133
in glass fiber = 108 < 198
Energization
Detailed conductor analysis

## Slide 26
Peak SIGMA RZ in conductor insulation (MPa) = 13 < 14
Cool-down
Energization
Peak SIGMA RZ in conductor insulation (MPa) = 13 < 14
R
Z
Detailed conductor analysis

## Slide 27
Peak SIGMA RZ in conductor insulation (MPa) = 13 < 14
Cool-down
Energization
Peak SIGMA RZ in conductor insulation (MPa) = 13 < 14
R
Z
Detailed conductor analysis

## Slide 28
Cryogenics Design and Heat loads
Chart: Cool-down with 10 g/s and DT=40 K
| 0 | 0.75862268518518472 | 1.516493055555554 | 2.2637731481481471 | 2.9906249999999983 | 3.7068865740740726 | 4.4124999999999988 | 5.0877893518518498 | 5.7230324074074046 | 6.3181134259259233 | 6.8632812499999982 | 7.0991666666666653 | 7.317129629629628 | 7.6570601851851832 | 7.8531828703703681 | 7.9115883235622535 | 7.9189727009243098
 | 300 | 280 | 260 | 240 | 220 | 200 | 180 | 160 | 140 | 120 | 100 | 90 | 80 | 60 | 40 | 20 | 4
Thermosiphon power available
100 W @ 4.55K
Heat Loads | 
Cold mass heat load @ 4.6 K | 36 W
Cold valves @ 4.6 K | 5 W
Phase separator tank @ 4.6 K | 5 W
Copper current leads @ 4.6 K-300 K | 12 W - 0.67g/s
Thermal shield supports + thermalisation @ 45 K - 65 K | 80 W

## Slide 29
Quench and Hot-Spot
Hot-spot temperature is well within the usual limits considered (100K)
Quench-back in the mandrel plays a fundamental role (reducing of 20 K the hotspot)
Quench caracteristic time = 15.3 s
3/4 of the energy in the dump resistance
1/4 in the coil + mandrel

## Slide 30
Conclusions
MARCO is mature to start the detailed phase design, to be achieved by the end of 2023. This includes the procurement of the first conductor’s length (by JLAB)
It respects all the magnetic requirements and even beyond (2.0 T instead of 1.7 T)
No show-stopper on the mechanics
No show-stopper on the conductor
No show-stopper on cryogenics and protection
Iron yoke will be finalized in the next weeks
Next week first design review for this phase

## Slide 31
Proposition de Stage
« Etude de l’impact de l’utilisation des conducteurs stabilisés en cuivre sur la transparence des aimants pour détecteurs de particules »
En considérant différents aimants supraconducteurs déjà construis, la/le stagiaire reproduira leur design magnétique et mécanique sur un logiciel multi-physiques aux éléments finis et réadaptera leur design en recherchant la meilleure géométrie possible d’un conducteur en cuivre à l’aide des algorithmes génétiques ou autres algorithmes d’intelligence artificielle.
L’évaluation de la transparence sera faite avec Geant4, le logiciel du CERN utilisé pour étudier la propagation des particules dans les matériaux.
Telles simulations, qui impliquent le traitement d’une grande mole de données, seront faites avec un super-ordinateur en calcul parallèle.
Contact : valerio.calvelli@cea.fr