## Slide 1: Using step-like nonlinear magnets for beam uniformization at target in high intensity accelerarors
Zheng Yang, Jing-Yu Tang, IHEP, China
P.A. Phi Nghiem, Nicolas Chauvin, CEA/Saclay/IRFU, France

## Slide 2: Topics
Introduction to CSNS C-ADS IFMIF accelerators
Beam spot uniformization
Introduction of the step-like magnet
Application on the CSNS C-ADS IFMIF
Introduction to the Simplified high-order field magnet

## Slide 3: CSNS high power proton accelerator
Phase | I | II | II’ or III
Beam power on target [kW] | 100 | 200 | 500
Beam energy on target [GeV] | 1.6 | 1.6 | 1.6
Ave. beam current [mA] | 63 | 125 | 315
Pulse repetition rate [Hz] | 25 | 25 | 25
Protons per pulse [1013] | 1.6 | 3.1 | 7.8
Linac energy [MeV] | 80 | 132 | 250
Linac type | DTL | DTL | +SCL
CSNS (China Spallation Neutron Source) is a high-power proton accelerator based multi-disciplinary facility for research, mainly relying on neutron scattering techniques.
Construction: 2011-2017
Site: Dongguan, Guangdong
IHEP and IOP

## Slide 4: China ADS high power proton accelerator
China is pursuing an ADS (Accelerator-Driven Subcritical System) program strongly, under CAS (IHEP, IMP, IPP and USTC)
Accelerator: 10mA, CW proton beam
RFQ+CH
RFQ+Spoke
2013
~5 MeV
2015
25~50 MeV
201X
50/150 MeV
~2022
0.6~1 GeV
~2032
1.2~1.5 GeV
5~10 MWt
100 MWt
≥1 GWt
Verification of two ways
Integration
Integral test
Phase II target
Phase III target
10 MeV
Phase I
R&D Facility
Phase II
Experiment Facility
Phase III
DEMO. Facility

## Slide 5: Introduction to IFMIF accelerator
IFMIF (International Fusion Material Irradiation Facility) is one part of Broader Approach signed between Europe and Japan
in parallel to the decision of ITER construction.

## Slide 6
L
M
H
Test Cells
High (>20 dpa/year, 0.5 L)
Medium (>1 dpa/year, 6 L)
Low (<1 dpa/year, > 8 L)
Lithium Target
25 mm thick, 15 m/s
Typical reactions 7Li(D,2n)7Be 6Li(D,n)7Be 6Li(n,T)4He
2 accelerators, 2x125 mA, 2x5MW
D+
IFMIF: International Fusion Materials Irradiation Facility

## Slide 7
IFMIF-EVEDA is studied and constructed in Europe, and to be installed in Japan.
The highest average current linac under developing in the world, pose many challenges
  Based on CW RFQ and superconducting HWR linac

## Slide 8
One of the critical issues concerning the interface between a high-power beam and its irradiation target is the spot uniformity to reduce the peak current density at the target and reduce the beam halo
  CSNS
  Beam footprint in rectangular shape: 12 cm (H) x 5cm (V)
  Ratio of the peak current density to the average: <3
  C-ADS
  Beam footprint in rectangular shape: 4.4cm (H) x 4.4cm (V)
  Ratio of the peak current density to the average: <2.5
IFMIF (to be revised)
    Beam footprint in rectangular shape: 20 cm (H) x 5 cm (V)
    Current density across the flat top is uniform (±5%)
    Current density: < 0.5 A/cm2 (for |x|>11 cm)
Beam spot uniformization

## Slide 9
Input beam of C-ADS beam transfer line
Input beam of IFMIF-HEBT

## Slide 10
Nonlinear magnets are needed for the beam spot uniformization at target
  More conventional: single octupole or pair of octupole and dodecapole for each plane (horizontal or vertical)
  New concept-1: step-like field magnets, initially proposed for ESS and CSNS
  New concept-2: simplified multipole magnets including different combinations of anti-symmetric second-order, third-order, fourth-order and fifth-order field magnets, recently proposed at IHEP

## Slide 11: Introduction of the step-like magnet
8 poles -r50 mm
Field on pole 0.30 T
Octupole
2 dipoles-r100 mm
Field on pole 0.040 T
Step-like magnet

## Slide 12: Advantage
Flexibility
uniformization of beam core and beam halo can be done separately by two steps
Cheaper
standard multipoles: 100 thousand dollars
step-like magnets : 20-40 thousand dollars

## Slide 13
Step-like field magnet prototyping

## Slide 14
Optimization principle
1. Change the last four or six quadrupoles and the length of drift to get a larger beam spot on the target and fulfill the request of the flat beams and phase advances (linear optics)
2. Adjust the parameters of the step-like magnets to obtain a good beam spot on the target (nonlinear optics)
3. Repeat 1. and 2. several times to find the best result

## Slide 15
Studies at IHEP:
Using step-like field magnets (SFM) for spot uniformization at CSNS
100000particles

## Slide 16: Tests with beam for spot uniformization
A test beam line using the ADS-RFQ is being set up for studies on both halo development and spot uniformization (plan under modification)
SFM can be step-like field magnets or simplified high-order magnets

## Slide 17
Simulation results at ADS RFQ beam test line:
Left: not concern about the space charge effect; Right: concern about the space charge effect
100000particles
10000particles

## Slide 18
Studies at ADS beam line (dump):
Using step-like field magnets (SFM) for spot uniformization

## Slide 19
Duodecapoles
Octupoles
Adaptation,
9° achromat
Non-linear lenses
Beam homogenisation
Beam expander
Li Target
Dipoles
Quadrupoles
"Classical" HEBT structure
Superconducting Linac
R. Duperrier, J. Payet, D. Uriot, Proc. of EPAC 2004

## Slide 20
Beam distribution at Li Target
Beam losses
scrapers 2.3 kW
(to be optimised)
To be improved
Tuning strategy to be defined

## Slide 21
Duodecapoles
Octupoles
Adaptation,
9° achromat
Li Target
Dipoles
Quadrupoles
Test (temporary) structure with SFM
Superconducting Linac
Step-like Field Magnet
J.Y.Tang, H.H. Li, S.Z. An, R. Maier
NIMA, 2004

## Slide 22
2 dipoles-r100 mm
Field on pole 0.040 T
2 dipoles-r100 mm
Field on pole 0.025 T

## Slide 23
Beam distribution at Li Target
Beam losses
scrapers 2.3 kW
(to be optimised)
To be improved
Larger Footprint
Tuning strategy to be defined

## Slide 24
Automatic procedure for obtaining flat rectangular beam
The Command :
MY_DIAG(Beam_Homogeneity) n Target_Value Dimensions_X Dimensions_Y Relative_Weight_Dimension/homogenity
Notes: 这里应该强调是在Trace-Win中进行的程序功能改进工作.

## Slide 25
Adaptation,
11° achromat
Li Target
Dipoles
Quadrupoles
Shorter structure with SFM

## Slide 26
No beam loss

## Slide 27
Density
Start-to-end without errors
Density
Start-to-end with errors

## Slide 28
Simplified high-order field magnets
  Used for a flat good field region
  Available for any order of anti-symmetric field or symmetric field
  Right: simplified 3rd order field magnet (model and relative difference to theoretical distribution)

## Slide 29
Studies at IHEP:
Using simplified high-order field magnets (2nd+4th) for spot uniformization at ADS-RFQ

## Slide 30
Thank you