## Slide 1: A Micromegas TPC for the ILC
Wenxin Wang
CEA-Saclay

## Slide 2
Introduction: Micromegas & TPC
Micromegas ILC-TPC
    ILC & LP-TPC
    Beam test with Micromegas modules
    Test bench
    Ion backflow measurement
Other Micromegas TPC application
  Imaging by neutrons
Conclusion
Introduction: Micromegas & TPC
Micromegas ILC-TPC
    ILC & LP-TPC
    Beam test with Micromegas modules
    Test bench
    Ion backflow measurement
Other Micromegas TPC application
  Imaging by neutrons
Conclusion
Outline

## Slide 3: Micromegas
PCB
Invented by Y. Giomataris et al, (CEA/Saclay) 1996
MICROMEsh GAseous Structure
Cathode
Mesh
Drift gap
~0.3 kV/cm
Amplification gap
~50-100 µm ~50 kV/cm
Eamplif / Edrift ~ 200
Characteristics:
Spatial resolution (<100μm)
Small gap: fast rise time (<1ns) and fast collection of ions (<100ns)
High gain (up to 105 or more)
Low ion back-flow into drift space

## Slide 4: TPC: Time Projection Chamber
E
Electrons diffuse and drift due to the E-field
Localization in time and position
B
A magnetic field reduces electrons diffusion
Micromegas TPC : the position-sensitive electron collection system is made by Micromegas
t
Ionization energy loss(dE/dx)
3D track points reconstruction
x
y
( Micromegas TPC )

## Slide 5: Outline
Introduction: Micromegas & TPC
Micromegas ILC-TPC
    ILC & LP-TPC
    Beam test with Micromegas modules
    Test bench
    Ion backflow measurement
Other Micromegas TPC application
  Imaging by neutrons
Conclusion

## Slide 6: Higgs boson & ILC
Higgs 125 GeV has been discovered at LHC
It can be studied in detail at ILC where it is produced by Higgs-strahlung.
Higgs-strahlung process:
This allows an unbiased selection by Z recoils, to measure mass and all possible decay modes.
This sets the goal resolution of 100 m per pad row.
(International Linear Collider)

## Slide 7: Top quark & ILC
A typical multi-jet final state at the ILC
(500 GeV event with multi-hadronic final state).
Many interesting processes have many jets and many charged tracks.
TPC provides 3D continuous tracking with low material budget. This is important for pattern recognition .

## Slide 8: ILD-TPC for ILC
L: 4.7m
: 3.6m
Design for an ILD TPC in progress:
Each endplate: 80 modules with 8000 pads
31 km
ILD
Spatial Resolution (in a B=3.5T magnetic field):
δ(x) ~ 100μm for the full 2.3m drift
Low material budget in front of the calorimeters:
Barrel: 5% X0
Endplates: ~25% X0

## Slide 9: Large Prototype-TPC (LP-TPC)
Magnet up to 1.2T
Field cage: 61 cm length and 72 cm diameter
7 interchangeable modules with keystone shape
Gaseous mixture: T2K gas (Ar:CF4:iC4H10 =95%:3%:2%)
EUDET setup at DESY

## Slide 10: MPGD: Micromegas & GEM
Readout |  | Pad Size | Electronics | Groups
MPGDs | Micromegas (Resistive anode) | (~ 3 × 7 mm2 Pad) | AFTER | Saclay-Carleton
Readout |  | Pad Size | Electronics | Groups
MPGDs | Micromegas (Resistive anode) | (~ 3 × 7 mm2 Pad) | AFTER | Saclay-Carleton
 | Double GEMs (Laser-etched) | (~ 1 × 6 mm2 Pad) | ALTRO | Asia
 | Triple GEMs (wet-etched) |  |  | Desy
Several Micro-Pattern Gaseous Detectors types of readout modules are studied
Micromegas
(test with 7 modules)
GEM
(test with 3 modules)

## Slide 11: Micromegas with Resistive Anode
w : pad width
0 : resolution at Z=0 without diffusion
Charge dispersion technique with a resistive anode
pads
mesh
E
B
Amplification gap: ~100m
resistive foil: ~75m
insulator: ~100m
Pad width limits MPGD TPC resolution
Direct signal readout technique
pads
mesh
E
B
Amplification gap: ~100m
Resistive foil also provides
anti-spark protection
: the surface charge density
R: the surface resistivity of the resistive layer
C: the capacitance per unit area.
Equation for surface charge density function on the 2D continuous RC network:

## Slide 12: Micromegas module
Module size: 22 cm × 17 cm
24 rows × 72 columns
Readout: 1726 Pads
Pad size: ~3 mm × 7 mm

## Slide 13
2008~2011:
Test with one module at the center of LP-TPC
2012~2013:
Test with multi-modules at the endplate of LP-TPC

## Slide 14: Tests with one single module
(2008~2011)
At the center of LP-TPC

## Slide 15: Micromegas modules
Resistive ink
~3 MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
(no resistive layer)
Resistive Kapton
~3 MΩ/□
Module 1
Module 2
Module 3
Module 4 &
Module 5

## Slide 16: Uniformity
Z=5cm
Mean Residual vs Row Number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film
(red points)
Z=50cm
Z=35cm
Row number
Resistive CLK Module
Resistive ink Module

## Slide 17: Spatial resolution
Module 5
Module 4
: the resolution at Z=0
: the effective number of electrons
Cd = 315.1 µm/√cm (Magboltz MC)
(B = 0T)

## Slide 18: Spatial resolution
(B = 1T)
Module_INK
Module_CLK
Cd = 94.2 µm/√cm (Magboltz MC)

## Slide 19: Spatial resolution

## Slide 20: Tests with multi-modules
(2012~2013)
Fully cover the endplate of LP-TPC
Using a quasi-industrial production chain

## Slide 21: Integrated electronics
14 cm
25 cm
Front-End Card
(FEC)
12.5 cm
2.8 cm
Remove packaging and protection diodes
Wire-bond AFTER chips
Use two 300-point connectors
0.78 cm
0.74 cm
3.5 cm
3.5 cm
AFTER Chip
  The resistive foil protects against sparks
4.5 cm

## Slide 22: Material budget of a module
 |  | M (g) | Radiation Length (g/cm2)
Module frame + Back-frame + Radiator (×6) | Al | 714 | 24.01
Detector + FEC PCB (×6) + FEM | Si | 712 | 21.82
12 ‘300-point’ connectors | Carbon | 30 | 42.70
screws for FEC + Stud screws+ | Fe | 294 | 13.84
Air cooling | brass | 12 | 12.73
 | Plexiglas | 128 | 40.54
Average of a module |  | 1890 | 21.38
Low material budget requirement for ILD-TPC:
Endplates: ~25% X0
(X0: radiation length in cm)
Front-End Card (FEC)
Pads PCB +
Micromegas
Front-End Mezzanine (FEM)
Cooling system
‘300-point’ connectors

## Slide 23: Test bench
A 55Fe source is put in an aluminum collimation tube and fixed on a set of two mechanical arms (X-Y).

## Slide 24: Test bench
Test with collimator
Test without collimator
to check the map of missing pads

## Slide 25: Modules comparison
At Vmesh = 380 V, Energy resolution ~12% r.m.s
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 0.12692 | 0.12361 | 0.11822 | 0.12788 | 0.11539 | 0.11309 | 0.12692

## Slide 26: Modules comparison
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 2469.0098 | 2979.0717 | 2327.5895 | 2559.4998 | 2063.5909 | 3134.0745 | 2844.6615
At Vmesh = 380 V, average gain ~ 2630, gain spread ~15%

## Slide 27: Gain Study using beam events
2500 at Vmesh=380V
( 2700 at Vmesh=380V
From test bench)
Charge per row
For 6.84 mm pitch & 5 GeV e-
Nelectron (MPV) expected = 45
(from HEED simulation)

## Slide 28: Beam events display
2D or 3D display from ILC software
Online monitor
Offline monitor

## Slide 29: Analysis Framework: MarlinTPC
MarlinTPC
Marlin based simulation, digitization, reconstruction and analysis code for the TPC.
KalDet &KalTest: (installed in Marlin)
    A ROOT-based Kalman Filter Package.
    Used to reconstruct tracks.

## Slide 30: Spatial resolution
Event selection
 only single track event

## Slide 31: Spatial resolution
Hit selection
Fit track with all rows
: supposed residual of the detector
: the fitted hit position in test row
: the position of track crossing the test row

## Slide 32: Spatial resolution
Profile histogram of the residual with the track in one row before bias correction
Profile histogram of the residual with the track in one row after bias correction
Pad size
(mm)
(mm)
(mm)
(mm)

## Slide 33: Spatial resolution
Distribution of the residuals (z = 15 cm)

## Slide 34: Spatial resolution
B=1 T Cd = 94.2 µm/√cm (Magboltz MC)
24 rows of a module

## Slide 35: Extrapolation of the spatial resolution
Extrapolate to 2.3m & B=3.5T
B=0T
B=1T
B=3.5T
--- Micromegas with
3 mm width pads
--- GEM with 1 mm
width pads
B=1T

## Slide 36: Distortions
B=1T
B=0T
After alignment B=0T

## Slide 37: Field distortions
Distortions in B=0T or B=1T
at different drift distances z (15cm~50cm)
B=1T
B=0T

## Slide 38
Ion backflow measurement

## Slide 39
Ion backflow measurement
Id : Current on the cathode
Ia : Current on the mesh
Ip : Current on the cathode without amplification applied in the amplification gap
A 10 cm ×10 cm T2K prototype
Bulk Micromegas
T2K gaseous mixture
Ar/CF4/Isobutane (95:3:2)

## Slide 40: Gain
Gain as a function of Vmesh
(Edrift = 0.2 kV/cm at atmospheric pressure)
A measured 55Fe spectrum
(at Vmesh = 350 V and Vdrift = 400 V)

## Slide 41: Electron transparency

## Slide 42: Ion backflow
For our Micromegas modules tested in LP-TPC, the field ratio is set around 200. The ion backflow will be of the order of  6×10-3.

## Slide 43
Introduction: Micromegas & TPC
Micromegas ILC-TPC
    ILC & LP-TPC
    Beam test with Micromegas modules
    Test bench
    Ion backflow measurement
Other Micromegas TPC application
  Imaging by neutrons
Conclusion
Outline

## Slide 44: Micromegas TPC for neutron imaging
Gas: Argon + 5% Isobutane
128 µm
HVmesh
Eamp ~ 23 kV/cm
15 mm
HVdrift
Edrift ~ 160 V/cm
PE
Detector layout: 1728 (48×36) pads of 1.75 mm×1.50 mm
+ bulk Micromegas
Elastic scattering on hydrogen n  p
+ masks (PE)
PCB
Micromegas
n
p
Aluminized polyethylene 1 mm
between 2 layers (0.5 µm) of Al
57.4 mm
88.6 mm
Cosmics
(x, y, t)

## Slide 45: Simulation for converter efficiency
Neutronproton recoiling efficiency in a polyethylene [C2H4]n layer coming from 241Am-9Be source
Incident neutron spectrum
According to ISO 8529(*)
* INTERNATIONAL STANDARD ISO 8529. Reference neutron radiations – Part 1: Characteristic and methods of productions. International Standard ISO 8529-1 (2001).

## Slide 46: Reconstruct track
Garfield
Avalanches
Drift lines from primary ionization e-
Proton track
\\

## Slide 47: Test with a 241Am-9Be neutron source
Letters “CEA” or “LZU”
8 cm thickness
4-4.5mm width
2.5mm
3 mm
3.5mm
4 mm

## Slide 48: Neutron imaging
Integrating the ADC of all events in one pad.
Reconstructed using the time information.

## Slide 49
Introduction: Micromegas & TPC
Micromegas ILC-TPC
    ILC & LP-TPC
    Beam test with Micromegas modules
    Test bench
    Ion backflow measurement
Other Micromegas TPC application
  Imaging by neutrons
Conclusion
Outline

## Slide 50
A lot of experience has been gained in building and operating Micromegas TPC panels.
The characteristics of the Micromegas modules, such as the uniformity, energy resolution, stability have been studied in detail.
7 modules have been successfully tested with full integration of the electronics at the same time.
Thanks to the resistive technology, the measured resolution is about 60 microns at zero drift distance with 3 mm wide pads. This meets ILC needs.
Distortions are observed. Their detailed study will allow to correct them and improve the design to minimize them.
Conclusion