## Slide 1
Understanding avalanches in Micro-Pattern Gaseous Detectors from single-electron response measurement

## Slide 2
MPGDs: powerful devices for high-energy physics
COMPASS
LHCb
ATLAS
upgrade
NSW
ALICE upgrade
T2K
CMS
upgrade
CLAS12
Micromegas
vertex detector

## Slide 3
Summary
- Active Target Detectors
- Statistical models of avalanche multiplication in gaseous detectors
- MPGD single-electron response (SER) measurement: examples
- The IPN Orsay laser test-bench
- Comparison with Monte-Carlo calculations

## Slide 4
Active Target Detectors
TPC-like detector where the gas is the reaction target and the detection medium
for 3D trajectory-reconstruction of the incoming ion-beam and the reaction products
IKAR ionisation chamber
MAYA @ GANIL
Study of hadron elastic scattering in the H3
beam @CERN (1976)
28x26x20cm3 filled gas volume (Pmax 3 bars)
Segmented cathode with 35x35 5mm hexagonal pads read by Gassiplex chips, amplification MWPC
R&D efforts to build new active target detectors with higher granularity pad planes using a MPGD as amplification device to improve luminosity, efficiency, energy and spatial resolution.
C.E. Demonchy et al., NIM A 573 (2007) 145-148
A.A. Vorobyov et al., NIM A 270 (1988) 419-430.

## Slide 5
The CENBG Time-Projection Chamber
A time-projection chamber for the 3D reconstruction of 2p radioactivity events
B. Blank et al., NIM A 613 (2010) 65-78
Isotope identification + implantation in the gas
+ 3D reconstruction of protons trajectory
Reconstruction of a 45Fe decay event
View of the TPC interior
Daughterboard equipped with two 32ch
VA/TA IDEAS ASICs
64 energy
and time
channels
384x384
channels
Active
volume:
13.8x13.8x6
cm3
Gas: P10,
500mbar

## Slide 6
ACTAR-TPC prototype
Collaboration: GANIL Caen, CENBG Bordeaux, IPN Orsay, CEA/Irfu Saclay, University of Leuven (Belgium),
Universidade de Santiago de Compostela (Spain)
Prototype MPGDs (Micromegas 128µm and 256µm, THGEM 600µm)
Circular PCB pad plane f 5.6cm in the MAYA drift field cage
2x2mm2 square pads – AFTER card 288 channels – Track length: 3.8cm
J. Pancin et al., NIM A 735 (2014) 532-540
Toward a next generation of active target TPC for experiments @ GANIL SPIRAL2
Angular resolution ~ 1o FWHM
iC4H10 50mbar
He+CF4 2%
iC4H10
Micromegas 256µm
5.15, 5.48 and 5.8keV a
Energy resolution:
5, 4.5 and 6% FWHM
Ar+CF4 2%
1100mbars
Micromegas 256µm
Next: demonstrator with a 2048 pixels anode PCB
equipped with the new electronics GET for TPC

## Slide 7
Prototype AT-TPC
D. Suzuki et al., NIM A 691 (2012) 39-54
Cylidrincal field cage
f 28 cm, length 50cm
Dual gas volume structure
Micromegas bulk 128µm
Anode PCB
253 pads
Active target detector under development @NSCL-MSU
Electronics:
Mesh: Canberra 2001 Preamp
Anode pads: AFTER (CEA/Saclay)
Pads biasing possible to avoid
saturation and reduce risk
of discharge
Commissionning
with a radioactive 6He beam
He 90% CO2 10% 1 bar
Drift: 0.8kV/cm , Mesh: -320V
Beam
4He
4He
6He
6He

## Slide 8
Summary
- Active Target Detectors
- Statistical models of avalanche multiplication in gaseous detectors
- MPGD single-electron response (SER) measurement: examples
- The IPN Orsay laser test-bench
- Comparison with Monte-Carlo calculations

## Slide 9
Energy and spatial resolutions
Spatial resolution :
Energy resolution :
sX: spatial resolution along the
pad-row direction
sX0: intrinsic resolution (=0 for
particle tracks perpendicular to
the pad row)
D: transverse diffusion
z: drift distance
N: total number of drift electrons
detected by the pad row
F: Fano factor (primary ionisation
fluctuations)
f: relative gain variance
(avalanche charge fluctuations)
W : Mean energy to create an ion-e-
pair in the gas
E : Particle energy
with:
M. Kobayashi, NIM A 562 (2006) 136-140
Avalanche charge fluctuations f set a limit
to energy and spatial resolutions.
Predictions ? Measurements ?

## Slide 10
Analytic models (I)
Furry (1937), Snyder (1947), Wijsman (1949), & others:
- Probability to ionise over a distance d is ad (a first Townsend coefficient)
- a is constant
- No attachment losses
For large mean size avalanches, avalanche charge fluctuates exponentially and
f =1.
Data from Cookson and Lewis (1966)
Hump in the
avalanche charge
distribution !!!
Data from Curran (1949)
Ar 50% CH4 50%
670mbars
CH4
Cylindrical counter
E/p=218V/cm/torr
Parallel plate
E/p=156V/cm/torr
E/p=120V/cm/torr
3550V
3280V
3550V

## Slide 11
Analytic models (II)
Several alternative analytic models to explain this departure from an exponential
distribution:
Raether’s group: after ionisation, electrons have to travel a minimum distance before their energy
suffices to ionise
Mean distance between ionisation: 1/a
Minimum distance between ionisation: U/E
k = E/ aU
k >>1
exponential
k ~1
hump
Models based on a parameterisation of the first Townsend coefficient a:
Byrne (1962): a(r,n) = f(r) (a0 + a1/n) , r: electron position in the avalanche, n number of electrons
in the avalanche
Polya distribution follows for on-average-large avalanches,
in agreement with Curran’s measurement but not with Cookson and Lewis’s
Lansiart & Morucci (1962): a depends on the avalanche charge n following a(n) = a(0) (1 + k/n2)
n
(s /
) = 1/(1+k)
< 1 in agreement with Curran’s measurement
Such an approach neglects relaxation effects (Legler 1967)
This model is unsuitable to describe electron avalanche statistics
(Alkhazov 1970)

## Slide 12
Analytic models (III)
Legler’s model (1961): Introduction of x , distance since last ionisation, and a(x), probability to ionise
again. From this parameterisation, the relative gain variance can be calculated
)
Snyder’s model (exponential distribution)
Legler’s model (Model gas P(n) = 1/
n
F(n/
n
)
Alkhazov’s
analysis (1970):
f = f0 (1- 1/
n
)
J. P. Sephton et al.,
NIM 219 (1984), 534-542.
See also Rob Veenhof’s talk @ IWAD 2014
http://indico.vecc.gov.in/indico/conferenceOtherViews.py?view=standard&confId=31#2014-10-28
G.D. Alkhazov,
NIM 89 (1970), 155-165.
1/k
f0

## Slide 13
Monte-Carlo approach
A Monte-Carlo approach is more practical than analytic models to describe
electron avalanche mechanisms in gas mixtures.
Inelastic collisions (vibrations, rotations)
Attachment
Elastic collision
All these processes are ruled by cross-sections which depend on the nature of
the gas and the electron energy.
Ionisation
Steve Biaggi’s Magboltz program relies on this approach
Improvement needed: Inclusion of Penning effect
Excitation

## Slide 14
Excitation-ionisation transfer
In certain atoms, metastable excited states are unable to deexcite immediately
by emission of a photon. A deexcitation may occur through a collision with
another atom resulting in the ionisation of the latter.
Example: Argon + iC4H10 mixture
ion: 15.7eV
D-exc: 14.0eV
P-exc: 13.0eV
S-exc: 11.55eV
ARGON
ion: 10.7eV
Exc 1: 7.4eV
Exc 2: 9.7eV
iC4H10
Penning effect
Ar* + iC4H10
Ar + iC4H10+ + e-
The transfer rate rp is the probability
that an excited state produces a new
electron by Penning effect
Courtesy of Özkhan Sahin

## Slide 15
Direct ionisation and excitation rates (I)
Direct ionisation rate
Total direct ionisation
rate (iC4H10 + rare gas)
Excitation rate
of rare gas
- The direct ionisation rate of iC4H10 is one
order of magnitude higher than the direct
ionisation rate of noble atoms in the Ne and
He-based mixtures
Magboltz 10.1
-The direct ionisation rate of iC4H10 is comparable
to that of Ar in the Ar-based mixture
The total direct ionisation rate is much
higher than the excitation rate of He or Ne.
Penning transfers of excited Ar* atoms are
expected to contribute more significantly to
the gain than in the Ne or He-based mixture
Excitation rate of Ar dominates the total
direct ionisation rate of the Ar-based mixture.

## Slide 16
Direct ionisation and excitation rates (II)
Ratio of total ionisation rate to the excitation rate of the states at 7.4 and 9.7eV in iC4H10
Ionisation potential:
Ar: 15.8eV
Ne: 21.6eV
He: 24.6eV
iC4H10: 10.7eV
Penning transfer
from the 7.4 and 9.7eV
excited states of
iC4H10 forbidden !!
Energy transferred to populate the 7.4 and 9.7eV excited states in iC4H10
is lost for ionisation.
Consequently, avalanche charge fluctuations are expected to increase for
gas mixtures with the lowest ratio (i.e the Ar-based mixture).

## Slide 17
Summary
- Active Target Detectors
- Statistical models of avalanche multiplication in gaseous detectors
- MPGD single-electron response (SER) measurement: examples
- The IPN Orsay laser test-bench
- Comparison with Monte-Carlo calculations

## Slide 18
DVGEM
Feedback
Single-electron response of a single GEM
Polya distribution
f = 0.31
R. Bellazzini et al., NIM A 581 (2007) 246-253
Ne 50% DME 50%
CMOS VLSI chip
Threshold: 2200 e-
GEM-MIGAS in single GEM mode
J.A. Mir et al, IEEE Trans. Nucl. Sci. NS-55 (2008) 2334-2340.
Polya
distribution
Micromesh at 0V
EI
Ed
Ortec
142A
He 85% iC4H10 15%
d = 50 µm
Ed=0.25kV/cm
EI= 6kV/cm
Electronics noise:
1.4x104 e- r.m.s.
0.3 £ f £ 0.4

## Slide 19
Single-electron response of multi-GEMs
3GEM +PCB configuration
Gains ~ few 105
Exponential
Exponential
Exponential
Exponential
Polya
A.Buzulutskov et al.,
NIM A 443 (2000) 164-180.
Active area: 2.5x2.5cm2
4-GEM
J. Va’vra and A. Sharma, NIM A 478 (2002) 235.
Active area:122mm2
Charge preamp
Gain: 2.7µV/e-
Sh. Time: 65ns
sNoise: 2100 e-
Charge preamp, 0.45V/pC,
14µs time constant
Exponential
f = 0.33
Visible gain ~ 2.105
Mesh
UV light

## Slide 20
Single-electron response of a Micromegas
J. Derré et al., NIM A 449 (2000), 314-321.
He 90% iC4H10 10%
Gain > 106
Detection threshold: 3x104 e-
f ~ 0.4
Polya distribution

## Slide 21
Summary
- Active Target Detectors
- Statistical models of avalanche multiplication in gaseous detectors
- MPGD single-electron response (SER) measurement: examples
- The IPN Orsay laser test-bench
- Comparison with Monte-Carlo calculations

## Slide 22
Laser test-bench for SER measurement
Drift electrode: Quartz window with a
0.5 nm thick Ni-Cr layer
Mesh: 333lpi Buckbee-Mears©
70% optical transmission
Nickel
Measurements with a set of 9 pads (3*3),
size of 4*4mm2
Electronics:
  Pads: Gassiplex chips (noise: 2 000 e- r.m.s,
  gain 2.2mV/fC, dynamic range 500fC)
  Mesh: gain 100 voltage amplifier
Trigger:
  Mesh signal in 55Fe source mode.
  Photonis© XP2282B photomultiplier anode signal
  in laser mode
Ne 95% iC4H10 5% @ 1 bar
Drift field: 1kV/cm
Detector primarily designed for tests at low pressure for the ACTAR project
T. Zerguerras et al., NIM A 608 (2009) 397-402
Measurement of the charge on the central pad.
SER detection threshold of 104 e-
Laser light attenuated to reach a proportion of events
with charge above threshold of ~7%

## Slide 23
Single-electron response measurement
Polya :
q = 2.3 ± 0.1
f = 0.30 ± 0.01
G= 3.7 104
q = 2.2 ± 0.1
f = 0.31 ± 0.01
G= 5.0 104
q = 2.3 ± 0.1
f = 0.30 ± 0.01
G= 6.0 104
Relative gain variance increase
Secondary avalanches
due to photon feedback
q = 1.9 ± 0.1
f = 0.34 ± 0.01
G= 7.6 104
q = 1.7± 0.1
f = 0.37 ± 0.01
G= 105
VMesh <500V
VMesh ³ 500V
E= 31.25 kV/cm
E= 31.88 kV/cm
E= 29.38 kV/cm
E= 30 kV/cm
E= 30.63 kV/cm
f = (sQ / Q )2 = 1/(1+q)

## Slide 24
Improvements in 2013
Simplified geometry :
- Complex anode pad plane geometry
- Position of the 55Fe source
Lower noise level:
- Lower limit of gain at ~ 3. 104 for SER measurements
- Only for high-gain gas mixtures (ex: Ne:iC4H10 95:5)
Redesigned detector
Simplification of the anode plane segmentation
Change Front-End Electronics
Adapt the electronics chain
Lower pressure:
Pressure regulation and control system for studies at lower
pressure.
2009
2013
2009
2013
2013

## Slide 25
Improved detector
Conversion gap: 3.2mm
Amplification gap: 160µm
Mesh: Buckbee Myers©
333 lpi nickel electroformed
micromesh
Improvement of electronics S/N ratio
Cremat CR-110 PAC
Gain: 1.4V/pC
Noise : 200 e- RMS (table)
380 e- RMS (detector)
+
CAEN N568B
Spectroscopy Amplifier
(CG, FG fixed, SH=3µs, PZ fixed, Offset fixed)
Regulation
Measurement
Detector
Pressure control system
Calibration through a high-precision
1pF capacitance at the channel test-input
Change of mechanics and simplification
of the anode pads plane

## Slide 26
55Fe spectrum
Ar 95% iC4H10 5%
Ed = 900 V/cm, Ea = 28.12 kV/cm, CG 4
Energy resolution @5.9keV: 20% FWHM
Ne 95% iC4H10 5%
Ed = 900 V/cm, Ea = 26.9 kV/cm, CG 2
Energy resolution @5.9keV: 14% FWHM

## Slide 27
Method for Single-Electron Response (SER) measurement
The laser is focused on the drift electrode (quartz) in front of the central pad
- Trigger: XP2282B PMT anode signal
- Proportion of events above charge threshold (2. 103 e-) < 5%
- The PMT anode charge is measured to monitor the laser light intensity
(variation < 4%)
- The CG of the N568B Spectroscopy Amplifier is adjusted depending on
the mesh voltage, all the other parameters being fixed
The drift field is of 900V/cm
Gas mixtures: Ar 95% iC4H10 5%, Ne 95% iC4H10 5%, He 95% iC4H10 5%
@ 748 torrs
To avoid any damage on the CR-110 chips, the maximum voltage
applied on the mesh was 10V below the sparking limit voltage

## Slide 28
SP fit: Polya
SGP fit: Gaussian + Polya
E = 28.12 kV/cm
E = 26.25 kV/cm
E = 26.25 kV/cm
Single-electron response measured with improved detector
f = 0.56 +/- 0.04
f = 0.30 +/- 0.01
f = 0.37 +/- 0.03
f = (sNe / Ne)2 = 1/(1+q)
Polya :
Gain Ne and
relative gain
variance f
deduced from
the fit

## Slide 29
Experimental gain curves
The maximum gain before sparking
is reached with the Ne-based mixture
The maximum gain reached with the
Ne-based mixture is one order of
magnitude higher than with Ar
At a given E, the gain of the Ne-based
mixture is 7 times larger than in the
Ar-based mixture
At a given E, the gain of the Ne-based
mixture is twice larger than in the
He-based mixture

## Slide 30
Experimental relative gain variances
For the three gas mixtures,
f is almost unchanged in the
measured range of E
Ne and He-based mixtures
have very close f .
f is almost twice larger in the
Ar-based mixture than in Ne
or He.
Consistent with models, valid
in uniform E, predicting larger
f for gas with lower ionisation
rate.

## Slide 31
Summary
- Active Target Detectors
- Statistical models of avalanche multiplication in gaseous detectors
- MPGD single-electron response (SER) measurement: examples
- The IPN Orsay laser test-bench
- Comparison with Monte-Carlo calculations

## Slide 32
SER simulation with Garfield++
avalanche
ending plane
Drift region
3,2mm - 0.9kV/cm
Amplification region
160µm - 20-35kV/cm
electron starting
point
SER events have been simulated in a microscopic avalanche model, using a two volume
simulation for the electron drift and the avalanche development / amplification.
All electrical fields are assume to be homogeneous and adopted as analytic fields. (Parallel plate approximation)
Simulation of the drift process respects the starting conditions of the electron initiating the avalanche.
Microscopic approach yields mean amplification and variance of the gain, spectra are available.
The individual treatment of each electron requires huge calculation time, sufficient statistic can not be simulated for high fields.
↯
✓
Courtesy of Fabian Kuger

## Slide 33
Avalanche extrapolation
How to access mean and variance for huge avalanches (> 105 e-) with significant statistics ?
Approach: Avalanche development is a statistical process. As soon as the avalanche has
sufficiently grown, single fluctuations in further amplification processes are averaged out.
full (physics) simulation
mathematical extrapolation
First amplification step dominates the size of the avalanche and has to be fully simulated until avalanche reaches sufficient size (~100 e-).
The further (CPU-consuming) amplification steps are dominated by statistics and can be handled with an mathematical extrapolation.
Justifications:
Full avalanche development consists of a series of independent steps, pi(k) is the probability of a single-electron to create an avalanche of k electrons at the i-th step.
pi(k) depends on the spatial step length , the electric field and the gas mixture.
 same conditions during different steps lead to equal pi(k) within each step.
Courtesy of Fabian Kuger

## Slide 34
For all simulations, the ‘full avalanche’ has been computed for low E-fields (≤ 27kV/cm) and ‘first-half-simulations’ in the full range (20-35kV/cm).
 The step-number-exponent x is determined in a control region (25-27kV/cm)
(x ~ 2)
 Mean and relative gain variance ,
Simulation studies
Gas mixture | E (kV/cm) | rp
Ar iC4H10 5% | 28.12 | 0.321 +/- 0.003
Ne iC4H10 5% | 26.25 | 0.482 +/- 0.017
He iC4H10 5% | 26.25 | 0.175 +/- 0.025
Feedback is not included
rp is assumed to be identical for all excited states
Courtesy of Fabian Kuger
Two kinds of simulations have been performed:
‘Without Penning transfer’ and ‘Penning-transfer included’
Only combination of both yields the impact of Penning
transfer on the avalanche size.

## Slide 35
Comparison of calculated and experimental SER
E = 28.12 kV/cm
E = 26.25 kV/cm
E = 26.25 kV/cm
f = 0.56 +/- 0.04
f = 0.30 +/- 0.01
f = 0.37 +/- 0.03
Calculations reproduce the experimental SER of the Ne
and He-based mixture.
The calculated SER of the Ar-based mixture
underestimates the experimental spectrum tail.
T. Zerguerras et al., NIM A 772 (2015) 76-82

## Slide 36
Comparison of calculated and experimental gains
For E > 30kV/cm, the difference
between the calculated curve and
the experimental data increase
Significant contribution due
to secondary avalanches not
included in the calculation model
Calculations reproduce data
up to E ~ 30kV/cm
Experimental points used for rp determination
T. Zerguerras et al., NIM A 772 (2015) 76-82

## Slide 37
Comparison of calculated and experimental relative gain variance
The hierarchy of calculated f
is consistent with experimental
data and expectations from
considerations on ionisation rates
Good agreement up to 30kV/cm
with experimental data of Ne and
He-based mixtures despite the
model approximations
Discrepancy between calculations
and experimental data for the
Ar-based mixture and above
30kV/cm for Ne and He-based
mixtures
Feedback not included
in the model
T. Zerguerras et al., NIM A 772 (2015) 76-82

## Slide 38
Summary
A laser test-bench has been developed at the IPN Orsay to measure the
single-electron response (SER) of MPGDs.
Gain and relative gain variances of three binary gas mixtures (Ar, Ne,
He + 5% iC4H10 @ 748 torrs ) are deduced from the SER of a Micromegas detector.
Thanks to recent improvements, the SER measurement threshold is lowered
down to gains of ~ 5. 103
A microscopic Monte-Carlo model is developed and includes all processes
occuring during an avalanche, according to their cross-sections, together with
excitation-ionisation transfer (Penning effect)
Calculations reproduce the gas hierarchy in terms of gain and relative gain
variance and are consistent with the expectations of models based on ionisation
rate consideration
The Argon-based mixture has the lowest performance in terms of gain, relative gain
variance and breakdown limit
For the Ar-based mixture and for E > 30kV/cm, discrepancies are observed because
of a significant feedback, not included in the model

## Slide 39
Collaboration
Thomas Zerguerras a, Bernard Genolini a, Fabian Kuger b,c, Miktat Imré a,
Michaël Josselin a, Vincent Lepeltier d,3, Alain Maroni a, Thi Nguyen-Trung a,
Jean Peyré a,2, Joël Pouthas a,1, Philippe Rosier a, Özkhan Sahin e,
Lucien Séminor a , Daisuke Suzuki a, Claude Théneau a, Rob Veenhof e,f
a Institut de Physique Nucléaire (UMR 8608), CNRS/IN2P3-Université Paris-Sud,
F-91406 Orsay Cedex, France
b University of Würzburg, 97070 Würzburg, Germany
c CERN, Geneva, Switzerland
d Laboratoire de l’Accélérateur Linéaire (UMR 8607), CNRS/IN2P3-Université Paris-Sud,
91898 Orsay Cedex, France
e Department of Physics, Uludag University, 16059 Bursa, Turkey
f RD51 Collaboration, CERN, Geneva, Switzerland
1 Present address: Laboratoire de Physique Corpusculaire, ENSICAEN, Bvd
Maréchal Juin, 14050 Caen, France
2 Present address: Centre de Sciences Nucléaires et de Sciences de la Matière
(UMR 8609), CNRS/IN2P3- Université Paris-Sud, 91406 Orsay, France
3 Deceased

## Slide 40
Thank you for your attention

## Slide 41
Back-up slides

## Slide 42
AT-TPC prototype
Readout circuit for the Micromegas

## Slide 43
IKAR

## Slide 44
Single-electron response of multi-GEMs
A.Buzulutskov et al.,
NIM A 443 (2000) 164-180.
GEM thickness: 50µm
GEM1, GEM2 and GEM3 pitch: 140µm
Double conical hole pattern:
Metallic hole f: 80µm
GEM1 and GEM3 kapton hole f 30µm
GEM2 kapton hole f 50µm
GEM4 active area: 2.5x2.5cm2
Active area:122mm2
Double conical hole pattern
Thickness: 50µm
Pitch: 120µm pitch
Metallic hole f 80µm
Kapton hole f 40µm
J. Va’vra and A. Sharma, NIM A 478 (2002) 235.

## Slide 45
Regulation
Measurement
Detector
Pressure control system

## Slide 46
Measurements @ different CG values
G = 7.7 104
q = 2.3 ± 0.1
f = 0.30 ± 0.01
Ne 95% iC4H10 5%,
Vmesh= 480V, 750 torrs
CG 2
CG 3
G = 7.3 104
q = 2.2 ± 0.1
f = 0.31 ± 0.01
CG 4
G = 7.7 104
q = 2.0 ± 0.1
f = 0.33 ± 0.01
CG 5
G = 8.1 104
q = 2.2 ± 0.1
f = 0.31 ± 0.01

## Slide 47
A pulse signal is injected on the test input of the central pad (Pad_C) through a 1pF capacitance
Chart: Pad_C calibration: CG 2, FG 0, SH 2, PZ 66, Offset 120
| 44 | 66 | 113 | 228 | 343 | 451 | 687 | 918 | 1147 | 1374 | 1835
Pad_C calibration | 31.6228 | 47.4342 | 79.0569 | 158.1139 | 237.1708 | 316.2278 | 474.3416 | 632.4555 | 790.5694 | 948.6833 | 1264.9111
Chart: Pad_C calibration: CG 3, FG 0, SH 2, PZ 66, Offset 120
| 45 | 91 | 138 | 231 | 462 | 695 | 926 | 1391 | 1857
Pad_C calibration | 15.8114 | 31.6228 | 47.4342 | 79.0569 | 158.1139 | 237.1708 | 316.2278 | 474.3416 | 632.4555
Chart: Pad_C calibration: CG 4, FG 0, SH 2, PZ 66, Offset 120
| 56 | 85 | 142 | 286 | 430 | 573 | 859 | 1146 | 1432 | 1720
Pad_C calibration | 10 | 15 | 25 | 50 | 75 | 100 | 150 | 200 | 250 | 300
Electronic chain calibration

## Slide 48
Electronic chain calibration
Chart: Pad_C calibration: CG 5, FG 0, SH 2, PZ 66, Offset 120
| 53 | 109 | 220 | 332 | 442 | 553 | 773 | 1104 | 1323 | 1663 | 1879
Pad_C calibration | 5 | 10 | 20 | 30 | 40 | 50 | 70 | 100 | 120 | 150 | 170
Chart: 
| 96 | 120 | 235 | 487 | 729 | 967 | 1202 | 1440 | 1679 | 1917
Channel Pad_C Calib : CG 6, FG 0, SH 2 (3µs) , PZ 66, Offset 120 | 4 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Chart: 
| 162 | 186 | 233 | 469 | 702 | 933 | 1165 | 1402 | 1630 | 1858
Channel Pad_C Calib : CG 7, FG 0, SH 2 (3µs) , PZ 66, Offset 120 | 3.5 | 4 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40